## Slide 1: Pipeline Hazard
CT101 – Computing Systems

## Slide 2: Content
Introduction to pipeline hazard
Structural Hazard
Data Hazard
Control Hazard

## Slide 3: Pipeline Hazards (1)
Pipeline Hazards are situations that prevent the next instruction in the instruction stream from executing in its designated clock cycle
Hazards reduce the performance from the ideal speedup gained by pipelining
Three types of hazards
  Structural hazards
    Arise from resource conflicts when the hardware can’t support all possible combinations of overlapping instructions
  Data hazards
    Arise when an instruction depends on the results of a previous instruction in a way that is exposed by overlapping of instruction in pipeline
  Control hazards
    Arise from the pipelining of branches and other instructions that change the PC (Program Counter)

## Slide 4: Pipeline Hazards (2)
Hazards in pipeline can make the pipeline to stall
Eliminating a hazard often requires that some instructions in the pipeline to be allowed to proceed while others are delayed
  When an instruction is stalled, instructions issued latter than the stalled instruction are stopped, while the ones issued earlier must continue
No new instructions are fetched during the stall

## Slide 5: Structural Hazards (1)
If certain combination of instructions can’t be accommodated because of resource conflicts, the machine is said to have a structural hazard
It can be generated by:
  Some functional unit is not fully pipelined
  Some resources has not been duplicated enough to allow all the combinations in the pipeline to execute
  For example: a machine may have only one register file write port, but under certain conditions, the pipeline might want to perform two writes in one clock cycle – this will generate structural hazard
    When a sequence of instructions encounter this hazard, the pipeline will stall one of the instructions until the required unit is available
    Such stalls will increase the Clock cycle Per Instruction from its ideal 1 for pipelined machines

## Slide 6: Structural Hazards (2)
Consider a Von Neumann architecture (same memory for instructions and data)
Notes: <number>
As a result, when an instruction will perform a data reference, will conflict with an instruction fetch.
In this example, the load instruction wants to access the memory to load data at the same time when instruction 3 wants to fetch an instruction from memory.

## Slide 7: Structural Hazards (3)
Stall cycle added (commonly called pipeline bubble)
Notes: <number>
To solve the problem, a stall cycle is added. The effect of the pipeline bubble is actually to occupy the resources for that instruction slot as it travels through the pipeline. Performance wise, instruction 3 will not complete during clock cycle 8, but during clock cycle 9.

## Slide 8: Structural Hazards (4)
Another way to represent the stall – no instruction is initiated in clock cycle 4
Instruction Number | Clock number |  |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
load | IF | ID | EX | MEM | WB |  |  |  |  | 
Instruction i+1 |  | IF | ID | EX | MEM | WB |  |  |  | 
Instruction i+2 |  |  | IF | ID | EX | MEM | WB |  |  | 
Instruction i+3 |  |  |  | stall | IF | ID | EX | MEM | WB | 
Instruction i+4 |  |  |  |  |  | IF | ID | EX | MEM | WB
Instruction i+5 |  |  |  |  |  |  | IF | ID | EX | MEM
Notes: <number>
Sometime those diagrams are drawn with a stall occupying a whole raw, with instruction 3 being moved to the next raw. In either case, the effect is the same. The instruction 3 is not beginning execution until cycle 5.

## Slide 9: Structural Hazards (5)
A machine with structural hazard will have lower CPI
Why a designer allows structural hazard?
  To reduce cost
    Pipelining all the functional units or duplicating them may be too costly
  To reduce latency
    Introducing too many pipeline stages may cause latency issues

## Slide 10: Data Hazards (1)
Data hazards occur when the pipeline changes the order of read/write accesses to operands so that the order differs from the order seen by sequentially executing instructions on an un-pipelined machine
Consider the execution of following instructions, on our pipelined example processor:
  ADD R1, R2, R3
  SUB R4, R1, R5
  AND R6, R1, R7
  OR R8, R1, R9
  XOR R10, R1, R11
Notes: <number>
All the instructions after ADD use the result from ADD.

## Slide 11: Data Hazards (2)
The use of results from ADD instruction causes hazard since the register is not written until after those instructions read it.
Notes: <number>
The ADD instruction writes the result in register R1 only at the WB stage, but SUB instruction reads the value during its ID stage. This is what is called a data hazard. Unless precautions are taken, the SUB instruction will read the wrong value and will use it…
The AND instruction is also affected by this hazard. As we can see from the figure, the write of R1 doesn’t complete until the end of clock cycle 5. Thus, the AND instruction that reads the registers in clock cycle 4 will receive the wrong results.
XOR instruction operates correctly, it reads its inputs (in clock cycle 6) after the ADD has written its result (in clock cycle 5). OR instruction can also be made to work without incurring an hazard, using a simple implementation technique. The technique is to perform the register file reads in the second half of the clock cycle and the writes in the first half.

## Slide 12: Data Hazards (3)
Eliminate the stalls for the hazard involving SUB and AND instructions using a technique called forwarding
Notes: <number>
The data hazard, in certain circumstances can be solved using an implementation technique called forwarding. The idea behind the forwarding is that the result produced by ADD is not really needed by the SUB instruction until it is actually produced. If the result can be moved from where the ADD instruction produces it , the EX/MEM register, to where the SUB needs it, the ALU input latches, then the need for a stall can be avoided.
Forwarding works as follow:
The ALU result from EX/MEM register is always fed back to the ALU input latches
If the forwarding hardware detects that the previous ALU operation has written the register corresponding to a source for the current ALU operation, control logic selects the forwarded result as the ALU input, rather than the value read from the register file.
We need to forward results not only from immediately previous instruction, but possible from instructions that started two or three cycles earlier.

## Slide 13: Data Hazards (4)
Store requires an operand during MEM and forwarding is shown here.
  The result of the load is forwarded from the output in MEM/WB to the memory input to be stored
  In addition the ALUOutput is forwarded to ALU input for address calculation for both Load and Store

## Slide 14: Data Hazards Classification
Depending on the order of read and write access in the instructions, data hazards could be classified as three types.
Consider two instructions i and j, with i occurring before j. Possible data hazards:
  RAW (Read After Write)
    j tries to read a source before i writes to it , so j incorrectly gets the old value;
    most common type of hazard, that is what we tried to explain so far.
  WAW (Write After Write)
    j tries to write an operand before is written by i. The write ends up being performed in wrong order, having i overwrite the operand written by j, the destination containing the operand written by i rather than the one written by j
    Present in pipelines that write in more than one pipe stage
  WAR (Write After Read)
    j tries to write a destination before it is read by i, so the instruction i incorrectly gets the new value
    This doesn’t happen in our example, since all reads are early and writes late

## Slide 15: Data Hazards Requiring Stalls (1)
Unfortunately not all data hazards can be handled by forwarding. Consider the following sequence:
  LW R1, 0(R2)
  SUB R4, R1, R5
  AND R6, R1, R7
  OR R8, R1, R9
The problem with this sequence is that the Load operation will not have data until the end of MEM stage.

## Slide 16: Data Hazards Requiring Stalls (2)
The load instruction can forward the results to AND and OR instruction, but not to the SUB instruction since that would mean forwarding results in “negative” time

## Slide 17: Data Hazards Requiring Stalls (3)
The load interlock causes a stall to be inserted at clock cycle 4, delaying the SUB instruction and those that follow by one cycle.
  This delay allows the value to be successfully forwarded onto the next clock cycle

## Slide 18: Data Hazards Requiring Stalls (4)
Before stall insertion
LW R1, 0(R2) | IF | ID | EX | MEM | WB |  |  |  |  | 
SUB R4, R1, R5 |  | IF | ID | EX | MEM | WB |  |  |  | 
AND R6, R1, R7 |  |  | IF | ID | EX | MEM | WB |  |  | 
OR R8, R1, R9 |  |  |  | IF | ID | EX | MEM | WB |  | 
LW R1, 0(R2) | IF | ID | EX | MEM | WB |  |  |  |  | 
SUB R4, R1, R5 |  | IF | ID | stall | EX | MEM | WB |  |  | 
AND R6, R1, R7 |  |  | IF | stall | ID | EX | MEM | WB |  | 
OR R8, R1, R9 |  |  |  | stall | IF | ID | EX | MEM | WB | 
After stall insertion

## Slide 19: Compiler Scheduling for Data Hazards (1)
Consider a typical code, such as A = B+C
LW R1, B | IF | ID | EX | MEM | WB |  |  |  |  | 
LW R2, C |  | IF | ID | EX | MEM | WB |  |  |  | 
ADD R3, R1, R2 |  |  | IF | ID | stall | EX | MEM | WB |  | 
SW A, R3 |  |  |  | IF | stall | ID | EX | MEM | WB | 
The ADD instruction must be stalled to allow the load of C to complete
The SW needs not be delayed because the forwarding hardware passes the result from MEM/WB directly to the data memory input for storing

## Slide 20: Compiler Scheduling for Data Hazards (2)
Rather than just allow the pipeline to stall, the compiler could try to schedule the pipeline to avoid the stalls, by rearranging the code
  The compiler could try to avoid the generating the code with a load followed by an immediate use of the load destination register
  This technique is called pipeline scheduling or instruction scheduling and it is a very used technique in modern compilers

## Slide 21: Instruction scheduling example
Generate code for our example processor that avoids pipeline stalls from the following sequence:
  A = B +C
  D = E - F
Solution
  LW Rb, B
  LW Rc, C
  LW Re, E ; swap instructions to avoid stall
  ADD Ra, Rb, Rc
  LW Rf, f
  SW a, Ra ; swap instruction to avoid stall
  SUB Rd, Re, Rf
  SW d, Rd

## Slide 22: Control Hazards (1)
Can cause a greater performance loss than the data hazards
When a branch is executed it may or it may not change the PC (to other value than its value + 4)
  If a branch is changing the PC to its target address, than it is a taken branch
  If a branch doesn’t change the PC to its target address, than it is a not taken branch
If instruction i is a taken branch, than the value of PC will not change until the end MEM stage of the instruction execution in the pipeline
  A simple method to deal with branches is to stall the pipe as soon as we detect a branch until we know the result of the branch

## Slide 23: Control Hazards (2)
A branch causes three cycle stall in our example processor pipeline
  One cycle is a repeated IF – necessary if the branch would be taken. If the branch is not taken, this IF is redundant
  Two idle cycles
Branch Instruction | IF | ID | EX | MEM | WB |  |  |  |  | 
Branch Successor |  | IF | stall | stall | IF | ID | EX | MEM | WB | 
Branch Successor +1 |  |  |  |  |  | IF | ID | EX | MEM | WB
Branch Successor +2 |  |  |  |  |  |  | IF | ID | EX | MEM

## Slide 24: Control Hazards (3)
The three clock cycles lost for every branch is a significant loss
  With a 30% branch frequency, the machine with branch stalls achieves only about half of the speedup from pipelining
  Reducing the branch penalty becomes critical
The number of clock cycles in a branch stall can be reduced by two steps:
  Find out if the branch is taken or not in early stage in the pipeline
  Compute the taken PC (address of the branch target) earlier
Notes: <number>
To optimize the branch behavior, both of the steps should be taken.

## Slide 25: Control Hazards (4)
Reducing the stall from branch hazards by moving the zero test and branch calculation into ID phase of pipeline. It uses a separate adder to compute the branch target address during ID. Because the branch target addition happens during ID, it will happen for all instructions. The branch condition (Regs[IF/ID.IR6…10] op 0) will also be done for all instructions. The selection of the sequential PC or the branch target PC will still occur during IF, but now it uses values from ID phase, rather than from EX/MEM register. In this case, the branch instruction is done by the end of ID phase, so EX, MEM and WB stages are not used for branch instructions anymore.
Notes: <number>
It uses a separate adder to compute the branch target address during ID. Because the branch target addition happens during ID, it will happen for all instructions. The branch condition (Regs[IF/ID.IR6…10] op 0) will also be done for all instructions. The selection of the sequential PC or the branch target PC will still occur during IF, but now it uses values from ID phase, rather than from EX/MEM register. In this case, the branch instruction is done by the end of ID phase, so EX, MEM and WB stages are not used for branch instructions anymore.

## Slide 26: Modified Pipelined Instruction Fetch
Instruction Fetch
  IF/ID.IR  mem[PC]
  IF/ID.NPC, PC  if (Regs[IF/ID. IR6…10] op 0) {IF/ID.NPC +(IF/ID.IR16)16##IF/ID.IR16…31}else{PC+4}
Operation:
  send out the PC and fetch the instruction from memory
  Increment the PC by 4 to address the next instruction or save the address generated by a taken branch of a previous instruction in decode stage

## Slide 27: Modified Pipelined Instruction Decode
Instruction Decode Cycle/Register Fetch
  ID/EX.A  Regs[IR6…10]; ID/EX.B  Regs[IR11…15]
  ID/EX.IR  IF/EX.IR
  ID/EX.Imm (IF/ID.IR16)16##IF/ID.IR16…31
  Compute the condition: Regs[IF/ID.IR6..10] op 0
  Compute the branch address: IF/ID.NPC + (IF/ID.IR16)16##IF/ID.IR16…31
Operation
  Decode the instruction and access the register files to access the registers; the output of the general purpose registers are read into two temporary register (A and B, part of the pipeline registers ID/EX stage) for use in latter clock cycles
  The lower 16 bits of IR, stored in pipeline registers from IF/ID stage are also sign extended and stored into temporary register Imm (part of ID/EX pipeline registers), for latter use
  Value IR is passed to the next stage of pipeline registers (from IF/ID to ID/EX)
  Compute the values for the cond and branch target and use them to set the PC if necessary (if taken branch)

## Slide 28: References
“Computer Architecture – A Quantitative Approach”, John L Hennessy & David A Patterson, ISBN 1-55860-329-8
“Computer Architecture”, Nicholas Charter, ISBN – 0-07-136207