## Slide 1: Instruction Set Architecture
CT101-Computing Systems

## Slide 2: Content
Instruction set architecture
Programming languages
Instruction types
Data types
Instruction formats
Addressing modes
Instruction set design

## Slide 3: Instruction set architecture
Includes the microprocessor’s instruction set, the set of all of the assembly language instructions that the microprocessor can execute
Specifies:
  The registers accessible to the programmer, their size and the instructions in the instructions set that can use each register
  Information necessary to interact with the memory (e.g. alignment)
  How microprocessors react to interrupts (e.g. interrupt routines)
Before getting into details about it, we need to describe programming languages
Notes:   Information necessary to interact with the memory - Certain microprocessors require instructions to start only at specific memory locations; this alignment of the instructions will be part of the instruction architecture
  How microprocessors react to interrupts - Some microprocessors have interrupts, that cause the processor to stop what is doing and perform some other preprogrammed functions (interrupt routines)
<number>

## Slide 4: Programing Languages
High level languages
  Hide all of the details about the computer and the operating system
  Platform independent
Assembly language
  Platform dependent
  Processors are made usually backwards compatible
Machine languages
  Contain the binary values that cause the processor to perform certain operations
  Platform specific
Notes:     Platform Independent - Same code can be compiled for different platforms
    Platform Dependent - Code written for a processor will not run on a different family of processors, with an incompatible instruction set
    Backwards compatible processors - See x86 family (code written for 286 will still run on Pentium machines)
    Platform Specific - When a microprocessor reads and executes an instruction, it is a machine language instruction
<number>

## Slide 5: Compiling Native Code
Notes: <number>
Compiler:
Checks to make sure every line in the code is valid
Once the program is syntax error free, it will finish compile the source code and generates object code
Object code is the machine language equivalent to the source code
At this point, the program has been complied successfully, but is not ready to execute.
Linking:
Some programs need object code from other programs or libraries (other object files)
A linker combines your object code with any other required object code
The combined code is stored as executable file, the code that the computer runs.
A loader copies the executable file into the memory, and then the microprocessor runs the code contained in that file.
One high level language statement is converted into one or more machine code instructions. There may be more than just one valid conversion for a statement, which complicates the compiler. This is not the case with the assembler. With assembler, one assembly instruction corresponds to exactly one machine code instruction. For this reason, assemblers are much less complicated than an compiler

## Slide 6: Assembling programs
Assembly language is specific to one microcontroller
Converts the source code into object code
The linker will combine the object code of your program with any other required object code to produce executable code
Loader will load the executable code into memory, for execution
Notes: <number>
In some cases, where there is no need for an operating system (i.e. in some of the consumer appliances), the code generated by the assembly operation is the final executable code.
Assembly language is sometime used to optimize pieces of code written in high level languages. Certain functions from a C++/C program may be written in assembly to optimize the execution time. Of course, the program is no longer portable between platforms.

## Slide 7: Java – different way of programming
Notes: <number>
Java programming language, is a high level programming language. Unlike the other high level programming languages, the code is not compiled into machine specific code that can be executed by a microprocessor. Instead, the java programs are compiled into something called bytecode. The bytecode is input to a JAVA Virtual Machine (JVM) , which interprets and executes the code. The JVM can be a hardware chip, but it is usually a program itself, often part of a web browser (to interpret applets).
The bytecode is platform independent. So, the JVM is specific for each platform, but the bytecode for the program remains the same across different platforms. This is a very nice feature of JAVA. Of course there is always a trade off….that refers to the execution speed.

## Slide 8: Instruction Set Architecture
Defines any aspects of the processor that an assembly language programmer needs to know, in order to write a correct program
Specifies:
  The registers accessible to the programmer, their size and the instructions in the instructions set that can use each register
  Information necessary to interact with the memory
    Certain microprocessors require instructions to start only at specific memory locations; this alignment of the instructions will be part of the instruction architecture
  How microprocessor reacts to interrupts
    Some microprocessors have interrupts, that cause the processor to stop what is doing and perform some other preprogrammed functions (interrupt routines)
Notes: <number>
Instruction set architecture – defines any aspects of the processor that an assembly language programmer needs to know, in order to write a correct program

## Slide 9: RISC vs. CISC (1)
The believe that better performance would be obtained by reducing the number of instruction required to implement a program, lead to design of processors with very complex instructions (CISC)
  CISC – Complex Instruction Set Computers
As compiler technologies improved, researchers started to wonder if CISC architectures really delivered better performances than architectures with simpler instruction set
  RISC – Reduced Instruction Set Computers

## Slide 10: RISC vs. CISC (2)
CISC
  Fewer instructions to execute a given task than RISC
  Programs for CISC take less storage space than programs for RISC
  Arithmetic or other instructions may read their operand from memory and could write the result in memory
RISC
  Simpler instructions, faster execution speeds per instruction, more instructions executed in same amount of time than CISC
  Cheaper to implement (simple instruction set results in simple implementation internal micro-architecture)
  Load/Store architecture – only load and store are used to access the external memory
Notes: <number>
It is difficult to say which architecture is better. Over the last 20 years, RISC architectures have taken useful instructions from CISC architectures and included them in their instruction sets. CISC architectures have dropped instructions that were not useful (too complex).

## Slide 11: RISC vs. CISC (3)
Addition of two operands from memory, with result written in memory, in RISC and CISC architectures
Having an operation broken into small instructions (RISC) allows the compiler to optimize the code
  i.e. between the two LD instructions (memory is slow) the compiler can add some instructions that don’t need memory access
The CISC instruction has no option but to wait for its operands to come from the memory, potentially delaying other instructions
RISC | CISC
LD R4, (R1) LD R5, (R2) ADD R6, R4, R5 ST (R3), R6 | ADD (R3), (R2), (R1)
Notes: <number>
Te difference between load/store architectures and architectures that can merge memory references with other operations is an excellent example of trade-offs between RISC and CISC architectures. A RISC architecture requires a few load/store instructions to bring the operands from the memory and save the result in the memory. However, the hardware required to implement the CISC processor would be more complex than the hardware required to implement the RISC processor. The CISC processor requires a longer cycle time or requires a few cycles to implement one instruction.

## Slide 12: Instruction types
Data Transfer Instructions
  Operations that move data from one place to another
  These instructions don’t actually modify the data, they just copy it to the destination
Data Operation Instructions
  Unlike the data transfer instructions, the data operation instructions do modify their data values
  They typically perform some operation using one or two data values (operands) and store the result
Program Control Instructions
  Jump or branch instructions used to go in another part of the program; the jumps can be absolute (always taken) or conditional (taken only if some condition is met)
  Specific instructions that can generate interrupts (software interrupts)

## Slide 13: Data transfer instructions (1)
Load data from memory into the microprocessor
  These instructions copy data from memory into microprocessor registers (i.e. LD)
Store data from the microprocessor into the memory
  Similar to load data, except that the data is copied in the opposite direction (i.e. ST)
  Data is saved from internal microprocessor registers into the memory
Move data within the microprocessor
  These instructions move data from one microprocessor register to another (i.e. MOV)

## Slide 14: Data transfer instructions (2)
Input data to the microprocessor
  A microprocessor may need to input data from the outside world, these are the instructions that do input data from the input device into the microprocessor
  In example: microprocessor needs to know which key was pressed (i.e. IORD)
Output data from the microprocessor
  The microprocessor copies data from one of its internal registers to an output device
  In example: microprocessor may want to show on a display the content of an internal register (the key that have been pressed) (i.e. IOWR)

## Slide 15: Data Operation Instructions
Arithmetic instructions
  add, subtract, multiply or divide: ADD, SUB, MUL, DIV, etc..
  Instructions that increment or decrement one from a value: INC, DEC
  Floating point instructions that operate on floating point values (as suppose to integer values): FADD, FSUB, FMUL, FDIV
Logic Instructions: AND, OR, XOR, NOT, etc …
Shift Instructions: SR, SL, RR, RL, etc…

## Slide 16: Program control instructions (1)
Conditional or unconditional jump and branch instructions
  JZ, JNZ, JMP, etc…
Comparison instructions
  TEST
Instructions to call and return a/from a routine; they can be as well, conditional
  CALL, RET, IRET, IRETW, etc..

## Slide 17: Program control instructions (2)
Specific instructions to generate software interrupts; three are also interrupts that are not part of the instruction set, called hardware interrupts, generated by devices outside of a microprocessor
  INT
Exceptions and traps – are triggered when valid instructions perform invalid operations, such as dividing by zero
Halt instructions - causes the processor to stop executions, such as at the end of a program
  HALT

## Slide 18: Data types
A microprocessor has to operate with multiple data types; this has a direct implication in the instruction architecture set, because the designer has to include different instructions to perform the same operation on different data types
Numeric data representation:
  Integer representation
    Unsigned representation: n bit value range from 2n -1 to 0
    Signed representation: n bit value range from -2n-1 to 2n -1-1
  Floating point representation
    A processor may have special registers and instructions for floating point data
Boolean data:
  Non zero value is used to represent TRUE and zero value is ussed to represent FALSE
Character data
  Stored as binary value, encoded using ASCII, UNICODE, etc…
  A microprocessor may concatenate strings of characters, replace certain characters in a string, etc..
  Some instruction sets do include instructions to directly manipulate character data

## Slide 19: Instruction formats
An instruction is represented as a binary value with specific format, called the instruction code
It is made out of different groups of bits, with different significations:
  Opcode – represents the operation to be performed (it is the instruction identifier)
  Operands – one, two or three represent the operands of the operation to be performed
A microprocessor can have one format for all the instructions or can have several different formats
An instruction is represented by a single instruction code

## Slide 20: Instruction formats
Notes: <number>
Consider a simplified example A=B+C
This instruction is an addition, with two source operands (B and C) and a destination operand (A)
If we are using 4 bits to represent the opcode of the instruction, then we will have 16 possible operations, including the addition. Assume that the bit pattern 1010 represents the addition operation.
For this example, there are four possible operands (2 bits representation). For this example A is 00, B is 01, C is 10 and D is 11.
A microprocessor can be designed with instructions that can take 3, 2, 1 or no operand. The possible format instructions for those cases are presented.

## Slide 21: Instruction formats
Fewer operands translates into more instructions to accomplish the same task
The hardware required to implement the microprocessor becomes less complex with fewer operands; microprocessors whose instructions specify a fewer number of operands can execute instructions more quickly than those that specify more operands
The example was simplified to show the difference between three, two, one and zero operands instructions; in practice, the instructions require many more bits than the used in these examples; an operand field may specify an arbitrary memory address, rather than one of the four registers; this could require 16, 32 or even more bits per operand

## Slide 22: CPU Elements
Program Counter or PC contains the address of the instruction that will be executed next
Stack – a data structure of last in first out type
  Dedicated hardware stack – it has a hardware limitation, (i.e. 8 locations)
  Memory implemented stack –limited by the physical memory of the system
    A stack is described by a special register – stack pointer – that holds the address of the last
  It can be used explicitly to save/restore data
  It is used implicitly by procedure call instructions (if available in the instruction set)
IR – instruction register that holds the current instruction being processed by the microprocessor; it is not exposed through the instruction set architecture; just an organization element

## Slide 23: Implicit stack usage
CALL – before the jump the PR address, the call instruction will save the PC (program counter) in the stack
Return – will extract the address of the next instruction before jump and restore the PC (program counter) value
Memory
1000
1001
CALL PR
…
2000
CALL PR
.
.
.
RETURN PR ENDP
1001
Stack
SP
Notes: <number>
Stack operations (for a stack that grows from higher addresses to lower addresses in the memory):
PUSH (X):
  (SP)= (SP)-1
  ((SP)) = X
POP (X)
  X = ((SP))
  (SP) = (SP)+1

## Slide 24: Explicit stack usage
Typical Stack operations (assuming that the stack grows from higher addresses towards lower addresses):
  PUSH (X):
    (SP)= (SP)-1
    ((SP)) = X
  POP (X)
    X = ((SP))
    (SP) = (SP)+1

## Slide 25: Addressing Modes
When a microprocessor accesses memory, to either read or write data, it must specify the memory address it needs to access
Several addressing modes to generate this address are known, a microprocessor instruction set architecture may contain some or all of those modes, deepening on its design
In the following examples we will use the LDAC instruction (loads data from a memory location into the AC (accumulator) microprocessor register)

## Slide 26: Direct mode
Instruction includes the A memory address
LDAC 5 – accesses memory location 5, reads the data (10) and stores the data in the microprocessor’s accumulator
This mode is usually used to load variables and operands into the CPU
Address A
Opcode
Instruction
Memory
Operand

## Slide 27: Indirect mode
Starts like the direct mode, but it makes an extra memory access. The address specified in the instruction is not the address of the operand, it is the address of a memory location that contains the address of the operand.
LDAC @5 or LDAC (5), first retrieves the content of memory location 5, say 10, and then CPU goes to location 10, reads the content (20) of that location and loads the data into the CPU (used for relocatable code and data by operating systems)
Address A
Opcode
Instruction
Memory
Pointer to operand
operand

## Slide 28: Register direct mode
It specifies a register instead a memory address
LDAC R – if register R contains an value 5, then the value 5 is copied into the CPU’s accumulator
No memory access
Very fast execution
Very limited address space
Register Address R
Opcode
Instruction
Registers
Operand

## Slide 29: Register indirect mode
LDAC @R or LDAC (R) – the register contains the address of the operand in the memory
Register R (selected by the operand), contains value 5 which represents the address of the operand in the memory (10)
One fewer memory access than indirect addressing
Register Address R
Opcode
Instruction
Memory
Operand
Registers
Pointer to
operand

## Slide 30: Immediate mode
The operand is not specifying an address, it is the actual data to be used
LDAC #5 loads actually value 5 into the CPU’s accumulator
No memory reference to fetch data
Fast, no memory access to bring the operand

## Slide 31: Implicit addressing mode
Doesn’t explicitly specify an operand
The instruction implicitly specifies the operand because always applies to a specific register
This is not used for load instructions
As an example, consider an instruction CLAC, that is clearing the content of the accumulator in a processor and it is always referring to the accumulator
This mode is used also in CPUs that do use a stack to store data; they don’t specify an operand because it is implicit that the operand must come from the stack

## Slide 32: Displacement addressing mode
Effective Address = A + (content of R)
Address field hold two values
  A = base value
  R = register that holds displacement
  or vice versa
Register R
Opcode
Instruction
Memory
Operand
Pointer to
Operand
Registers
Address A
+

## Slide 33: Relative addressing mode
It is a particular case of the displacement addressing, where the register is the program counter; the supplied operand is an offset; Effective Address = A + (PC)
The offset is added to the content of the CPU’s program counter register to generate the required address
The program counter contains the address of next instruction to be executed, so the same relative instruction will produce different addresses at different locations in the program
Consider that the relative instruction LDAC $5 is located at memory address 10 and it takes two memory locations; the next instruction is at location 12, so the operand is actually located at (12 +5) 17; the instruction loads the operand at address 17 and stores it in the CPU’s accumulator
This mode is useful for short jumps and relocatable code

## Slide 34: Indexed addressing mode
Works like relative addressing mode; instead adding the A to the content of program counter (PC), the A is added to the content of an index register
If the index register contains value 10, then the instruction LDAC 5(X) reads data from memory at location (5+10) 15 and stores it in the accumulator
Good for accessing arrays
  Effective Address = A + R
  R++

## Slide 35: Based addressing mode
Works the same with indexed addressing mode, except that the index register is replaced by a base address register
A holds displacement
R holds pointer to base address
R may be explicit or implicit
e.g. segment registers in 80x86

## Slide 36: Addressing modes

## Slide 37: Instruction set architecture design
What is the processor able to do
  If will be general purpose, then the ISA should be pretty rich to perform a variety of tasks
  Specialized processor, then the ISA should perform a specific set of tasks, well known in advance
The instruction set has to have all the instructions to perform its required tasks – completeness
The instruction set has to be orthogonal – to minimize the overlap between instructions
The register set:
  Too few registers will cause too many accesses to the memory, thus reducing performance
  Too many registers would be overkill for specialized microcontrollers

## Slide 38: Instruction set architecture design
Does the microprocessor have to be backwards compatible with other microprocessors?
What type of data and sizes of data will the microprocessor deal with??
  If floating point operation is needed, then the design must include instructions that will work on floating point data; also registers to store floating point data are needed;
Are interrupts needed?
  If needed, the design should include the registers and instructions to deal with interrupts
Are conditional instructions needed?
  Usually, the conditions are stored in 1-bit registers that store the value of various conditions; typical flags include the zero flag (set 1 when an operation produces a result of zero), sign flag (set to one when an instruction produces an negative result), etc…

## Slide 39: References
“Computer Systems Organization & Architecture”, John D. Carpinelli, ISBN: 0-201-61253-4