## Slide 1: CPU Review and Programming Models
CT101 – Computing Systems

## Slide 2: Contents
Review of computer organization
Processor instruction cycle and organization
Stack and GPR processor architectures
Stack used to implement procedure calls

## Slide 3: Basic Computer Organization
Notes: <number>
Most computer systems can be divided into three subsystems: the processor (known also as CPU), the memory and the Input/Output subsystem. The processor is responsible for executing programs, the memory is responsible for storage space for programs and data they reference and the I/O subsystem allows the processor to control devices that interact with outside world (such as CDROM, Monitor, Keyboard, etc..)

## Slide 4: Computer organization
Notes: <number>
In most computer systems, the processor has a single data buss that connects to a switch module, such as the PCI bridge found in many PC systems. Some processors do integrate the switch module onto the same chipset as the processor itself, to reduce the number of systems required to build a computer system, and thus the system cost.
The switch communicates with the memory through a memory bus, a dedicated set of wires that transfer data between these two systems. A separate I/O bus connects the switch to the I/O devices. Separate memory and I/O buses are used because the I/O system is generally designed for maximum flexibility while the memory system is design for maximum speed. The goal of the I/O bus is to allow for a large number of different devices to be connected to the processor, while the memory system is designed for maximum throughput.

## Slide 5: Von Neumann and Harvard architectures
Von Neumann
  Allows instructions and data to be mixed and stored in the same memory module
  More flexible and easier to implement
  Suitable for most of the general purpose processors
Harvard:
  Uses separate memory modules for instructions and for data
  It is easier to pipeline
  Higher memory throughput
  Suitable for DSP (Digital Signal Processors)
Notes: Pentium is using an von Neumann architecture for the external memory and is using a Harvard architecture for its internal cache memory (allowing 8KB of cache for data and anther (separate) 8kB of cache for instructions
<number>

## Slide 6: Programs
Instruction sequences that tell computer what to do
To the computer, a program is made out of a sequence of numbers that represent individual operations.
  those operations are known as machine instructions or just instructions
  A set of instructions that a processor can execute is known as instruction set

## Slide 7: The Processor - Instruction Cycles
The instruction cycle is the procedure of processing an instruction by the microprocessor:
  Fetches or reads the instruction from the memory
  Decodes the instruction, determining which instruction is to be executed (which instruction has been fetched)
  Executes the instruction – performs the operations necessary to complete what the instruction is suppose to do (different from instruction to instruction, may read data from memory, may write data to memory or I/O device, perform only operations within CPU or combination of those)
Each of the phases fetch -> decode -> execute consist of a sequence of one or more operations inside the CPU (and interaction with the subsystems)

## Slide 8: Processor Organization
Notes: <number>
Any processor is made up of execution unit(s), control unit and register file.
Registers:
  PC (program counter) keeps the address of the next instruction
  IR (instruction register) keeps the instruction being executed

## Slide 9: Execution Unit Example
//Code for a = b + c
LD R3, b //copy value b from memory to R3
LD R4, c //copy value c from memory to R4
add R3, R4 //sum placed in R3
ST R3, a //store the result into memory
Notes: <number>
Execution unit – performs various arithmetic and logic operations (such as add, multiply, etc..) on binary representation of numbers (integers or floating point numbers). Computations are performed by loading the values into general purpose registers, perform the arithmetic on the registers and then saving the results back into the memory
Status registers are used by various parts of the CPU to store status of the operations. One of the roles of the status registers is to hold data where CPU keeps information about the computations being executed (such as the result of the last function unit operation was zero).

## Slide 10: Control Unit
The control unit controls the execution of the instructions stored in the main memory (retrieve and execute them)
Notes: <number>
The control unit has three components:
A component that brings the instruction from the main memory into the internal registers of the CPU, called Fetch Unit
A component that identifies what instruction is – the Decode Unit
Another component that signals the other parts of the computer to execute the instruction
The Program Counter register contains the memory address of the instruction is currently processing. The program counter register is incremented in the fetch stage (so it is very often referred as holding the next instruction address)
The Instruction Register holds the current instruction, once it has been fetched from the main memory.
When the machine is initially started, the PC is loaded with the address of the first instruction to be executed (usually a hardwired address). There many variations on how the computing system can start. One usual way is where the memory (usually ROM) will contain initialization code and a program called bootstrap loader that will load the operating system from a peripheral storage or from the network.

## Slide 11: Programming Models
A processor programming model defines how instructions access their operands and how instructions are described in processor’s assembly language
Processors with different programming models can offer similar set of operations but may require very different approaches to programming
We will study two different processor architectures and will learn what differences in programming pose stack vs GPR models

## Slide 12: Stack Based Architectures
The Stack
Implementing Stacks
Instructions in a stack based architecture
Stack based architecture instruction set
Programs in stack based architecture

## Slide 13: The Stack (1)
Is a last in first out (LIFO) data structure
  Consists of locations, each of which can hold a word of data
  It can be used explicitly to save/restore data
Supports two operations
  PUSH – takes one argument and places the value of the argument in the top of the stack
  POP – removes one element from the stack, saving it into a predefined register of the processor
It is used implicitly by procedure call instructions (if available in the instruction set)
Notes: <number>
The stack name comes from the fact that the data structure acts like a stack of plates (or other items). When a new plate is put on a stack of plates, it goes on the top, and it is the first plate to be removed when someone take a plate off the stack. The stack consists of locations, each of which can hold a word of data.

## Slide 14: The Stack (2)
When a new data is added to the stack, it is placed at the top of the stack, and all the contents of the stack is pushed down one location
Consider the code:
  PUSH #10
  PUSH #11
  POP
  PUSH #8

## Slide 15: Implementing Stacks
  Dedicated hardware stack
    it has a hardware limitation, (i.e. 8 locations for an SX controller)
    Very fast
  Memory implemented stack
    Limited by the physical memory of the system
    Slow compared with hardware stack, since extra memory addressing has to take place for each stack operation
  Stack overflows can occur in both implementations
    When the amount of data in the stack exceeds the amount of space allocated to the stack (or the hardware limit of the stack)

## Slide 16: Stack Implemented in Memory
Every push operation will increment the top of the stack pointer (with the word size of the machine); Every pop operation will decrement the top of the stack pointer
Notes: <number>
A stack overflow will occur if the top of the stack pointer will reach the stack limit. In our example, the size of the stack is 64 KB.
When the top of the stack pointer and the bottom of the stack are the same, the stack is empty, and an attempt to pop any data will result in an error.
Several variations of this approach are possible, where the bottom of the stack points to the highest address of allocated buffer, and the stack grows towards the lower addresses.

## Slide 17: Optimized Stack Implementation
Implementation using register file and memory (registers are used as “cache” for the stack)
Notes: <number>
With pure memory implementation for the stack, the ADD instruction (for example), would take about 4 memory addressing to complete (one for fetching the instruction, two to bring in the operands and another one to save the result). A better implementation is presented in this slide, where the last N pushed elements are preserved inside the processor, in the register files.

## Slide 18: Instructions in a Stack Based Architecture
Get their operands from the stack and write their results to the stack
Advantage - Program code takes little memory (no need to specify the address of he operands in memory or registers)
  Push is one exception, because it needs to specify the operand (either as constant or address)

## Slide 19: Simple Stack Based Instruction Set
PUSH #a | Stack <-a
POP | a<-Stack (the value popped is discarded)
ST | a <-Stack (a) <-Stack
LD | a <-Stack Stack <- (a)
ADD | a <- Stack b <- Stack Stack <- a + b
SUB | a <- Stack b <- Stack Stack <- b – a
AND | a <- Stack b <- Stack Stack <- a & b (bit wise computation)
OR | a <- Stack b <- Stack Stack <- a ¦ b (bit wise computation)
Notes: <number>
a<-b : The value of b is placed in a
(a): The memory location whose address is contained in a
#a: The constant value a
PC: Program counter, for describing the branch instructions

## Slide 20: Programs in Stack Based Architecture (1)
Writing programs for stack based architectures is not easy, since stack-based processors are better suited for postfix notation rather than infix notation
  Infix notation is the traditional way of representing math expressions, with operation placed between operands
  Postfix notation – the operation is placed after the operands
Once the expression has been converted into postfix notation, implementing it in programs is easy
Create a stack based program that computes:
  2 + (7&3)
Notes: <number>
Starting at the left of the expression, each constant is pushed into the stack, and each operator is replaced by appropriate instruction

## Slide 21: Programs in Stack Based Architecture (2)
First we need to convert the expression into postfix notation:
  2 + (7&3) = 2 + (7 3 &) = (2 (7 3 &)+)
Convert the postfix notation into a series of instructions, using the instructions from the instruction set presented earlier
    PUSH #2
    PUSH #7
    PUSH #3
    AND
    ADD
To verify the result, we need to hand simulate the execution

## Slide 22: General Purpose Register Architecture
Instructions in a GPR architecture
A GPR instruction set
Programs in GPR architecture

## Slide 23: General Purpose Register Architecture (1)
The instructions read their operands and write their results to random access register file.
The general purpose register file allows the access of any register in any order by specifying the number (register ID) of the register
The main difference between a general purpose register and the stack is that reading repeatedly a register will produce the same result and will not modify the state of the register file.
  Popping an item from a LIFO structure (stack) will modify the contents of the stack

## Slide 24: General Purpose Register Architecture (2)
Many GPR architectures assign special values to some registers in the register file to make programming easier
  i.e. sometime, register 0 is hardwired with value 0 to generate this most common constant

## Slide 25: Instructions in GPR Architecture (1)
GPR instructions need to specify the register that hold their input operands and the register that will hold the result
The most common format is the three operands instruction format.
  ADD r1, r2, r3 instructs the processor to read the contents of r2 and r3, add them together and write the result in r1
Instructions having two or one input are also present in GPR architecture

## Slide 26: Instructions in GPR Architecture (2)
A significant difference between GPR architecture and stack based architecture is that programs can choose which values should be stored in the register file at any given time, allowing them to cache most accessed data
  In stack based architectures, once the data has been used, it is gone.
GP architectures have better performance from this point of view, at the expense of needing more storing space for the program (since the instructions are larger, needing to encode also addresses of the operands)

## Slide 27: Simple GPR Instruction Set
ST (ra), rb | (ra) <- rb
LD ra, (rb) | ra <- (rb)
ADD ra, rb, rc | ra <- rb +rc
SUB ra, rb, rc | ra <- rb -rc
AND ra, rb, rc | ra <- rb & rc
OR ra, rb, rc | ra <- rb ¦ rc
MOV ra, rb | ra <- rb
MOV ra, #constant | ra <- constant
Sample instruction set, similar with the one presented for the
Stack-based architecture.

## Slide 28: Programs in a GPR Architecture (1)
Programming a GPR architecture processor is less structured than programming a stack based architecture one.
There are fewer restrictions on the order in which the operations can be executed
  On stack based architectures, instructions should execute in the order that would leave the operands for the next instructions on the top of the stack
  On GPR, any order that places the operands for the next instruction in the register file before that instruction executes is valid.
    Operations that access different registers can be reordered without making the program invalid
Notes: <number>
Reordering is sometime used to improve performances.

## Slide 29: Programs in GPR Architecture (2)
Create a GPR based program that computes:
  2 + (7&3)
GPR programming uses infix notation:
    MOV R1, #7
    MOV R2, #3
    AND R3, R1, R2
    MOV R4, #2
    ADD R4, R3, R4
The result will be placed in R4

## Slide 30: Comparing Stack based and GPR Architectures
Stack-based architectures
  Instructions take fewer bits to encode
  Reduced amount of memory taken up by programs
  Manages the use of register automatically (no need for programmer intervention)
  Instruction set does not change if size of register file has changed
GPR architectures
  With evolution of technology, the amount of space taken up by a program is less important
  Compilers for GPR architectures achieve better performance with a given nmber of general purpose registers than they are on stack-based architectures with same number of registers
    The compiler can choose which values to keep (cache) in register file at any time
GPR architectures are used by modern computers (workstations, PCs, etc..)

## Slide 31: Using Stacks to Implement Procedure Calls (1)
Programs need a way to pass inputs to the procedures that they call and to receive outputs back from them
Procedures need to be able to allocate space in memory for local variables, without overriding any data used by their calling program
It is impossible to determine which registers may be safely used by the procedure (especially if the procedure is located in a library), so a mechanism to save/restore registers of calling program has to be in place
Procedures need a way to figure out where they were called from, so the execution can return to the calling program when the procedure completes (they need to restore the program counter)

## Slide 32: Using Stacks to Implement Procedure Calls (2)
When a procedure is called, a block of memory in the stack is allocated. This is called a stack frame
  The top of the stack pointer is incremented by the number of locations in the stack frame
Notes: <number>
When a procedure is called, the contents of the calling program’s register file are copied into the stack frame along with its return address and the inputs to the procedure. The procedure is using the rest of the stack frames for its local data. Since the amount of inputs and local data is different from procedure to procedure, each stack frame is different too. The arrangement of data within the stack frame is also variable from programming system to programming system.
When a procedure finishes, it jumps to the return address contained in the stack and execution of the calling program resumes. The calling program reads its saved register file and handles the procedure’s result, which can be passed either in a register or through the stack too.

## Slide 33: Using Stacks to Implement Procedure Calls (3)
Nested procedure calls – main program calls function f(), function f() calls function g(), function g() calls function h()
Notes: <number>
When a program makes nested procedure calls (procedures that call other procedures), each nested procedure allocates its stack frame in the top of those already in the stack. As long as the stack doesn’t overflow, the nesting can be done as deeply as necessary.

## Slide 34: Calling Conventions
Different programming systems may arrange data in procedure’s stack frame differently and may require the steps involved in calling a procedure be performed in different orders.
The pre-requirements that a programming system places on how a procedure is called and how the data is passed between a calling program and its procedures are called calling conventions.
Calling conventions are designed in such a way to minimize the amount of data passed between the calling program and its procedures.

## Slide 35: References
“Computer Systems Organization & Architecture”, John D. Carpinelli, ISBN: 0-201-61253-4