## Slide 1: Digital Logic Fundamentals & CLC Review
CT101 – Computing Systems

## Slide 2: Contents
Overview
Basic Gates and Boolean algebra
Boolean functions manipulation and implementation
Complex combinatorial circuit elements (multiplexers, decoders, encoders, comparators, adders)
CLC design & Implementation

## Slide 3: Overview
Gates, latches, memories and other logic components are used to design computer systems and their subsystems
Two types of digital logic:
  Combinatorial Logic Circuitry: output is a function of inputs
  Sequential logic: output is a complex function of current inputs, previous inputs or state and previous outputs
Neither combinatorial logic or sequential logic is better than the other. In practice, both are used as appropriate in circuit design.
Notes: <number>
Combinatorial logic – the output of this type of logic is dependent solely on its current inputs. When certain input values are set, a combinatorial circuit generates output values corresponding to those input values. When the input of the combinatorial logic are changed, the outputs are changing to reflect the changes in the new input values. Previous values of the inputs do not matter, the current outputs depend solely on the current inputs.
Sequential logic – the outputs of a sequential logic circuit depend on both the current inputs and on previous inputs and outputs of the circuit. Sequential elements have storage elements that record the state of the circuit. In other words, the state information combined with the inputs is generating the outputs. The state and inputs also combine to generate a new state of the circuit. The same inputs in a sequential circuit may generate different outputs and different new states, depending on the circuit’s current state.
In practice both types of logic are used. The sequential logic include combinatorial logic…the reverse is not true.

## Slide 4: Boolean Algebra
Review Boolean algebra, basic functions and methods used to combine, manipulate and transform Boolean functions & application to implementation of combinatorial logic circuitry
A Boolean algebra value can be either true or false.
Digital logic uses 1 to represent true and 0 to represent false.
This presentation introduces the Boolean algebra basic

## Slide 5: AND
Output is one if every input has value of 1
More than two values can be “and-ed” together
For example xyz = 1 only if x=1, y=1 and z=1
x | y | out = xy
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Notes: <number>
Truth table is the way to describe any combinatorial circuitry.

## Slide 6: OR
x | y | out = x+y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Output is 1 if at least one input is 1.
More than two values can be “or-ed” together.
For example x+y+z = 1 if at least one of the three values is 1.

## Slide 7: XOR (Exclusive OR)
The number of inputs that are 1 matter.
More than two values can be “xor-ed” together.
General rule: the output is equal to 1 if an odd number of input values are 1 and 0 otherwise
x | y | out =
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 8: NOT
This function operates on a single Boolean value.
Its output is the complement of its input.
An input of 1 produces an output of 0 and an input of 0 produces an output of 1
x | x'
0 | 1
1 | 0

## Slide 9: NAND
Output value is the complemented output from an “AND” function.
x | y | out = x NAND y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 10: NOR
x | y | out = x NOR y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Output value is the complemented output from an “OR” function.

## Slide 11: XNOR
Output value is the complemented output from an “XOR” function.
x | y | out =x xnor y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 12: Manipulating Boolean Functions
x | y | z | xy' | yz | xy'+yz
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 1 | 1
Consider a function that must be 1 if either x = 1 and y = 0 or y = 1 and z = 1
We express it as: f(x,y,z) = xy’+ yz
Truth Table

## Slide 13: Combinatorial Logic Circuit
Combinatorial Logic Circuit that implements the function f(x,y,z)=xy’+yz

## Slide 14: DeMorgan’s Law
(ab)’=a’+b’
(a+b)’=a’b’
Property for generating equivalent functions
  Allows conversion of AND function to an equivalent OR function and vice-versa
Could allow the simplification of complex functions, that will allow a simpler design
It is useful in generating the complement of a function

## Slide 15: Using DeMorgan’s law
Generate complement of f(x,y,z)=xy’+yz
(xy’ + yz)’ = (xy’)’(yz)’ = (x’ + y)(y’ + z’) = x’y’ + x’z’ + yy’ + yz’ (because yy’=0) => (xy’+yz)’ = x’y’ + x’z’ + yz’
x | y | z | x'y' | x'z' | yz' | x'y‘ + y'z‘ + yz'
0 | 0 | 0 | 1 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0 | 0 | 0

## Slide 16: Karnaugh Map (K map)
Method for minimizing logic
The rows and columns of the K-map correspond to the possible values of the function's input
Each cell in the K-map represents a minterm (i.e. a three variables function has: x’y’z’, x’y’z, x’yz’, x’yz, xy’z’, xy’z, xyz’ and xyz)
Notes: <number>
Each possible set of input values of a digital function is called a minterm. For instance, for a function with three inputs (xyz), there are eight possible minterms: x’y’z’, x’y’z, x’yz’, x’yz, xy’z’, xy’z, xyz’ and xyz. We can express a function as a logical OR of all minterms for which its value is true.
Figure (a) shows a three input Karnaugh map. There are 8 possible combinations of input values and 8 cells in the K-map
Figure (b) shows a four input K-map.
Notice that in those K-maps the input values do not follow the linear progression: 00 01 10 11. Rather, they are ordered 00 01 11 10. This ordering is called Gray Code order.

## Slide 17: Gray Code
The 1-bit Gray code serves as basis for the 2-bit Gray code, the 2-bit Gray code is the basis for 3-bit Gray code, etc…
Gray code sequences are cycles: 000 -> 001 -> 011 -> 010 -> 110 -> 111 -> 101 -> 100 -> 000 ….
Adjacent values differ by only one bit
Notes: <number>
To derive the 2-bit sequence, we start by listing the 1-bit sequence. Then we list the 1 bit sequence again, but in reverse (reflected) order. We append a leading bit of 0 to the values in the original 1 bit sequence and a leading 1 to the values in the reflected sequence; this gives us the 2 bit Gray code.
The same algorithm is used to generate the (n+1)-bit Gray code out of n-bit Gray code.

## Slide 18: K-map Example
Consider (xy’+yz)’ = x’y’ + x’z’ + yz’
Group together the 1s in the map:
  g1: x’y’z’+x’y’z=x’y’(z’+z)=x’y’
  g2: x’yz’+xyz’ = yz’(x’+x)=yz’
  g3: x’yz’+x’y’z’=x’z’(y+y’)=x’z’
Must select the fewest groups that cover all active minterms (1s): (xy’ + yz)’= x’y’ + yz’
x | y | z | x'y'+y'z'+yz'
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 19: K-map for more complex function
The final minimized function is: x’z’ + wx’ + w’xyz
w’x’y’z’ + w’x’yz’ + wx’y’z’ + wx’y’z + wx’yz + wx’yz’

## Slide 20: Possible Implementations
Notes: <number>
The implementation of the function in the previous slide using two input gates (Figure a) and using two and four input gates (Figure b).

## Slide 21: Buffers
Regular buffer - always passes the input to the output
  its purpose being to boost the signal of the input to a higher level (maintain 0 or1 values to ensure that the system performs properly)
It will introduce a delay (as any other gate), known as propagation time through buffers.
  If they are not used wisely, they can be a dangerous source of hazard in digital logic circuits
in | out
0 | 0
1 | 1
Notes: <number>
Z – High impedance state
Two types of buffers: regular buffers and tri-state buffers.
The regular buffers always passes the input to the output, its purpose being to boost the current of the input to a higher level. When implemented in circuitry, the Boolean values 0 and 1 have specific voltage and current values; buffers maintain those values to ensure that the system performs properly.
The tri-state buffer is more complex. It has a data input, just like regular buffers, but also has an ENABLE input. If ENB=1 then the buffer is enabled and the input is passed directly to the output. However, if ENB=0, the buffer is disabled. Regardless of the input (represented by a don’t care value X in the truth table), the output is a high impedance state, Z. The tri-state buffer can also have an inverted enable signal.
High Impedance State: I = V/R (Ohm Law) if R (impedance) -> very big than the I (current) goes nearly to zero (I-> 0). For a constant voltage, the current decreases as impedance increases. The high impedance state reduces the current levels so low that the buffer appears in the circuit as not connected to anything. This is the role of tri-state buffers: they can be disabled to essentially break connections.

## Slide 22: Buffers
The tri-state buffer: it has a data input, just like regular buffers, but also has an ENABLE input.
  If ENB=1 then the buffer is enabled (input is passed to output)
  if ENB=0, the buffer is disabled (regardless of the input, output will be in a high impedance sate Z)
High Impedance State
  I = V/R (Ohm Law) if R (impedance) -> very big than the I (current) goes nearly to zero (I-> 0)
  They can be disabled to essentially break connections.
in | ENB | out
x | 0 | Z
0 | 1 | 0
1 | 1 | 1
in | ENB | out
x | 1 | Z
0 | 0 | 0
1 | 0 | 1

## Slide 23: Multiplexers
It is a selector.
  Chooses one of its data inputs and passes it to the output according to some other selection inputs
Consider four binary data inputs as inputs of a multiplexer.
  Two select signals will determine which of the four inputs will be passed to the output.
Figure (a) presents the internal structure of a four inputs multiplexer, b and c present the multiplexer schematic representation with active high enable signal (b) and active low enable signal (c)

## Slide 24: Multiplexer
Multiplexer internal structure
Notes: <number>
The four AND gates include the following pair of inputs, beside the data inputs: S1’S0’, S1’S0, S1S0’ and S1S0.
If S1=0 and S0=0 then the inputs at the top AND gate are input0, S1’(1) and S0’(1). The output of this AND gate is the value of the Input0. The other three AND gate inputs are either S1 or S0 or both … that means that the output of those gates is zero. The inputs of the OR gate are Input0 and three zeros => the output is Input0
Setting S1 and S0 to 01, 10 or 11 produces outputs of the value of Input1, Input2, respectively Input3
Finally the values are passed to a tri-state buffer. If the buffer is Enabled (E=1) than the value is passed to the output of the multiplexer. Otherwise, the output is high impedance value Z.

## Slide 25: Multiplexers
Multiplexer schematic representation with active high enable signal
Multiplexer schematic representation with active low enable signal

## Slide 26: Multiplexer
Multiplexers can be cascaded to select from a large number of inputs
4 to 1 multiplexer made of 2 to 1 multiplexers
Notes: <number>
Multiplexers can be cascaded to select from a large number of inputs.
This slide presents a 4-to-1 multiplexer constructed from 2-to-1 multiplexers
The two most left multiplexers are using the same control signal S0. These two multiplexers generate the two inputs for the final mux, which chooses the value to output.
This circuit performs exactly the same function as to the 4-to-1 multiplexer described above

## Slide 27: Decoders
Accepts a binary value as input and decodes it.
  It has n inputs and 2n outputs, numbered from 0 to 2n -1.
  Each output represents one minterm of the inputs
The output corresponding to the value of the n inputs is activated
  For example, a decoder with three inputs and eight outputs will activate output 6 whenever the input values are 110.
Figure (a) shows a two to four decoder internal structure, (b) and (c) show its schematic representation with active high enable signal and active low enable signal

## Slide 28: Decoders
For inputs S1S0 = 00, 01, 10 and 11 the outputs are 0, 1, 2 respectively 3 are active
As with the multiplexer, the output can tri-state all outputs
Notes: <number>
For inputs S1S0 = 00, 01, 10 and 11 the outputs are 0, 1, 2 respectively 3 are active
As with the multiplexer, the output can tri-state all outputs

## Slide 29: Decoders
Can have active high or active low enable signals.
  have active low outputs (the selected output has a value 0 and all the other outputs have a value 1)
  output all 0 when not enabled instead of state Z (the ones in the figure).
Notes: <number>
Decoders can have active high or active low enable signals. In addition, other variants have active low outputs (the selected output has a value 0 and all the other outputs have a value 1) or output all 0 when not enabled instead of state Z.

## Slide 30: Encoders
The encoder is the exact opposite of the decoder.
  It receives 2n inputs and outputs a n bit value corresponding to the one input that has a value of 1.
An 4-to-2 encoder and its schematic representations are presented in (a), (b) and (c) .
Exactly zero or one input is active
It will fail if more than one input is high
The encoder will output S1S0 = 00 if either input 0 is active or no input is active.
The V signal distinguishes between these two cases

## Slide 31: Encoders

## Slide 32: Priority Encoders
A priority encoder works just a regular encoder, with one exception: whenever one or more input is active, the output is set to correspond to the highest active input
For example, in a 4-to-2 encoder, in inputs 0,1 and 3 are active, then the S1S0=11 output is set, corresponding to the input 3.
This circuitry disables a given input if a higher numbered input is active
This guarantees that not more than one active signal is passed to the rest of the circuitry, which can be the same as the regular encoder

## Slide 33: Comparators
A comparator compares a two n-bit binary values to determine which is greater or if they are equal
  Consider the simple 1-bit comparator to illustrate the design
  It is possible to extend the design for multi-bit numbers
X>Y only if Xi=1, Yi=0
X<Y only if Xi=0, Yi=1
X=Y only if Xi=Yi=0 or Xi=Yi=1
1 bit comparator

## Slide 34: 1 bit comparator with propagated inputs
Notes: <number>
Compare two n bit numbers:
Start by comparing the most significant bits. If they are not equal, the number that has value 1 must be larger than the other one, regardless of the values of the less significant bits; 1XXX… is always greater than 0XXX..
If the most significant bits are equal, we must check the next bit (by applying the above method), and so on, until one number is found to be greater than the other, or all bits are checked and the numbers are found to be equal.
To do this, the comparator from the previous slide must be modified to include information from previous bit comparison.

## Slide 35: N bit comparator
If: X = Yin is active then the numbers are equal so far
If X>Yin or X<Yin is active, that value is simply passed through; This corresponds to the case where we have checked the high-order bits and already know which value is larger.
Notes: <number>
If: X = Yin is 1 then the numbers are equal so far
If X>Yin or X<Yin is active, that value is simply passed through; This corresponds to the case where we have checked the high-order bits and already know which value is larger.

## Slide 36: Adders
Used not only to perform addition but also to perform subtraction, multiplication and division
The most basic of the adders is the half adder
  Inputs two 1-bit value, x and y, and outputs their 2-bit sum as bits C and S
  Bit C is the carry and bit S is the sum
In real world, circuits that perform addition are more than 1 bit wide
A wider than 1 bit adder can’t use this circuit, because there is no way to input carry information from the previous bits

## Slide 37: Full Adder
Three inputs:
  Two data inputs
  One carry input
Functions

## Slide 38: N-bit adders
With the carry input, full adders can be cascaded to produce an n bit adder by connecting output C from one adder to input Cin of the next adder
Such an adder is called Ripple adder (because the bits ripple through the adder). Consider the worst case scenario (X=1111 and Y=0001) and follow the carry through the circuit
A four bit ripple adder is presented
Notes: <number>
X=1111 and Y=0001:
the right most full adder outputs C=1 and S=0
Next adder takes C as input, and will also output C=1 and S=0
Next adder …same operation
Each full adder has a small propagation delay, this delay adds up for all the adders in the circuit, as the carry bits are propagated, or ripple, from left to right.

## Slide 39: Memory
Group of circuits used to store data
  It is not strict combinatorial in design, but it can be used as combinatorial component in circuit design; for that reason we will include a brief presentation of the memory circuitry in this presentation
Has some number of memory locations, each of which stores a binary value of some fixed length
The number of locations and the size of locations is variable from memory chip to memory chip, but it is the same within the same chip
The size is denoted as the number of locations times the number of bits in each location

## Slide 40: Memory
The address input of a memory chip choose one of its locations.
  A memory chip with 2n locations requires n address inputs, usually labeled An-1An-2 … A0 (512 X 8 memory has address lines A8A7A6 … A0)
The data pins on a memory chip are used to access the data. There is one pin per bit in each location.
  For chips with m bits per location, these pins are Dm-1Dm-2 … D0 (512 X 8 memory has address lines D7D6D5 … D0)
Other pins:
  Chip enable (CE) enables or disables the chip. When disabled, the data pins output the high impedance Z; CE may be active high or low
  Some other type of pins, up the class of the memory
Notes: A memory chip of size 512 X 8 has 512 memory locations, each of which has 8 bits
<number>

## Slide 41: Memory
Two main memory classes:
  ROM (Read Only Memory) (a)
  RAM (Random Access Memory) (b)

## Slide 42: ROM
Data is programmed into the chip using an external ROM programmer
  The programmed chip is used as a component into the circuit
  The circuit doesn’t change the content of the ROM
Can be used as lookup tables to implement various boolean functions – can be used implement CLCs
Used by PCs to store the instructions that form their Basic Input/Output System (BIOS)
When power is removed from a ROM chip, the information is not lost, so it is a nonvolatile type of memory
It has a OE (Output Enable) specific control pin. Both OE and CE must be enabled in order for the ROM to output data; otherwise its data output is tri-stated.

## Slide 43: RAM
Read/write memory, that initially doesn’t contain any data
The computing system that it is used in usually stores data at various locations to retrieve it latter from these locations
Its data pins are bidirectional (data can flow into or out of the chip via these pins), as opposite to those of ROM that are output only
It loses its data once the power is removed, so it is a volatile memory
It has a directional select signal R/W’; When R/W’=1, the chip outputs data to the rest of the circuit; when R/W’ = 0 it inputs data from the rest of the circuit

## Slide 44: Combinatorial Circuit Design
Some useful components can be designed using the gates and the components described so far during the course
This part describes the design of a binary coded decimal (BCD) to 7 segment decoder, which is used in digital displays
This design will use only combinatorial logic gates, making use of the minimization logic techniques we have described
Alternative design can be done using lookup tables for each logical function stored in ROM

## Slide 45: Design Requirements
Design the logic circuitry that will drive a seven segment LED display and will be able to represent numbers from 0 to 9
Notes: <number>
The BCD to 7-segment decoder performs a common function: it converts the binary representation of a decimal digit, 0000 to 1001, to the signals needed to show the digit on a 7 segment display.

## Slide 46: Possible numbers and their representation on 7 segment display

## Slide 47: Truth Table

## Slide 48: Signal a implementation
X1X0 | 00 | 01 | 11 | 10
X3X2 |  |  |  | 
00 | 1 | 0 | 1 | 1
01 | 0 | 1 | 1 | 1
11 | X | X | X | X
10 | 1 | 1 | X | X
a = f(X3, X2, X1, X0) =
X3
+ X1
+ X2X0
+ X2’X1’X0’

## Slide 49: Signal b implementation
X1X0 | 00 | 01 | 11 | 10
X3X2 |  |  |  | 
00 | 1 | 1 | 1 | 1
01 | 1 | 0 | 1 | 0
11 | X | X | X | X
10 | 1 | 1 | X | X
b = f(X3, X2, X1, X0) =
X1’X0’
+ X1X0
+ X2’

## Slide 50: Signal c implementation
X1X0 | 00 | 01 | 11 | 10
X3X2 |  |  |  | 
00 | 1 | 1 | 1 | 0
01 | 1 | 1 | 1 | 1
11 | X | X | X | X
10 | 1 | 1 | X | X
c = f(X3, X2, X1, X0) =
X1’+
+ X0
+ X2

## Slide 51: Signal d implementation
X1X0 | 00 | 01 | 11 | 10
X3X2 |  |  |  | 
00 | 1 | 0 | 1 | 1
01 | 0 | 1 | 0 | 1
11 | X | X | X | X
10 | 1 | 0 | X | X
d = f(X3, X2, X1, X0) =
X3X1’X0’+
+ X2’X1’X0’
+ X3’X2’X1
+ X2X1’X0
+ X1X0’

## Slide 52: Signal e implementation
X1X0 | 00 | 01 | 11 | 10
X3X2 |  |  |  | 
00 | 1 | 0 | 0 | 1
01 | 0 | 0 | 0 | 1
11 | X | X | X | X
10 | 1 | 0 | X | X
e = f(X3, X2, X1, X0) =
X1X0’
+ X2’X1’X0’

## Slide 53: Signal f implementation
X1X0 | 00 | 01 | 11 | 10
X3X2 |  |  |  | 
00 | 1 | 0 | 0 | 0
01 | 1 | 1 | 0 | 1
11 | X | X | X | X
10 | 1 | 1 | X | X
f = f(X3, X2, X1, X0) =
X3
+ X2X0’
+ X2X1’
+ X1’X0’

## Slide 54: Signal g implementation
X1X0 | 00 | 01 | 11 | 10
X3X2 |  |  |  | 
00 | 0 | 0 | 1 | 1
01 | 1 | 1 | 0 | 1
11 | X | X | X | X
10 | 1 | 1 | X | X
g = f(X3, X2, X1, X0) =
X3
+ X2’X1
+ X2X1’
+ X1X0’

## Slide 55: 7 segment display
All the anode segments are connected together
Power must be applied externally to the anode connection that is common to all the segments
By applying the ground to a particular segment (i.e. a,b,g etc..), the appropriate segment will light up

## Slide 56: 7 segment common anode
A resistor should be added in order to limit the current through LED
The current to light the active LED is sink by the logic component, which is preferable

## Slide 57: 7 segment display
All the cathode of the LED are connected together
The common connection must be grounded and power must be applied to appropriate segment in order to illuminate that segment
The current to light the active LED is generated by the logic component, which generates the logic 1

## Slide 58: 7447 TTL IC
Real world example of BCD to 7 segment decoder
Outputs of the decoder are active low and a common anode 7 segment display is used

## Slide 59: References
“Computer Systems Organization & Architecture”, John D. Carpinelli, ISBN: 0-201-61253-4