## Slide 1: Computing Systems Organization
CT101 – Computing Systems

## Slide 2: Contents
Describe the operation of a computer at the functional level
Explain the function of the main components of a computer system
Detail the interaction of computer sub-systems
Detail the organization of computer sub-systems

## Slide 3: Computer organization
Instruction set architecture provides a good understanding of what a microprocessor can do; provides no information how to use the processor in a bigger system.
In order to design a computing system, more information is need than the instruction set
Computer system subsystems:
  CPU
  Buses
  Memory
  Input/Output

## Slide 4: Basic Computing Systems Organization

## Slide 5: System buses
Set of wires, that interconnects all the components (subsystems) of a computer
  A source component sources out data onto the bus
  A destination component inputs data from the bus
May have a hierarchy of buses
  Address, data and control buses to access memory and an I/O controller.
  Second set of buses from I/O controller to attached devices/peripherals
  PCI bus is an example of a very common local bus
Notes: <number>

## Slide 6: Address bus
CPU reads/writes data from the memory by addressing a unique location; outputs the location of the data (aka address) on the address buss; memory uses this address to access the proper data
Each I/O device (such as monitor, keypad, etc) has a unique address as well (or a range of addresses); when accessing a I/O device, CPU places its address on the address bus. Each device will detect if it is its own address and act accordingly
Devices always receive data from the CPU; CPU never reads the address buss (it is never addressed)

## Slide 7: Data bus
When the CPU fetches data from memory, it first outputs the address on the address bus, then the memory outputs the data onto the data bus; the CPU reads the data from data bus
When writing data onto the memory, the CPU outputs first the address on the address bus, then outputs the data onto the output bus; memory then reads and stores the data at the proper location
The process to read/write to a I/O device is similar

## Slide 8: Control bus
Address and data buses consist of n lines, which combine to transmit one n bit value; control bus is a collection of individual control signals
These signals indicate whether the data is to be read into or written out the CPU, whether the CPU is accessing memory or an IO device, and whether the I/O device or memory is ready for the data transfer
This bus is mostly a collection of unidirectional signals

## Slide 9: CPU
The Central Processing Unit (CPU a.k.a. Processor) is the chip which acts as a control center for all operations. It executes instructions (a program) which are contained in the memory section.
Basic operations involve
  the transfer of data between itself and the memory section
  manipulation of data in the memory section or stored internally
  the transfer of data between itself and input/output devices
The CPU is said to be the brains of any computer system. It provides all the timing and control signals necessary to transfer data from one point to another in the system.

## Slide 10: Programs: Instructions and Operands
A program = a number of CPU instructions.
Instruction components:
  an instruction code (aka OPCODE)
  one or more operand's (data which the instruction manipulates)
The instruction specifies to the CPU what to do, where the data is located, and where the output data (if any) will be put.
Instructions are held in the memory section of the computer system. Instructions are transferred one at a time into the CPU, where they are decoded then executed. Instructions follow each other in successive memory locations.
Memory locations are numbered sequentially. The processor unit keeps track of the instruction it is executing by using a internal counter (location in the memory) known as the program counter (sometimes called instruction pointer).

## Slide 11: Von Neumann and Harvard architectures
Von Neumann
  Allows instructions and data to be mixed and stored in the same memory module
  More flexible and easier to implement
  Suitable for most of the general purpose processors
Harvard:
  Uses separate memory modules for instructions and for data
  It is easier to pipeline and there are no memory alignment problems
  Higher memory throughput
  Suitable for DSP (Digital Signal Processors)
Notes: i.e. Pentium is using an von Neumann architecture for the external memory and is using a Harvard architecture for its internal cache memory (allowing 8KB of cache for data and anther (separate) 8kB of cache for instructions
<number>

## Slide 12: Computer Memory
Memory contains instructions for the processor to execute or data it operates on
Address Locations - Memory consists of a sequential number of locations, each of which are a specific number of bits wide.
  byte wide memory 8 bits (PC-8088)
  16 bits (XT-8086, AT-80286)
  32 bits (386DX, 486SX, 486DX)
  64 bits (Modern systems – Pentium and up)
Each memory location is referred to as an address, and generally expressed in hexadecimal notation (using base 16 numbers).
The size is denoted as the number of locations times the number of bits in each location
The processor selects a specific address in memory by placing the address on the address bus . The value on this address bus is used by the memory system to find the data at the specific location

## Slide 13: Computer Memory
The total number of address locations which can be accessed by the processor is known as its physical address space. How large this is determined by the size of the address bus, and is often expressed in terms of Kilobytes (x1024), Megabytes or Gigabytes.
  16 bits address bus = 64K (65536 locations)
  20 bits address bus = 1MB (IBM PC)
  32 bits address bus = 4GB (486DX)
Access Times - Access time refers to how long it takes the processor to read or write to a specific memory location within a chip. The limiting factor is the type of technology used to implement the memory cells inside the chip.
Volatility - This refers to whether or not the contents of the memory is lost when power is turned off. If the contents are lost, the memory is volatile. If the contents are retained, then the memory is non-volatile.

## Slide 14: Memory read/write operations
a) Memory read operation
b) Memory write operation
Notes: <number>
The I/O read and write operations are similar to the memory read and write operations.
A processor may use either memory mapped I/O (when the address of the I/O device is in the direct memory space, and the sequence to read/write data in the device are the same with the memory read/write sequence) or isolated I/O

## Slide 15: Input/Output devices
Peripheral devices allow input and output to occur.
Examples of peripheral devices are
  disk drive controllers
  keyboards
  mice
  video cards
  parallel and serial cards
  real-time clocks
The processor is involved in the initialization and servicing of these peripheral devices.

## Slide 16: I/O read/write operations
The I/O read and write operations are similar to the memory read and write operations.
A processor may use:
  memory mapped I/O (when the address of the I/O device is in the direct memory space, and the sequence to read/write data in the device are the same with the memory read/write sequence)
  isolated I/O – the process is similar, but the processor has a second set of control signals to make the distinction between a memory access and an I/O access (memory locations and I/O devices can be located at the same address, which makes this extra control signal necessary); for I/O operations, the processor holds IO/M’ (or similar) signal high for the duration of the I/O operation

## Slide 17: CPU Function – Instruction cycle
The instruction cycle is the procedure of processing an instruction by the microprocessor:
  Fetches (reads) the instruction from the memory
  Decodes the instruction, determining which instruction is to be executed (what instruction has been fetched)
  Executes the instruction – performs the operations necessary to complete what the instruction is suppose to do (different from instruction to instruction, may read data from memory, may write data to memory or I/O device, perform only operations within CPU or combination of those)
Each of the functions fetch -> decode -> execute consist of a sequence of one or more operations inside the CPU (and interaction with the subsystems)

## Slide 18: Fetch Cycle
In the first phase, the processor generates the necessary timing signals to fetch the next instruction from the memory system.
The instruction is transferred from memory to an internal location inside the processor (the instruction register)
In the above image, the processor is ready to begin the Fetch cycle. The current contents of the instruction counter (program counter) is address 0100. This value is placed on the address bus, and a READ signal is activated on the control bus. The memory receives this and finds the contents of the memory location 0100, which happens to be the instruction MOV AX, 0.
The memory places the instruction on the Data Bus, and the processor then copies the instruction from the Data Bus to the Instruction Register.

## Slide 19: Decode Cycle
The processor transfers the instruction from the instruction register to the Decode Unit.
It compares the instruction to an internal table, and when a match is found, the table contains the list of macro instructions (a number of steps) which are required to perform the instruction.
  In our case, the instruction means place the value 0 into the AX register. The decode unit now has all the details of how to do this.
During this phase the processor (if required by the instruction) will get any operand's required by the instruction.
  The final effect of instruction MOV AX, 0 is to set the value of the AX register of the processor to the constant value 0. The processor has the instruction (MOV AX), but now needs the constant value 0 to complete the instruction before executing it. In this instance, the processor will fetch the constant value 0 from the next location in memory (it is found immediately after the instruction, in the next memory location 0101)
Notes: <number>
The instruction is decoded by the processor. During this cycle, the processor, if required by the instruction, will get any operand's required by the instruction. For instance, the instruction MOV AX, 0 sets the value of the AX register of the processor to the constant value 0. The processor has the instruction (MOV AX), but now needs the constant value 0 to complete the instruction before executing it. In this instance, the processor will fetch the constant value 0 from the next location in memory (it is found immediately after the instruction, in the next memory location 0101)
In the above image, the processor transfers the instruction from the instruction register to the Decode Unit. It compares the instruction to an internal table, and when a match is found, the table contains the list of macro instructions (a number of steps) which are required to perform the instruction. In our case, the instruction means place the value 0 into the AX register. The decode unit now has all the details of how to do this.

## Slide 20: Execute Cycle
In the last phase, the processor executes the instruction. In the example above, this involves setting the contents of the internal register AX to the constant value 0
The final part of execute phase is to adjust the Instruction Counter to point to the next instruction to be executed, which is found at address 0102
Notes: <number>
In the above image, the processor executes the series of macro instructions related to the instruction MOV AX,0. The final part is to adjust the Instruction Counter to point to the next instruction to be executed, which is found at address 0102

## Slide 21: Fetch/Decode/Execute
Animated fetch decode execute

## Slide 22: References
“Computer Systems Organization & Architecture”, John D. Carpinelli, ISBN: 0-201-61253-4
“Operating Systems – A modern perspective”, Garry Nutt, ISBN 0-8053-1295-1