## Slide 1: Electronic Circuits
CT101 – Computing Systems

## Slide 2: Contents
Review the definition of voltage, electric current, resistance and power.
Introduction to various electronic components
Introduction to FET transistor design and principle of operation.
Use of FET transistor in logic circuits
Understand a logic gate function

## Slide 3: Electrical Charge
Matter is made up of atoms that contain both protons and electrons
  Protons are positively charged and electrons are negatively charged
Electric field surrounds every charged particle that can exert force on other charged particles.
  Field strength is the same for every electron and proton, with a magnitude of one “fundamental unit” of 1.602 x 10-19 Coulombs.
A coulomb is a measure of charge derived from a measurement of electric current – one coulomb of charge is transferred by one ampere of current in one second
  to get a matter of scale, one coulomb of charge flows through a 120W light bulb in one second.
Notes: All matter is made up of atoms that contain both positively and negatively charged particles (protons and electrons).
Surrounding every charged particle is an electric field that can exert force on other charged particles. A positive field surrounds a proton, and a negative field surrounds an electron.
Field strength is the same for every electron and proton, with a magnitude of one “fundamental unit” of 1.602 x 10-19 Coulombs.
A coulomb is a measure of charge derived from a measurement of electric current – one coulomb of charge is transferred by one ampere of current in one second
  to get a matter of scale, one coulomb of charge flows through a 120W light bulb in one second.
<number>

## Slide 4: Voltage
A positive electric field around a group of protons will exert a repelling force on other groups of protons and an attracting force on groups of electrons.
  Since an electric field can cause charged particles to move, it can do some amount of work, and so it is said to have electrical potential energy.
The amount of energy an electric field can impart to unit of charge is measured in joules per coulomb, more commonly known as voltage.
  Voltage is used as a short name for electrical potential difference.
Voltage is a way of using numbers to describe an electric field
  Voltage is the “electromotive force” that can cause charged particles to move.
Notes: A positive electric field surrounding a group of one or more protons will exert a repelling force on other groups of protons, and an attracting force on groups of electrons.
Since an electric field can cause charged particles to move, it can do some amount of work, and so it is said to have electrical potential energy.
The amount of energy an electric field can impart to unit charge is measured in joules per coulomb, more commonly known as voltage. Voltage is commonly used as a short name for electrical potential difference.
Voltage is a way of using numbers to describe an electric field
  Voltage may be thought of as the “electromotive force” that can cause charged particles to move.
<number>

## Slide 5: Power Supply
A power supply is a device containing imbalance of electrons.
  One side (the negative side) has material containing an abundance of electrons
  The other side (positive side) has material containing a relative absence of electrons.
The electrical potential energy available in the power supply, measured in volts, is determined by the number of electrons it can store, the separation distance between negative and positive materials, the properties of the barrier between the materials, and other factors.
  Some power supplies (like small batteries) output less than a volt, while others (like power generation stations) can output tens of thousands of volts.
Notes: A power supply is a device containing imbalance of electrons:
  One side (the negative side) has material containing an abundance of electrons
  The other side (positive side) has material containing a relative absence of electrons.
The electrical potential energy available in the power supply, measured in volts, is determined by the number of electrons it can store, the separation distance between negative and positive materials, the properties of the barrier between the materials, and other factors.
  Some power supplies (like small batteries) output less than a volt, while others (like power generation stations) can output tens of thousands of volts.
In general, power supplies of up to 9V – 12V are considered “safe” for humans to interact with (at least when skin layers are intact), but some people can have adverse (and potentially fatal) interactions with even low-voltage supplies. In our work, we will not encounter any supplies above 5V.
<number>

## Slide 6: Resitance
Electrons carry the smallest possible amount of negative charge, and billions of them are present in even the tiniest piece of matter.
  Insulators - electrons are held firmly in place by heavier, positively charged protons. Electrons cannot move freely between atoms.
  Conductors - electrons can move more easily from atom to atom.
The movement of electrons in a conductor is called electric current, measured in amperes.
  If a power supply is used to impress a voltage across a conductor, electrons will move from the negative side of the supply through the conductor towards the positive side.
  All materials, even conductors, exhibit some amount of resistance to the flow of electric current. The amount of resistance determines how much current can flow – the higher the resistance, the less current can flow.
Notes: Electrons carry the smallest possible amount of negative charge, and billions of them are present in even the tiniest piece of matter.
  Insulators - electrons are held firmly in place by heavier, positively charged protons. Electrons cannot move freely between atoms.
  Conductors - electrons can move more easily from atom to atom.
The movement of electrons in a conductor is called electric current, measured in amperes.
If a power supply is used to impress a voltage across a conductor, electrons will move from the negative side of the supply through the conductor towards the positive side.
  All materials, even conductors, exhibit some amount of resistance to the flow of electric current. The amount of resistance determines how much current can flow – the higher the resistance, the less current can flow.
A conductor has very low resistance, so a conductor by itself would never be placed across a power supply because far too much current would flow, damaging either the supply or the conductor itself. Rather an electronic component called a resistor would be used in series with the conductor to limit current flow
<number>

## Slide 7: Ohm’s Law
In 1825 Georg Ohm demonstrated through a series of experiments that voltage, current and resistance are related through a fundamental relationship
  Voltage (V) is equal to Current (I) times resistance (R), or V = I·R.
Resistance is measured in ohms, with the symbol Ω.
One volt impressed across 1 ohm of resistance will cause 1 amp of current to flow (and one coulomb of charge will pass through the resistor in one second).
Similarly, 3.3V impressed across 3.3 Ω will cause 1A of current to flow.

## Slide 8: Power
Collisions occur between the electrons flowing from the power supply and the materials in the resistor when current flows through.
  These collisions cause electrons to give up their potential energy, and that energy is dissipated as heat.
In electric circuits, power, measured in Watts, is defined as (voltage x current) or P = V·I.
  The power transferred to the resistor at any given time results in resistor heating. The more power transferred to the resistor, the hotter it gets.
  For a given voltage, a smaller-valued resistor would allow more current to flow (see Ohm’s law), and therefore more energy would be dissipated as heat (and the resistor would get hotter).
Notes: As current flows through the resistor, collisions occur between the electrons flowing from the power supply and the materials in the resistor. These collisions cause electrons to give up their potential energy, and that energy is dissipated as heat.
In electric circuits, power, measured in Watts, is defined as (voltage x current) or P = V·I. The power transferred to the resistor at any given time results in resistor heating. The more power transferred to the resistor, the hotter it gets.
  For a given voltage, a smaller-valued resistor would allow more current to flow (see Ohm’s law), and therefore more energy would be dissipated as heat (and the resistor would get hotter).
The total energy consumed in an electric circuit is simply the time integral of power, measured in Watts per second, or Joules. Thus, in the circuit above, the electric power delivered to the resistor is P = 3.3V x 1A, or 3.3Watts and in one second, 3.3W x 1second or 3.3J of energy is dissipated.
<number>

## Slide 9: Energy
The total energy consumed in an electric circuit is simply the time integral of power, measured in Watts per second, or Joules.
  Thus, in the circuit below, the electric power delivered to the resistor is P = 3.3V x 1A, or 3.3Watts and in one second, 3.3W x 1second or 3.3J of energy is dissipated.

## Slide 10: Electric and Electronic Circuits
Are collection of electronic components that have been assembled and interconnected to perform a given function
  The word circuit derives from the fact that electric power must flow from the positive terminal of a power source through one or more electronic devices and back to the negative terminal of a power source, thereby forming a circuit.
If the connections between an electronic device and either the positive or negative terminals of a power supply are interrupted, the circuit will be broken and the device will not function
Components in a circuit are connected to one another by means of electrical conductors or wires.
  Examples of components: resistors, capacitors, diodes, transistors, etc…
Notes: Many different types of components and devices can be found in modern circuits, including resistors, capacitors, and inductors, semiconductor devices like diodes, transistors, and integrated circuits
<number>

## Slide 11: Digital Circuits
Notes: A digital circuit is constructed of a power supply, devices, and conduction nets. Some nets provide
circuit inputs from the “outside world”; in a schematic, these input nets are generally shown entering
the left side of component and/or the overall circuit. Other nets present circuit outputs to the outside
world; these nets are generally shown exiting the schematic on the right. In the shown schematic, circuit components are shown as arbitrary shapes, nets are shown as lines, and inputs and outputs are denoted by connector symbols.
A digital circuit requires a power supply to provide a constant and stable source of electric power to all devices. A “power supply” in a digital circuit provides a local, contained imbalance of electrons that provides a voltage source that can do useful work, such as transmitting information through a conductor from one device to another.
A digital circuit allows a controlled flow of electrons from of the negative to positive side of the power supply, but only via the
paths designed into the circuit. As electrons flow to and from the devices in a given circuit, they can
change device properties in useful ways.
<number>

## Slide 12: Power Supply in Digital Circuits
In a digital circuit power supply voltage levels are constrained to two distinct values:
  “Logic High Voltage” (called LHV or Vdd) and
  “Logic Low Voltage” (called LLV or GND).
  VDD may be thought as source of positive charge while GND source of negative charge in a circuit
GND net in any circuit is the universal reference voltage against which all other voltages are measured.
  Any nodes labelled GND in a schematic are assumed to be connected into the same node. Often, a downward pointing triangle symbol is attached to a GND node in addition to (or instead of) the GND label.
Vdd node in a digital circuit is typically the highest voltage
  All nodes labelled Vdd are tied together into the same node.
Notes: Vdd may be thought of as the “source” of positive charges in a circuit, and GND may be thought of as the “source” of negative charges in a circuit.
In modern digital systems, Vdd and GND are separated by anywhere from 1 to 5 volts. Older or inexpensive circuits typically use 5 volts, while newer circuits use 1-3 volts.
<number>

## Slide 13: Review of Zeros and Ones
All data in digital circuits are represented by signals
  A signal in a digital circuit is a circuit net that transports an output voltage (either VDD or GND) from one device to one or more inputs connections of other devices.
The set of voltage values {Vdd, GND} that define the state of a signal wire in a digital system are commonly represented by the numeric symbols {1, 0}, with ‘1’ representing Vdd and ‘0’ representing GND.
  it follows that data in digital symbols can be represented by binary (base two) numbers. One signal wire in a digital circuit can carry one binary digit ( “bit”) of information;
Groupings of signal wires (called “bus”) can carry multiple bits that can define a binary number.
Notes: All data in digital circuits are represented by signals that can be in one of only two states, and all data operations combine two-state data inputs to produce two sate data outputs. Systems that use two-state data are known as binary systems, and a two-sate signal is a binary signal.
<number>

## Slide 14: Electronic Circuit Components
Resistors
Capacitors
Input Devices
Output Devices
Connectors
Printed Circuit Boards
Integrated Circuits

## Slide 15: Resistors
Two-terminal devices that restrict, or resist, the flow of current.
  The larger the resistor the less current can flow through it for a given voltage as demonstrated by Ohm’s law: V= I*R
Electrons flowing through a resistor collide with material in the resistor body, and it is these collisions that cause electrical resistance.
  These collisions cause energy to be dissipated in the form of heat or light (as in a toaster or light bulb).
Resistor Symbol
Carbon Film Through
Hole Resistor
Surface Mount
Resistors
Notes: <number>

## Slide 16: Resistors
The amount of power (in Watts) dissipated in a resistor can be calculated using the equation P= I*V = I2R)
  A resistor that can dissipate about 5 Watts of power would be about the size of a writing pen, and a resistor that can only dissipate 1/8 Watt is about the size of a grain of rice. If a resistor is placed in a circuit where it must dissipate more that its intended power, it will simply melt.
The physical size and appearance of a resistor is determined by the required application.
  Resistors that must dissipate large amounts of energy (such as in a toaster) are relatively large, whereas resistors that dissipate small amounts of current are relatively small.
  A one-ohm resistance is a relatively small value, and 100KOhm resistance is a relatively large value.

## Slide 17: Capacitors
Two-terminal device that can store electric energy in the form of charged particles.
  You can think of a capacitor as a reservoir of charge that takes time to fill or empty.
The voltage across a capacitor is proportional to the amount of charge it is storing – the more charge added to a capacitor of a given size, the larger the voltage across the capacitor.
  It is not possible to instantaneously move charge to or from a capacitor, so it is not possible to instantaneously change the voltage across a capacitor. It is this property that makes capacitors useful on many applications.
Capacitor Symbol
SMD ceramic at top left;
SMD tantalum at bottom left;
Through-hole tantalum at top right;
Through-hole electrolytic at bottom right;
Notes: Smaller capacitors, appearing as small blocks, disks or wafers, often have their values printed on them in an encoded manner . For these capacitors, a three-digit number typically indicates the capacitor value in picofarads. The first two digits provide the "base" number, and the third digit provides an exponent of 10 (so, for example, "104" printed on a capacitor indicates a capacitance value of 10 x 104 or 100000 pF). Occasionally, a capacitor will only show a two-digit number, in which case that number is simply the capacitor value in pF. (To be complete, if a capacitor shows a three-digit number and the third digit is 8 or 9, then the first two digits are multiplied by .01 and .1 respectively). Often, a single letter is appended to the capacitance value – this letter indicates the quality of the capacitor.
<number>

## Slide 18: Capacitors
Capacitance is measured in Farads.
  A one Farad capacitor can store one Coulomb of charge at one volt.
  For engineering on a small scale (i.e., hand-held or desk-top devices), a one Farad capacitor stores far too much charge to be of general use (it would be like a car having a 1000 gallon gas tank).
More useful capacitors are measured in micro-farads (uF) or pico-farads (pF).
  The terms "milli-farad“ and "nano-farad" are rarely used. Large capacitors often have their value printed plainly on them, such as "10 uF" (for 10 microfards).

## Slide 19: Input Devices (Buttons & Switches)
Input devices like buttons and switches should be able to produce VDD or GND based on some user action.
The slide switches are also known as “single throw-double pole” (STDP) switches, because only one switch (or throw) exists, but two positions (or poles) are available
The push button switches are “momentary” contact buttons
Push Button Switch STDP Switch
Notes: Circuits often require inputs that come directly from users (as opposed to inputs that come from other devices). User-input devices can take many forms, among them keyboards (as on a PC), buttons (as on a calculator or telephone), rotary dials, switches and levers, etc.
<number>

## Slide 20: Output Devices
Include computer monitors, LCD alphanumeric panels (as on a calculator), small lamps or light-emitting diodes (LED's).
Typical demo boards include some number of individual LED's, and seven-segment LED displays that can display the digits 0-9 in each digit position (each segment in the seven-segment display contains a single LED).
LED's are two-terminal semiconductor devices (diodes) that conduct current in only one direction (from the anode to the cathode).

## Slide 21: Output Devices
LED chips are secured inside a plastic housing, and they emit light at a given frequency (RED, YELLOW, etc.) when a small electric current (typically 10mA to 25mA – a catalogue value) flows through them.
LEDs will not turn on unless their anodes are some minimal voltage above their cathodes, typically about two volts (a catalogue value too). If less than the minimum threshold voltage is applied to an LED, it will remain dark.
LED requires a 2V drop to turn on, leaving 1.3V to drop across the resistor. Thus, a 130 ohm resistor is required to cause 10mA of current to flow in the circuit (3.3V – 2V = 1.3V and 1.3V / 130 ohms = 10mA).

## Slide 22: Connectors
They all communicate electronic information between the board and outside devices.
Since connectors come in so many different sizes and shapes, they are usually shown on the PCB silk screen and on circuit schematics as just rectangular boxes using a “J” labelling.
Notes: <number>

## Slide 23: Printed Circuit Board
Flat surface known as PCB
Two broad categories:
  prototype or experimental circuits (breadboards or proto-boards);
  production and/or commercial sale.
Production circuit boards design is done using CAD software (e.g. OrCAD, Protel, etc..).
Notes: Electronic components are often assembled and interconnected on a flat surface known as a circuit board.
The several types of existing circuit boards may be divided into two broad categories:
  those intended for prototype or experimental circuits;
  and those intended for production and/or commercial sale.
Circuit boards used for experimental work are often referred to as breadboards or protoboards.
Production circuit boards are design usually using specialised CAD software (e.g. OrCAD, Protel, etc..). Once the design is completed, the PCB has to be manufactured. Typical steps are shown in the picture.
Breadboards allow engineers to construct circuits quickly, so that they can be studied and modified
until an optimal design is discovered. In a typical breadboard use, components and wires are added to
a circuit in an ad hoc manner as the design proceeds.
<number>

## Slide 24: Integrated Circuits
Semiconductor circuits that use collections microscopic transistors that are all co-located on the same small piece of silicon. Represented with “U” on schematics or PCBs
Various functions from simple logic to highly complex processing functions.
  Some chips contain just a handful of transistors, while others contain sever al hundred million transistors (e.g. Intel processors).
Dual In-line Package vs Plastic Leaded Chip Carrier
Notes: As shown in the figures, the chips themselves are much smaller than their packages. During
manufacturing, the small, fragile chips are glued (using epoxy) onto the bottom half of the package,
bond-wires are attached to the chip and to the externally available pins, and then the top half of the
chip package is permanently affixed. Smaller chips may only have a few pins, but larger chips can
have more than 500 pins. Since the chips themselves are on the order of a centimetre on each side,
very precise and delicate machines are required to mount them in their packages.
Smaller chips might be packaged in a "DIP" package (DIP is an acronym for Dual In-line Package) as
shown below. Typically on the order of 1" x 1/4", DIP packages are most often made from black plastic, and they can have anywhere from 8 to 48 pins protruding in equal numbers from either side.
DIPs are used exclusively in through-hole processes. Larger chips use many different packages – one
common package, the "PLCC" (for Plastic Leaded Chip Carrier) is shown. Since these larger
packages can have up to several hundred pins, it is often not practical to use the relatively large leads
required by through-hole packages. Thus, large chips usually use surface mount packages, where the
external pins can be smaller and more densely packed.
<number>

## Slide 25: Digital Circuits
A digital circuit represents and manipulates information encoded as electric signals that can assume one of two Vdd or GND.
  If a given circuit net is at Vdd, then that signal is said to carry a logic ‘1’; if the net is at GND, then the node carries a logic ‘0’
The components in digital circuits are simple on/off switches that can pass logic ‘1’ and logic ‘0’ signals from one circuit net to another.
Most typically, these switches are arranged to combine input signals to produce an output signal according to basic logic relationships
Notes: Using just switches and resistors, it is also possible to create logical circuits that perform compound logical relationships, like “F = (A and B) or C”.

## Slide 26: Digital Circuits
Assuming a logic ‘1’ is closing the switch and a logic ‘0’ opens the switch, in the example the combination of switches can implement logic functions
  One well-known logic circuit is an NAND gate that combines two input signals to produce an output that is the logic NAND (negative AND) of the inputs (i.e., if both input1 and input2 are a ‘1’, then the output is a ‘0’).
  Another well-known logic circuit is OR gate that combines two input signlas to produce an output that is the logic OR of the inputs (i.e. if input1 or input2 are ‘1’, then the output is a ‘1’ )

## Slide 27: Transistors
…. ARE SWITCHES!!!
are arranged so that they can be turned on or off by signals carrying either VDD or GND
The transistor switches used in modern digital circuits are called “Metal Oxide Semiconductor Field Effect Transistors”, or MOSFETs (or just FETs).
FETs are three terminal devices that can conduct current between two terminals (the source and the drain) when a third terminal (the gate) is driven by an appropriate logic signal.
Notes: Of course, when the gate voltage changes from Vdd to GND or vice-versa, it must necessary assume voltages between Vdd and GND – we assume that this happens infinitely fast, so that we can ignore FET characteristics during the time the gate voltage is switching.

## Slide 28: Transistors
In the simplest FET model (which is appropriate for our use here), the electrical resistance between the source and the drain is a function of the gate-to-source voltage
  the higher the gate voltage, the lower the resistance (and therefore, the more current that can flow).
In analog circuits (like audio amplifiers), the gate-to-source voltage is allowed to assume any voltage between GND and Vdd;
  but in digital circuits, the gate-to-source voltage is constrained to be either Vdd or GND

## Slide 29: Transistors
FETs can be thought as electrically controllable “ON/OFF” switches
Notes: In a simple digital model, FETs can be thought of as electrically controllable "on/off" switches. An electrical connection is created between the
source and the drain (i.e., the FET is turned “on”) when the gate input is asserted. One kind of FET, called an nFET, is turned on when Vdd is present
at the control input, and a second type, called a pFET, is turned on when GND is present at the control input. Thus, an "asserted" input for an nFET means that
the control signal is at Vdd, and for a pFET means the control input is at a GND. The figures show the circuit symbols and equivalent switch diagrams for both nFETs and pFETs.

## Slide 30: More about Integrated Circuits
FETs can also be arranged into circuits that perform useful logic functions such as AND, OR, NOT, etc.
  Several very small FETs are constructed on a single small piece of silicon (or chip of silicon) and then interconnected with equally small metal wires.
These microscopic FETs are typically implemented using geometries in the region of 90, 60, 45, 28 or 20 nanometres.
  Since a silicon chip might measure several millimetres on a side, several millions of FETs can be constructed on a single chip.
Circuits assembled in this fashion are said to form "integrated circuits" (or IC’s), because all circuit components are constructed and integrated on the same piece of silicon.

## Slide 31: FETs Manufacturing
Ions implant to make silicon chip more conductive in the FET source and the drain regions – called diffusion regions
A thin insulating layer is created between these diffusion regions, and another conductor is "grown" on top of this insulator
The grown conductor (typically silicon) forms the gate, and the area immediately under the gate and between the diffusion regions is called the channel.
Finally, metal wires are connected to the source, drain, and gate structures so that the FET can be connected in a larger circuit.
Notes: A silicon chip is implanted with ions to make it more conductive in the areas that will become the FET source and the drain regions – called diffusion regions
A thin insulating layer is created between these diffusion regions, and another conductor is "grown" on top of this insulator
This grown conductor (typically silicon) forms the gate, and the area immediately under the gate and between the diffusion regions is called the channel. Finally, wires are connected to the source, drain, and gate structures so that the FET can be connected in a larger circuit.
<number>

## Slide 32: FETs – Principle of Operation
The source and drain diffusion areas of an nFET are implanted with negatively charged particles. When an nFET is used in a logic circuit, its source lead is connected to GND, so that the nFET source, like the GND node, has an abundance of negatively charged particles.
If the gate voltage of an nFET is at the same voltage as the source lead (i.e., GND), then the presence of the negatively charged particles on the gate repels negatively charged particles from the channel region immediately under the gate. A net positive charge accumulates under the gate, and two back-to-back positive-negative junctions of charge (called pn junctions) are formed. These pn junctions prevent current flow in either direction.
If the voltage on the gate >= the threshold voltage (about 0.5V), positive charges begin to accumulate on the gate and positive charges in the channel region immediately under the gate are repelled. A net negative charge accumulates under the gate, forming a channel of continuous conductive region in the area under the gate and between the source and drain diffusion areas. When the gate voltage reaches Vdd, a large conductive channel forms and the nFET is “strongly” on.
Notes: The basic principles of FET operation are actually quite straightforward. The discussion applies only to nFETs; pFET operation is entirely similar. but the voltages must be reversed.
Both the source and drain diffusion areas of an nFET are implanted with negatively charged particles. When an nFET is used in a logic circuit, its source lead is connected to GND, so that the nFET source, like the GND node, has an abundance of negatively charged particles.
If the gate voltage of an nFET is at the same voltage as the source lead (i.e., GND), then the presence of the negatively charged particles on the gate repels negatively charged particles from the channel region immediately under the gate (note that in semiconductors such as silicon, positive and negative charges are mobile and can move about the semiconductor lattice under the influence of charged-particle induced electric fields). A net positive charge accumulates under the gate, and two back-to-back positive-negative junctions of charge (called pn junctions) are formed. These pn junctions prevent current flow in either direction.
If the voltage on the gate is raised above the source voltage by an amount exceeding the threshold voltage (or Vth, which equals about 0.5V), positive charges begin to accumulate on the gate and positive charges in the channel region immediately under the gate are repelled. A net negative charge accumulates under the gate, forming a channel of continuous conductive region in the area under the gate and between the source and drain diffusion areas. When the gate voltage reaches Vdd, a large conductive channel forms and the nFET is “strongly” on.
<number>

## Slide 33: FETs Summary
nFETs used in logic circuits have their source leads attached to GND and Vdd on their gate turns them on
pFETs have their source leads attached to Vdd and GND on their gate turns them on

## Slide 34: Rules for Digital Logic Circuits with FETs
pFET sources must be connected to Vdd and nFET sources must be connected to GND
The circuit output must never be left floating;
The logic circuit output must never be connected to both Vdd and GND at the same time
  i.e., the circuit output must not be “shorted”.
The circuit must use the fewest possible number of FETs.

## Slide 35: Digital Logic Circuits with FETs
AND structure is created from Q1 and Q2.
  Using just these two FETs, Y is driven to GND whenever A and B are at Vdd. But we must ensure the output Y is at Vdd when A or B are at GND.
  This can be accomplished with an OR structure of pFETs (Q3 and Q4 in the parallel connection).
The series (AND) structure and parallel (OR) structure are assembled in the circuit on the right, which is a NAND gate!

## Slide 36: Basic Logic Circuits with FETs

## Slide 37: Logic Gates
A bubble on signal (either input or output) means that signal must be LLV to produce indicated logic function. Likewise, lack of bubble means signal must be LHV to produce indicated function.
  The symbols on the top may be considered the primary symbols (mostly used in schematics)
  Those on the bottom may be considered the conjugate symbols (properly, each symbol is the conjugate of the other).
Notes: A bubble on input means that input must be at LLV to produce the indicated logic function output, and a bubble on the output means that a LLV output signal is produced as a result of the logic function.
The lack of a bubble on inputs means that signals must be at LHV to produce the indicated function, and the lack of a bubble on the output means that a LHV signal is produced as a result of the logic function.
Note that each of the symbols above has two appearances. The symbols on the top may be considered the primary symbols, and those on the bottom may be considered the conjugate symbols (properly, each symbol is the conjugate of the other).
<number>

## Slide 38: Logic Circuits using Gates
A circuit schematic for any logic equation can be easily created by substituting logic gate symbols for logical operators, and by showing inputs as signal wires arriving at the logic gates.
Example: Implementing logic function "F = (AB)' + C'B in two different ways

## Slide 39: Reading Logic Circuits
The logic gate that drives the output signal defines the “major” logic operation, and it can be used to determine how other terms must be grouped in the equation.
  An inverter, or an output bubble on a logic gate, requires that the inverted signal or function output be shown in the output of the “downstream” gate
  A bubble on the input of a logic gate can be thought of as an inverter on the signal leading to the gate
Notes: <number>

## Slide 40: Logic Circuits Optimizations
Two “back-to-back” signal inversions cancel each other.
  That is, if a signal is inverted, and immediately inverted again before it is used anywhere else, then the circuit would perform identically. This observation can be used to simplify circuits, or to make them more efficient.
Simplification achieved by removing the two inverters on signal C, and made more efficient by adding inversions on internal nodes
  NAND gates (at four transistors each) could be used instead of AND/OR gates (at six transistors each).

## Slide 41: References
"Real Digital - A hands-on approach to digital design“, Clint Cole, http://www.digilentinc.com/classroom/realdigital/