## Slide 1: FSM Design & Implementation
CT101 – Computing Systems

## Slide 2: Contents
Finite State Machine theory
Front to end design of finite state machines, both Mealy and Moore types.
  Design example is provided for a modulo 6 counter
Other Design Examples
  String Checker
  Tollbooth Controller

## Slide 3: FSM Overview
Finite State Machine is a tool to model the desired behavior of a sequential system.
  The designer has to develop a finite state model of the system behavior and then designs a circuit that implements this model
A FSM consists of several states. Inputs into the machine are combined with the current state of the machine to determine the new state or next state of the machine.
Depending on the state of the machine, outputs are generated based on either the state or the state and inputs of the machine.

## Slide 4: FSM Structure
X represents the range of possible input values (2n)
Y represents the range of output values (2m)
Q represents the range of the possible states of the system (2k)
Transfer functions:
  f: X x Q -> Y
  g: X x Q -> Q

## Slide 5: FSM Representation
FSM = (X, Y, Q, f, g)
  If there is no state in the Q range (Q≡Ø, the circuitry has no history), then:
    g: X x Ø->Ø, there is no state transition function
    f: X x Ø -> Y is becoming f: X -> Y
  In this case, the FSM is equivalent to an CLC
    FSM| Q≡Ø = CLC = (X, Y, f)

## Slide 6: Asynchronous vs. Synchronous
Async FSM – the next state becomes the present state after the delays through the delay elements
Sync FSM – obtained by replacing the delay elements di with memory elements (registers).
  The wi bits of the next state will be written in the registers (memory elements) only on the clock (on edge or level) is applied.

## Slide 7: Sync FSM with immediate outputs
The FSM where the outputs, after they have been calculated, are used immediately (of course in the stable period of the state interval), is called an immediate state machine.
Notes: <number>
The FSM where the outputs, after they have been calculated, are used immediately (of course in the stable period of the state interval), is called an immediate state machine.

## Slide 8: Sync FSM with delayed outputs
The next state is assigned as present state on the next clock cycle. Similarly, we can proceed with the outputs, obtaining the delayed state machine. Each bit of the output is passed through a memory element.
Notes: <number>
The next state is assigned as present state on the next clock cycle. Similarly, we can proceed with the outputs, obtaining the delayed state machine. Each bit of the output is passed through a memory element. Through this memory elements, whenever the t+1 clock cycle is applied, the values calculated by CLC (function f) for t interval are assigned to the output (Y(t+1) := Y(t) ). By doing this we can obtain outputs unaffected by combinatorial hazard.

## Slide 9: Timing diagram for synchronous FSM
Notes: <number>
The clock signal has a period T;
The T period has to be bigger than the transient interval;
The transient interval is given by the longest propagation path through the CLC
The inputs are stable over the clock period (written into a register whenever the clock is applied and held stable over the clock period)

## Slide 10: FSM Example
Events:
  Wake up at fixed time every day
  Weekends: you don’t need alarm, so you wake up, turn off the alarm and resume sleep
FSM modeling this chain of events, with:
  Three states:
    Asleep
    Awake but still in bed
    Awake and up
  Inputs:
    Alarm
    Weekday (determines you how to react to alarm)
  Outputs:
    Turn off the alarm

## Slide 11: State tables
Similar to the truth table
  Doesn’t contain the system clock when specifying its transitions (it is implicit that transitions occur only when allowed by clock)
Unless different stated, all the transitions are occurring on the positive edge of the clock
Present State | Inputs | Next State | Outputs

## Slide 12: Alarm clock state table
When you are asleep and alarm goes on, you go from being asleep to being awaked in bed; you also turn off the alarm
The next two rows encode your actions:
  You get up
  You go back to sleep
This table doesn’t cover what you wouldn’t do…(i.e. if you are asleep and the alarm doesn't go off, you remain asleep, etc..)
Present State | Alarm | Weekday | Next State | Turn off alarm
Asleep | On | X | Awake in bed | Yes
Awake in bed | Off | Yes | Awake and up | No
Awake in bed | Off | No | Asleep | No

## Slide 13: Alarm clock state table
Covers all the cases
  First row covers the situation you are asleep, the alarm doesn’t go off and you remain asleep
  Last row covers the situation you are awake and up and you remain awake and up
  The third row covers the case you are already up and the alarm goes off. You turn it off and remain Awake in bed
Present State | Alarm | Weekday | Next State | Turn off alarm
Asleep | Off | X | Asleep | No
Asleep | On | X | Awake in bed | Yes
Awake in bed | On | X | Awake in bed | Yes
Awake in bed | Off | Yes | Awake and up | No
Awake in bed | Off | No | Asleep | No
Awake and up | X | X | Awake and up | No

## Slide 14: State diagram
Graphical representation of the state table
  Each state is represented by a circle vertex
  Each row of the state table is represented as a directed arc from present state vertex to the next state vertex
In this diagram, the outputs are associated with the states

## Slide 15: Alternative state diagram
The outputs are associated with the arcs
  An output of 1 represents that “turn off the alarm” is Yes
  By convention , inputs which are don’t care and inactive outputs are not shown.

## Slide 16: Mealy and Moore machines
Moore machine
  Associates its outputs with states
  The outputs are represented either within the vertex corresponding to a state or adjacent to the vertex
Mealy machine:
  Associates its outputs with the transitions
  In addition to the input values, each arc also shows the output values generated during the transition; the format of the label of each arc is Inputs/Outputs
Both can be used to represent any sequential system and each has its advantages.

## Slide 17: Mealy FSM
Output is dependent on the inputs and the current state
Delayed output FSM implies the fact that the calculated output for an input applied at time t is assigned at time t+1. This is correct at an Mealy FSM

## Slide 18: Moore FSM
Output is dependent only on the current state
Immediate Moore FSM: the output is obtained with a clock period delay, since the then the next state becomes present state
Delayed Moore FSM: the output is actually obtained with two clock period delay, because of the Registers Bank 2

## Slide 19: Moore machine diagram
Self arcs can be missing (since it outputs are associated with the states and not with the arcs)
Offers a simpler implementation when the output values depend only on the state and not on the transitions
It is well suited for representing the control units of microprocessors

## Slide 20: Mealy machine diagram
Self arcs must be shown (because the output values are shown on the arcs)
Can be more compact than Moore machine, especially when two or more arcs with different output values go into the same state

## Slide 21: Modulo 6 Counter - Specification
A module 6 counter is a 3-bit counter that counts through the following sequence:
  000->001->010->011->100->101->000->…
  0 -> 1 -> 2 -> 3 -> 4 -> 5 -> 0 …
It doesn’t use value 6 (110) nor 7 (111)
It has an input U that controls the counter:
  When U=1 the counter increments its value on the rising edge of the clock
  When U=0 the counter retains its value on the rising edge of the clock
The value of the count is represented as three bit value (V2V1V0)
There is an additional output C (Carry) that is 1 when going from 5 to 0 and 0 otherwise (the C output remains 1 until the counter goes from 0 to 1)

## Slide 22: Modulo 6 Counter – State table
For each state examine what happens for all possible values of the inputs
  In state S0 input U can be either 0 or 1
  If U=0 the state machine remains in state S0 and outputs C=1 and V2V1V0=000
  If U=1 the state machine goes in state S1, outputs C=1 and V2V1V0=001
In the same manner, each state goes to the next state if U=1 and remains in the same state if U=0
Present State | U | Next State | C | V2V1V0
S0 | 0 | S0 | 1 | 000
S0 | 1 | S1 | 0 | 001
S1 | 0 | S1 | 0 | 001
S1 | 1 | S2 | 0 | 010
S2 | 0 | S2 | 0 | 010
S2 | 1 | S3 | 0 | 011
S3 | 0 | S3 | 0 | 011
S3 | 1 | S4 | 0 | 100
S4 | 0 | S4 | 0 | 100
S4 | 1 | S5 | 0 | 101
S5 | 0 | S5 | 0 | 101
S5 | 1 | S0 | 1 | 000

## Slide 23: Modulo 6 Counter - Mealy state diagram
The outputs are represented on the arcs as CV2V1V0

## Slide 24: Modulo 6 Counter – Moore state diagram
The outputs are represented adjacent to the state
The inputs are represented on the arcs

## Slide 25: FSM Implementation
Converting a problem to equivalent state table and state diagram is just the first step in the design process
The next step is to design the system hardware that implements the state machine.
This section deals with the process involved to design the digital logic to implement a finite state machine.
First step is to assign a uniquely binary value to each of the state that the machine can be in. The state must be encoded in binary.
Next we design the hardware to go from the current state to the correct next state. This logic converts the current state and the current input values to the next state values and stores that value.
The final stage would be to generate the outputs of the state machine. This is done using combinatorial logic.

## Slide 26: Assigning State Values
Each state must be assigned to a unique binary value; for a machine with n states we have [log2n] bits;
For the modulo 6 counter example, we have six states. We will assign state value 000 to S0, 001 to S1, and so on, up to 101 to S5.

## Slide 27: Assigning State Values
Any values can be assigned to the states, some values can be better than others (in terms of minimizing the logic to create the output and the next state values)
This is actually an iterative process: first the designer creates a preliminary design to generate the outputs and the next states, then modifies the state values and repeats the process. There is a rule of thumb, that simplifies the process: whenever possible, the state should be assigned the same with the output values associated with that state. In this case, same logic can be used to generate the next state and the output

## Slide 28: Mealy and Moore Machine Implementations
The current state value is stored into the register
The state value together with the machine inputs, are input to a logic block (CLC) that generates the next state value and machine outputs
The next state is loaded into the register on the rising edge of the clock signal

## Slide 29: Mod 6 Counter – Mealy Implementation
The logic block (CLC) is specific to every system and may consist of combinatorial logic gates, multiplexers, lookup ROMs and other logic components
The logic block can’t include any sequential components, since it must generate its value in one clock cycle
The logic block contains two parts:
  One that generates the outputs (f function, CLC1)
  One that generates the next state (g function, CLC2)

## Slide 30: Mod 6 Counter – Moore Implementation
The outputs depend only on the present state and not on its inputs
Its configuration is different than the Mealy machine
  The system output depends only on the present state, so the implementation of the output logic is done separately
  The next state is obtained from the input and the present state (same as for the Mealy machine)

## Slide 31: Generating the Next State
Since the Mealy and Moore machines must traverse the same states under the same conditions, their next state logic is identical
We will present three methods to generate the next state logic:
  (i) Combinatorial logic gates
  (ii) Using multiplexers
  (iii) Using lookup ROM
To begin with, we need to setup the truth table for the next state logic

## Slide 32: Modulo 6 Counter - Next State Logic (i)
The system inputs and the present states are the inputs of the truth table
Next state bits are the outputs
We have to construct a Karnaugh map for each output bit and obtain its equation
After that we design the logic to match the equations
Present State P2P1P0 | U | Next State N2N1N0
000 | 0 | 000
000 | 1 | 001
001 | 0 | 001
001 | 1 | 010
010 | 0 | 010
010 | 1 | 011
011 | 0 | 011
011 | 1 | 100
100 | 0 | 100
100 | 1 | 101
101 | 0 | 101
101 | 1 | 000

## Slide 33: Modulo 6 Counter – Next State Logic (i)
N2 = P2P0’ + P2U’ +P1P0U
N1 = P1P0’ + P1U’ + P2’P1’P0U
N0 = P0’U + P0U’

## Slide 34
Modulo 6 Counter – Next State implementation using logic gates (i)

## Slide 35: Modulo 6 Counter – Next State Logic (ii)
An alternative approach to design the next state logic is to use multiplexers.
Each input to the multiplexer corresponds to the next state under one possible value of the system inputs; the inputs drive the input signals of the multiplexer
For the modulo 6 counter, we use the U input to drive the multiplexer; U is choosing one of two possible next states, the next state if U=0 and the next state if U = 1
To determine the inputs of the multiplexer we begin with splitting the truth table into multiple truth tables, one for each possible value of the system inputs
Then we follow the procedure we have used to obtain the next state using combinatorial logic gate

## Slide 36: Modulo 6 Counter – Next State Logic (ii)
Initial truth table is broken into two tables:
  One for U=0
  One for U=1
Create Karnaugh maps from these tables to obtain the equations for N2, N1 and N0 when U=0 and when U=1
Present State P2P1P0 | Next State N2N1N0
000 | 000
001 | 001
010 | 010
011 | 011
100 | 100
101 | 101
Present State P2P1P0 | Next State N2N1N0
000 | 001
001 | 010
010 | 011
011 | 100
100 | 101
101 | 000
U = 1
U = 0

## Slide 37: Modulo 6 Counter – Next State Logic (ii)
U = 0 we observe that the next state is the same with current state:
  N2 = P2
  N1 = P1
  N0 = P0
U = 1:
  N2 = P2P0’+P1P0
  N1 = P1P0’ + P2’P1’P0
  N0 = P0’
P1P0 | 00 | 01 | 11 | 10
P2 |  |  |  | 
0 | 0 | 0 | 1 | 0
1 | 1 | 0 | x | x
P1P0 | 00 | 01 | 11 | 10
P2 |  |  |  | 
0 | 0 | 1 | 0 | 1
1 | 0 | 0 | x | x
P1P0 | 00 | 01 | 11 | 10
P2 |  |  |  | 
0 | 1 | 0 | 0 | 1
1 | 1 | 0 | x | x
N2
N1
N0
U=1

## Slide 38: Modulo 6 Counter – Next State Logic (ii)
Next state logic implementation using multiplexers and logic gates. Please note that using multiplexers simplifies the combinatorial logic circuitry

## Slide 39: Modulo 6 Counter – Next State Logic (iii)
Another approach to generate the next state logic for a FSM is to use a lookup ROM.
In this approach, the present state values and inputs are connected to the address bus of a ROM; the next state is obtained from the ROM outputs
The correct value must be stored in each location of the ROM to ensure proper operation

## Slide 40: Modulo 6 Counter – Next State Logic (iii)
The three bits that encode the present state (P2P1P0) are connected to the three high-order address inputs to the ROM (A3A2A1)
The one condition bit U is connected to the low order address bit A0
The data in each location is the value of the next state for present state and the input values

## Slide 41: Generating System Outputs
Both for Mealy and Moore machines we follow the same design procedure to develop their output logic
There are two approaches to generate the output (similar to generate the next state logic):
  Using combinatorial logic gates
  Using lookup ROM
We are beginning by creating the truth table:
  For Mealy machine, the truth table inputs will be the present state and the system inputs, and the table outputs are the system outputs
  For Moore machine, only the state bits are inputs of the truth table, since only these bits are used to generate the system outputs; the table outputs are the system outputs

## Slide 42: Modulo 6 Counter Outputs (i)
P2P1P0 | U | C | V2V1V0
000 | 0 | 1 | 000
000 | 1 | 0 | 001
001 | 0 | 0 | 001
001 | 1 | 0 | 010
010 | 0 | 0 | 010
010 | 1 | 0 | 011
011 | 0 | 0 | 011
011 | 1 | 0 | 100
100 | 0 | 0 | 100
100 | 1 | 0 | 101
101 | 0 | 0 | 101
101 | 1 | 1 | 000
P2P1P0 | C | V2V1V0
000 | 1 | 000
001 | 0 | 001
010 | 0 | 010
011 | 0 | 011
100 | 0 | 100
101 | 0 | 101
Mealy
Moore

## Slide 43: Outputs - Mealy (i)
P0U | 00 | 01 | 11 | 10
P2P1 |  |  |  | 
00 | 0 | 0 | 0 | 0
01 | 0 | 0 | 1 | 0
11 | X | X | X | X
10 | 1 | 1 | 0 | 1
P0U | 00 | 01 | 11 | 10
P2P1 |  |  |  | 
00 | 0 | 0 | 1 | 0
01 | 1 | 1 | 0 | 1
11 | X | X | X | X
10 | 0 | 0 | 0 | 0
P0U | 00 | 01 | 11 | 10
P2P1 |  |  |  | 
00 | 0 | 1 | 0 | 1
01 | 0 | 1 | 0 | 1
11 | X | X | X | X
10 | 0 | 1 | 0 | 1
P0U | 00 | 01 | 11 | 10
P2P1 |  |  |  | 
00 | 1 | 0 | 0 | 0
01 | 0 | 0 | 0 | 0
11 | X | X | X | X
10 | 0 | 0 | 1 | 0
V2 = P2P0’ + P1P0U + P2U’
V1 = P2P1’P0U + P1P0’ + P1U’
V1 = P0’U + P0U’
C = P2’P1’P0’U’ + P2P0U

## Slide 44: Modulo 6 Counter Outputs (i)
Mealy machine (note that the equations for V2, V1, V0 are exactly the same as for the N2, N1, N0. This is the result of optimally assignation of the state values. Same combinatorial logic can be use to obtain the outputs):
  V2 = P2P0’+P2U’+P1P0U
  V1 = P1P0’+P1U’+P2P1’P0U
  V0 = P0’U+P0U’
  C = P2’P1’P0’U’+P2P0U
Moore machine:
  V2 = P2
  V1 = P1
  V0 = P0
  C = P2’P1’P0’ = (P2+P1+P0)’

## Slide 45: Modulo 6 Counter – Mealy Implementation (i)

## Slide 46: Modulo 6 Counter – Moore Implementation (i)

## Slide 47: Modulo 6 Counter System Outputs (ii)
It is possible to generate the system outputs using a lookup ROM
The inputs of the lookup ROM are the present states and the system inputs. The outputs of the ROM are the system outputs
We can use same ROM to generate next state and system outputs
Since for the Mealy machine V2 = N2, V1 = N1 and V0 = N0, only one output is used for each pair. If the outputs weren’t the same as the next state, separate output bits would be needed.

## Slide 48: Modulo 6 Counter – Moore Implementation (ii)

## Slide 49: FSM Alternative Design
There are some other methods to implement a FSM; one of them is to use a a counter to store the current state and a decoder to generate signals corresponding to each state
The counter can be incremented, cleared or loaded with a value to go from one state to another.
Unlike the other methods, you don’t have to generate the same state value in order to remain in the same state; this can be accomplished by neither incrementing, clearing nor loading the counter

## Slide 50: FSM with Counter and Decoder
The counter plays the role of the register in Mealy and Moore designs, as well as a portion of the next state logic
The state value is input to a decoder; each output of the decoder represents one state
The decoder outputs and system inputs are input to the logic bloc that generates the system outputs and the information needed to generate the next state value

## Slide 51: FSM with Counter and Decoder
If the system inputs are used to generate both the next state and the system outputs, this design can be used to implement a Mealy machine.
If the system outputs are generated solely by using the state value, and the system inputs are used only to generate the next state, then it implements a Moore machine
Modulo 6 counter Moore implementation using this approach

## Slide 52: Modulo 6 Counter Moore Implementation with Counter and Decoder
Notes: <number>
The 3 bit counter holds the present state and sends its value to the decoder
The output of the decoder represents the states: output 0 represents S0, and so on
Since this is a Moore machine, only the state signals are combined to produce the outputs V2V1V0 and C
The next state control, when U=1, the modulo 6 counter is incremented. When the output is 000, 001, 010, 011, 100 this is accomplished by incrementing the state counter. When the output is 101, incrementing the counter would result in a value of 110 of the state counter, which is not right, while 000 is the desired value. In this case, the counter is cleared. When U=0, no signal is activated and the counter retains its previous value, thus remaining in the same state.

## Slide 53: Unused States
The FSM presented so far works well if it is in a known state
There will be a problem if the machine enters an unused state, also called unknown state or undefined state
This could be caused by a flaw in the design but most of the times, this is happening when the machine powers-up.

## Slide 54: Modulo 6 Counter Analysis
The modulo 6 counter (consider Moore machine implementation) has six states with binary state values from 000 to 101
The state value is stored in the register of the finite state machine hardware; an unused state is entered when an unused state is stored in this register;
The unused states for this design example are 110 and 111

## Slide 55: Modulo 6 Counter – Revised (acceptable) diagram
When present state is 110, the next state is 110 if U=0 or 111 if U=1
When present state is 111, the next state is 111 if U=0 or 000 if U=1

## Slide 56: Modulo 6 Counter – Revised (wrong) diagram
If a circuit that implements this diagram powers-up in state 110 or 111 will never reach a valid state

## Slide 57: Modulo 6 Counter – State diagram with dummy states
Create dummy states for all unused states
Each dummy state would go to a known state on the next clock cycle (usually to a reset state)
Two dummy states: 110 and 111
By convention, the values 1 on the arcs indicate that the transfer is unconditional – that is always taken
Note also the output values: C=0 and 111 indicates the user that the machine is in an invalid state (it is a design decision)

## Slide 58: Modulo 6 Counter – State table with dummy states
Use this table to construct Karnaugh maps which yield to the following values for next state and outputs:
Next state:
  N2 = P2P1’P0’ + P2P1’U’ + P1P0U
  N1 = P2’P1P0’ + P2’P1U’ + P2’P1’P0U
  N0 = P2’P0’U + P1’P0’U + P1’P0U’
Outputs:
  C = P2’P1’P0’
  V2 = P1
  V1 = P1
  V0 = P0 + P2P1
P2P1P0 | U | N2N1N0 | C | V2V1V0
000 | 0 | 000 | 1 | 000
000 | 1 | 001 | 0 | 001
001 | 0 | 001 | 0 | 001
001 | 1 | 010 | 0 | 010
010 | 0 | 010 | 0 | 010
010 | 1 | 011 | 0 | 011
011 | 0 | 011 | 0 | 011
011 | 1 | 100 | 0 | 100
100 | 0 | 100 | 0 | 100
100 | 1 | 101 | 0 | 101
101 | 0 | 101 | 0 | 101
101 | 1 | 000 | 1 | 000
110 | 0 | 000 | 0 | 111
110 | 1 | 000 | 0 | 111
111 | 0 | 000 | 0 | 111
111 | 1 | 000 | 0 | 111

## Slide 59: String Checker - Specification
Inputs a string of bits, one per clock cycle
When the previous three bits form the pattern 110, it sets the output match M=1; otherwise M=0
The pattern is checked continuously through the entire bit stream; the system DOES NOT check the first three bits and then the next three bits and so on.
The system checks bits 123 and then bits 234 and then bits 345 and so on.

## Slide 60: String Checker – State table (i)
The last there bits received represent the state of the system
Bits are received from left to right (i.e. the current state is S0 (000), if a new bit with value 1 is received, then the next value of the state is S1 (001)
Each state goes from one state in two possible next states, depending on the value of I
Example S2 corresponds to the case where last three bits were 010:
  I=0 next state is S4 (100), output is M=0
  I=1 next state is S5 (101), output is M=0
Present State | I | Next State | M
S0 (000) | 0 | S0 | 0
S0 (000) | 1 | S1 | 0
S1 (001) | 0 | S2 | 0
S1 (001) | 1 | S3 | 0
S2 (010) | 0 | S4 | 0
S2 (010) | 1 | S5 | 0
S3 (011) | 0 | S6 | 1
S3 (011) | 1 | S7 | 0
S4 (100) | 0 | S0 | 0
S4 (100) | 1 | S1 | 0
S5 (101) | 0 | S2 | 0
S5 (101) | 1 | S3 | 0
S6 (110) | 0 | S4 | 0
S6 (110) | 1 | S5 | 0
S7 (111) | 0 | S6 | 1
S7 (111) | 1 | S7 | 0

## Slide 61: String Checker – State diagrams (i)

## Slide 62: String Checker – Hardware Implementation
Assign values to the states
  S0 assign 000 and so on
Start to design the hardware for this implementation, starting with generic
  Design the next state logic
  Design the output logic
P2P1P0 | I | N2N1N0
000 | 0 | 000
000 | 1 | 001
001 | 0 | 010
001 | 1 | 011
010 | 0 | 100
010 | 1 | 101
011 | 0 | 110
011 | 1 | 111
100 | 0 | 000
100 | 1 | 001
101 | 0 | 010
101 | 1 | 011
110 | 0 | 100
110 | 1 | 101
111 | 0 | 110
111 | 1 | 111

## Slide 63
String Checker – Next state logic
  N2 = P1
  N1 = P0
  N0 = I
P0I | 00 | 01 | 11 | 10
P2P1 |  |  |  | 
00 | 0 | 0 | 0 | 0
01 | 1 | 1 | 1 | 1
11 | 1 | 1 | 1 | 1
10 | 0 | 0 | 0 | 0
N2
P0I | 00 | 01 | 11 | 10
P2P1 |  |  |  | 
00 | 0 | 1 | 1 | 0
01 | 0 | 1 | 1 | 0
11 | 0 | 1 | 1 | 0
10 | 0 | 1 | 1 | 0
P0I | 00 | 01 | 11 | 10
P2P1 |  |  |  | 
00 | 0 | 0 | 1 | 1
01 | 0 | 0 | 1 | 1
11 | 0 | 0 | 1 | 1
10 | 0 | 0 | 1 | 1
N1
N0

## Slide 64: String Checker – Moore Machine
The output logic is straight forward; when the machine is in state S6 the M is 1, otherwise is 0. This can be implemented as:
  M = P2P1P0’

## Slide 65: String Checker – Mealy Machine
M = P1P0I’
P0I | 00 | 01 | 11 | 10
P2P1 |  |  |  | 
00 | 0 | 0 | 0 | 0
01 | 0 | 0 | 0 | 1
11 | 0 | 0 | 0 | 1
10 | 0 | 0 | 0 | 0
M
P2P1P0 | I | M
000 | 0 | 0
000 | 1 | 0
001 | 0 | 0
001 | 1 | 0
010 | 0 | 0
010 | 1 | 0
011 | 0 | 1
011 | 1 | 0
100 | 0 | 0
100 | 1 | 0
101 | 0 | 0
101 | 1 | 0
110 | 0 | 0
110 | 1 | 0
111 | 0 | 1
111 | 1 | 0

## Slide 66: String Checker – State table (ii)
Sometimes there are simpler alternative methods:
  S0 – no bits matched
  S1 – one bit matched
  S2 – two bits matched
S3 – three bits matched
In each state, consider the possible values of the input bit and determine which next state is appropriate
Present State | I | Next State | M
S0 (---) | 0 | S0 (---) | 0
S0 (---) | 1 | S1 (--1) | 0
S1 (--1) | 0 | S0 (---) | 0
S1 (--1) | 1 | S2 (-11) | 0
S2 (-11) | 0 | S3 (110) | 1
S2 (-11) | 1 | S2 (-11) | 0
S3 (110) | 0 | S0 (---) | 0
S3 (110) | 1 | S1 (--1) | 0

## Slide 67: String Checker – State diagrams (ii)

## Slide 68: Toll Booth Controller - Specification
Has two input sensors:
  Car sensor C (car in toll booth) = 1 if there is a car or 0 if there is no car
  Coin sensor (and its value):
    I1I0 = 00 – no coin has been inserted
    I1I0 = 01 – a 5 cents coin has been inserted
    I1I0 = 10 – a 10 cents coin has been inserted
    I1I0 = 11 – a quarter coin has been inserted
Two output lights and one alarm output
  When a car pulls into the toll booth, a red light (R) is lit until the driver deposits at least 35 cents, when the red light goes off and the green light (G) is lit;
  The green light remains lit until the car leaves the toll booth, when this happen, the red light is lit again
  If the car leaves the toll booth without paying the full amount, the red light is lit and the alarm (A) sound
  The alarm remains active until another car pulls into the booth

## Slide 69: Toll Booth Controller – States definition
State | Condition | R | G | A
Snocar | No car in toll booth | 1 | 0 | 0
S0 | Car in toll booth, 0 cents paid | 1 | 0 | 0
S5 | Car in toll booth, 5 cents paid | 1 | 0 | 0
S10 | Car in toll booth, 10 cents paid | 1 | 0 | 0
S15 | Car in toll booth, 15 cents paid | 1 | 0 | 0
S20 | Car in toll booth, 20 cents paid | 1 | 0 | 0
S25 | Car in toll booth, 25 cents paid | 1 | 0 | 0
S30 | Car in toll booth, 30 cents paid | 1 | 0 | 0
Spaid | Car in toll booth, toll paid | 0 | 1 | 0
Scheat | Car left toll booth without paying full toll | 1 | 0 | 1

## Slide 70: Toll Booth Controller – State table
Current State | C | I1I0 | Next state | R | G | A
Snocar | 0 | XX | Snocar | 1 | 0 | 0
Snocar | 1 | XX | S0 | 1 | 0 | 0
Spaid | 0 | XX | Snocar | 1 | 0 | 0
Spaid | 1 | XX | Spaid | 0 | 1 | 0
Scheat | 0 | XX | Snocar | 1 | 0 | 1
S0 | 0 | XX | Scheat | 1 | 0 | 1
S0 | 1 | 00 | S0 | 1 | 0 | 0
S0 | 1 | 01 | S5 | 1 | 0 | 0
S0 | 1 | 10 | S10 | 1 | 0 | 0
S0 | 1 | 11 | S25 | 1 | 0 | 0
S5 | 0 | XX | Scheat | 1 | 0 | 1
S5 | 1 | 00 | S5 | 1 | 0 | 0
S5 | 1 | 01 | S10 | 1 | 0 | 0
S5 | 1 | 10 | S15 | 1 | 0 | 0
S5 | 1 | 11 | S30 | 1 | 0 | 0
S10 | 0 | XX | Scheat | 1 | 0 | 1
S10 | 1 | 00 | S10 | 1 | 0 | 0
S10 | 1 | 01 | S15 | 1 | 0 | 0
S10 | 1 | 10 | S20 | 1 | 0 | 0
S10 | 1 | 11 | Spaid | 0 | 1 | 0
Current State | C | I1I0 | Next state | R | G | A
S15 | 0 | XX | Scheat | 1 | 0 | 1
S15 | 1 | 00 | S15 | 1 | 0 | 0
S15 | 1 | 01 | S20 | 1 | 0 | 0
S15 | 1 | 10 | S25 | 1 | 0 | 0
S15 | 1 | 11 | Spaid | 0 | 1 | 0
S20 | 0 | XX | Scheat | 1 | 0 | 1
S20 | 1 | 00 | S0 | 1 | 0 | 0
S20 | 1 | 01 | S25 | 1 | 0 | 0
S20 | 1 | 10 | S30 | 1 | 0 | 0
S20 | 1 | 11 | Spaid | 0 | 1 | 0
S25 | 0 | XX | Scheat | 1 | 0 | 1
S25 | 1 | 00 | S25 | 1 | 0 | 0
S25 | 1 | 01 | S30 | 1 | 0 | 0
S25 | 1 | 10 | Spaid | 0 | 1 | 0
S25 | 1 | 11 | Spaid |  |  | 
S30 | 0 | XX | Scheat | 1 | 0 | 1
S30 | 1 | 00 | S30 | 1 | 0 | 0
S30 | 1 | 01 | Spaid | 0 | 1 | 0
S30 | 1 | 10 | Spaid | 0 | 1 | 0
S30 | 1 | 11 | Spaid | 0 | 1 | 0

## Slide 71: Toll Booth Controller – Moore State diagram

## Slide 72: References
“Computer Systems Organization & Architecture”, John D. Carpinelli, ISBN: 0-201-61253-4