## Slide 1: HDL – Hardware Description Languages
CT101 – Computing Systems

## Slide 2: Contents
Overview, modules, simulation & synthesis
Combinatorial logic modeling
Structural modeling
Sequential logic modeling
More combinatorial logic
Finite state machines modeling
Parametrized modules
Testbenches

## Slide 3: Overview
Two way to describe logic
  Schematic entry (done up to now)
  HDL (Hardware Description Language)
    VHDL
    (System) Verilog
Module – block of hardware with inputs and outputs
  Examples: an AND gate, a multiplexer, etc..
  Can be described in two ways
    Behavioral – what module does
    Structural – how a module is built from simpler pieces

## Slide 4: Example of HDLs
System Verilog | VHDL (Just for example, we will NOT study VHDL)
module sillyfunction(input logic a, b, c, output logic y); assign y = ~a & ~b & ~c ¦ a & ~b & ~c ¦ a & ~b & c; endmodule | library IEEE; use IEEE.STD_LOGIC_1164.all; entity sillyfunction is port(a, b, c: in STD_LOGIC; y: out STD_LOGIC); end; architecture synth of sillyfunction is begin y <= (not a and not b and not c) or (a and not b and not c) or (a and not b and c); end;
A SystemVerilog module begins with the module name and a listing of the inputs and outputs. The assign statement describes combinational logic. ~ indicates NOT, & indicates AND, and ¦ indicates OR. Logic signals such as the inputs and outputs are Boolean variables (0 or 1). They may also have floating and undefined values, as discussed latter. The logic type was introduced in SystemVerilog. It supersedes the reg type, which was a perennial source of confusion in Verilog. logic should be used everywhere except on signals with multiple drivers. Signals with multiple drivers are called nets and will be explained latter. | VHDL code has three parts: the library use clause, the entity declaration, and the architecture body. The entity declaration lists the module name and its inputs and outputs. The architecture body defines what the module does. VHDL signals, such as inputs and outputs, must have a type declaration. Digital signals should be declared to be STD_LOGIC type. STD_LOGIC signals can have a value of '0' or '1', as well as floating and undefined values. The STD_LOGIC type is defined in the IEEE.STD_LOGIC_1164 library, which is why the library must be used. VHDL lacks a good default order of operations between AND and OR, so Boolean equations should be parenthesized.
Notes: A module is a good application of modularity. It has a well defined interface, consisting of its inputs and outputs, and it performs a specific function. The particular way in which it is coded is unimportant to others that might use the module, as long as it performs its function.
<number>

## Slide 5: A bit of history
System Verilog | VHDL
Verilog was developed by Gateway Design Automation as a proprietary language for logic simulation in 1984. Gateway was acquired by Cadence in 1989 and Verilog was made an open standard in 1990 under the control of Open Verilog International. The language became an IEEE standard1 in 1995. The language was extended in 2005 to streamline idiosyncrasies and to better support modeling and verification of systems. These extensions have been merged into a single language standard, which is now called System Verilog (IEEE STD 1800-2009). System Verilog file names normally end in .sv. | VHDL is an acronym for the VHSIC Hardware Description Language. VHSIC is in turn an acronym for the Very High Speed Integrated Circuits program of the US Department of Defense. VHDL was originally developed in 1981 by the Department of Defense to describe the structure and function of hardware. Its roots draw from the Ada programming language. The language was first envisioned for documentation but was quickly adopted for simulation and synthesis. The IEEE standardized it in 1987and has updated the standard several times since. This chapter is based on the 2008 revision of the VHDL standard (IEEE STD 1076-2008), which streamlines the language in a variety of ways. VHDL file names normally end in .vhd.

## Slide 6: Simulation & Synthesis
HDL is written to describe a piece of digital electronics. The behavior needs to be correct (verified via simulation) and has to be transformed into logic gates (done via synthesis).
Simulation – inputs are applied to a module and the outputs are checked to verify that the module operates correctly | Synthesis – a textual description of a module (e.g. Verilog) is transformed into logic gates
Simulation results for sillyfunction presented earlier (y is true when a,b,c are 000, 100 or 101 | Synthesis results for sillyfuncion. Can be represented as netlist or schematic
Notes: Circuit descriptions in HDL resemble code in a programming language. However, you must remember that the code is intended to represent
hardware. SystemVerilog and VHDL are rich languages with many commands. Not all of these commands can be synthesized into hardware. We will focus on System Verilog commands that are synthesizable in hardware.
<number>

## Slide 7: Simulation & Synthesis
Not all code is synthesizable
  For example, a command to print results on the screen during simulation does not translate into hardware.
  Because our primary interest is to build hardware, we will emphasize a synthesizable subset of System Verilog.
We will divide HDL code into synthesizable modules and a testbench.
  The synthesizable modules describe the hardware.
  The testbench contains code to apply inputs to a module, check whether the output results are correct, and print discrepancies between expected and actual outputs. Testbench code is intended only for simulation and cannot be synthesized.
Notes: One of the most common mistakes for beginners is to think of HDL as a computer program rather than as a shorthand for describing digital
hardware. If you don’t know approximately what hardware your HDL should synthesize into, you probably won’t like what you get. You might
create far more hardware than is necessary, or you might write code that simulates correctly but cannot be implemented in hardware. Instead,
think of your system in terms of blocks of combinational logic, registers, and finite state machines. Sketch these blocks on paper and show how
they are connecte.d before you start writing code
<number>

## Slide 8: Combinatorial Logic Modeling
We design synchronous sequential circuits, which consist of combinational logic and registers.
The outputs of combinational logic depend only on the current inputs.
This section describes how to write behavioral models of combinational logic with System Verilog.

## Slide 9: Bitwise operators
module inv(input logic [3:0] a, output logic [3:0] y); assign y = ~a; endmodule
a[3:0] represents a 4-bit bus. The bits, from most significant to least significant, are a[3], a[2], a[1], and a[0]. This is called little-endian order, because the least significant bit has the smallest bit number. We could have named the bus a[4:1], in which case a[4] would have been the most significant. Or we could have used a[0:3], in which case the bits, from most significant to least significant, would be a[0], a[1], a[2], and a[3]. This is called big-endian order.
Endianness is purely arbitrary for this example (inverters don’t care how bits are received), however
Endianness matters for operators (such as addition, etc..). Any order is acceptable as long as is used consistently.
We will use the little-endian order [N-1:0] in our System Verilog examples.

## Slide 10: More bitwise operators
module gates(input logic [3:0] a, b, output logic [3:0] y1, y2, y3, y4, y5); /* five different two-input logic gates acting on 4-bit busses */ assign y1 = a & b; // AND assign y2 = a ¦ b; // OR assign y3 = a ^ b; // XOR assign y4 = ~(a & b); // NAND assign y5 = ~(a ¦ b); // NOR endmodule
~, ^, and ¦ are examples of SystemVerilog operators, whereas a, b, and y1 are operands. A combination of operators and operands, such as a & b, or ~(a ¦ b), is called an expression. A complete command such as assign y4 = ~(a & b); is called a statement. assign out = in1 op in2; is called a continuous assignment statement. Continuous assignment statements end with a semicolon. Anytime the inputs on the right side of the = in a continuous assignment statement change, the output on the left side is recomputed. Thus, continuous assignment statements describe combinational logic.

## Slide 11: Reduction Operators
module and8(input logic [7:0] a, output logic y); assign y = &a; // &a is much easier to write than // assign y = a[7] & a[6] & a[5] & a[4] & // a[3] & a[2] & a[1] & a[0]; endmodule
Reduction operators imply a multiple-input gate acting on a single bus. This code describes an eight input AND gate with inputs a7, a6 .. A0. Analogous reduction operators exist for OR, XOR, NAND, NOR and XNOR gates
Recall that an multiple input XOR performs parity, returning TRUE if odd number of inputs are TRUE

## Slide 12: Conditional Assignment
module mux2(input logic [3:0] d0, d1, input logic s, output logic [3:0] y); assign y =s ? d1 : d0; endmodule
The conditional operator ?: chooses, based on a first expression, between a second and third expression. The first expression is called the condition. If the condition is 1, the operator chooses the second expression. If the condition is 0, the operator chooses the third expression. ?: is especially useful for describing a multiplexer because, based on the first input, it selects between two others. If s is 1, then y = d1. If s is 0, then y = d0. ?: is also called a ternary operator, because it takes three inputs. It is used for the same purpose in the C and Java programming languages.
Selects the output from amongst alternatives based on input called the condition
We show herewith a 2:1 4 bit multiplexer implemented using conditional assignment

## Slide 13: Internal Variables
module fulladder(input logic a, b, cin, output logic s, cout); logic p, g; assign p =a ^ b; assign g =a & b; assign s = p ^ cin; assign cout = g ¦ (p & cin); endmodule
In System Verilog, internal signals are usually declared as logic.
Useful to break a complex function into intermediate steps. Full adder is described by following equations (where ⊕ is XOR):
S = A ⊕ B ⊕ Cin
Cout = AB+ACin+BCin
Intermediate signals, P and G:
P = A ⊕ B
G=AB
Rewrite full adder as follows:
S=P ⊕ Cin
Cout = G + PCin
Notes: It is important that in a conventional language S = P⊕Cin comes after P = A⊕B, because statements are
executed sequentially.
In an HDL, the order does not matter. Like hardware, HDL assignment statements are evaluated any time the inputs, signals on the right hand side, change their value, regardless of the order in which the assignment statements appear in a module.
<number>

## Slide 14: Precedence
The operator precedence for SystemVerilog is much like you would expect in other programming languages. In particular, AND has precedence over OR.
So in the fulladder module earlier we could take advantage of this precedence to eliminate the parentheses.

## Slide 15: Numbers
The format for declaring constants is N'Bvalue, where N is the size in bits, B is a letter indicating the base, and value gives the value.
Numbers can be specified in binary, octal, decimal, or hexadecimal (bases 2, 8, 10, and 16, respectively). The size, i.e., the number of bits, may optionally be given, and leading zeros are inserted to reach this size.
Underscores in numbers are ignored and can be helpful in breaking long numbers into more readable chunks.
If the size is not given, the number is assumed to have as many bits as the expression in which it is being used. Zeros are automatically padded on the front of the number to bring it up to full size. For example, if w is a 6-bit bus, assign w = 'b11 gives w the value 000011. It is better practice to explicitly give
the size. An exception is that '0 and '1 are SystemVerilog idioms for filling a bus with all 0s and all 1s, respectively.

## Slide 16: Z’s and X’s
module tristate(input logic [3:0] a, input logic en, output tri [3:0] y); assign y = en ? a : 4'bz; endmodule
Notice that y is declared as tri rather than logic. logic signals can only have a single driver. Tristate busses can have multiple drivers, so they should be declared as a net. Two types of nets in SystemVerilog are called tri and trireg. Typically, exactly one driver on a net is active at a time, and the net takes on that value. If no driver is active, a tri floats (z), while a trireg retains the previous value. If no type is specified for an input or output, tri is assumed. Also note that a tri output from a module can be used as a logic input to another module.
HDLs use z to indicate a floating (high impedance) value, z is particularly useful for describing a tristate buffer, whose output floats when the enable is 0.
Similarly, HDLs use x to indicate an invalid logic level. If a bus is simultaneously driven to 0 and 1 by two enabled tristate buffers (or other gates), the result is x, indicating contention. If all the tristate buffers driving a bus are simultaneously OFF, the bus will float, indicated by z.
This example shows a tri-state buffer Verilog example
Notes: At the start of simulation, state nodes such as flip-flop outputs are initialized to an unknown state (x in SystemVerilog and u in VHDL). This is helpful to track errors caused by forgetting to reset a flip-flop before its output is used
<number>

## Slide 17: Gates with Z’s and X’s
AND Gate truth table with z and x
If a gate receives a floating input, it may produce an x output when it can’t determine the correct output value.
Similarly, if it receives an illegal or uninitialized input, it may produce an x output

## Slide 18: Bit Swizzling
assign y = {c[2:1], {3{d[0]}}, c[0], 3'b101};
The {} operator is used to concatenate busses. {3{d[0]}} indicates three copies of d[0]. Don’t confuse the 3-bit binary constant 3'b101 with a bus named b. Note that it was critical to specify the length of 3 bits in the constant; otherwise, it would have had an unknown number of leading zeros that might appear in the middle of y. If y were wider than 9 bits, zeros would be placed in the most significant bits.
Often it is necessary to operate on a subset of a bus or to concatenate (join together) signals to form busses. These operations are collectively known as bit swizzling.
Example is given the 9-bit value c2c1d0d0d0c0101 using bit swizzling operations.

## Slide 19: Delays
‘timescale 1ns/1ps module example(input logic a, b, c, output logic y); logic ab, bb, cb, n1, n2, n3; assign #1 {ab, bb, cb} = ~{a, b, c}; assign #2 n1 = ab & bb & cb; assign #2 n2 =a & bb & cb; assign #2 n3 =a & bb & c; assign #4 y = n1 ¦ n2 ¦ n3; endmodule
SystemVerilog files can include a timescale directive that indicates the value of each time unit. The statement is of the form 'timescale unit/precision. In this file, each unit is 1 ns, and the simulation has 1 ps precision. If no timescale directive is given in the file, a default unit and precision (usually 1 ns for both) are used. In SystemVerilog, a # symbol is used to indicate the number of units of delay.
HDL statements may be associated with delays, specified in arbitrary units. They are useful during simulation and are ignored during synthesis.
Example shows sillyfunction with delays. y = a’b’c’+ ab’c’ +ab’c. It assumes that inverters have a delay of 1 ns, three-input AND gates have a delay of 2 ns, and three-input OR gates have a delay of 4 ns.
Simulation waveforms, with y lagging 7 ns after the inputs, are shown. Note that y is initially unknown at the beginning of the simulation.
Notes: HDL statements may be associated with delays specified in arbitrary units. They are helpful during simulation to predict how fast a circuit will work
(if you specify meaningful delays) and also for debugging purposes to understand cause and effect (deducing the source of a bad output is tricky if
all signals change simultaneously in the simulation results).
These delays are ignored during synthesis; the delay of a gate produced by the synthesizer depends on its tpd and tcd specifications, not on numbers in HDL code.
HDL Example 4.13 adds delays to the original function from HDL
Example 4.1, y = a b c+ ab c +abc. It assumes that inverters have a delay
of 1 ns, three-input AND gates have a delay of 2 ns, and three-input OR
gates have a delay of 4 ns. Figure 4.10 shows the simulation waveforms,
with y lagging 7 ns after the inputs. Note that y is initially unknown at
the beginning of the simulation.
<number>

## Slide 20: Structural Modeling
We have discussed behavioral modeling, describing a module in terms of the relationships between inputs and outputs.
Structural modeling describes a module in terms of how it is composed of simpler modules.
We will show how to build a 4:1 multiplexer from instances of 2:1 multiplexers

## Slide 21: Structural Modeling
module mux4(input logic [3:0] d0, d1, d2, d3, input logic [1:0] s, output logic [3:0] y); logic [3:0] low, high; mux2 lowmux(d0, d1, s[0], low); mux2 highmux(d2, d3, s[0], high); mux2 finalmux(low, high, s[1], y); endmodule
The three mux2 instances are called lowmux, highmux, and finalmux. The mux2 module must be defined elsewhere in the SystemVerilog code (we defined it earlier and we will define it again usin tristate buffers).
Each copy of the 2:1 multpiplexer is called an instance
Multiple instances of the same module are distinguished by different names
This is an example of regularity where a 2:1 multiplexer is reused multiple times

## Slide 22: Structural Modeling
module mux2(input logic [3:0] d0, d1, input logic s, output tri [3:0] y); tristate t0(d0, ~s, y); tristate t1(d1, s, y); endmodule
In SystemVerilog, expressions such as ~s are permitted in the port list for an instance. Arbitrarily complicated expressions are legal but discouraged because they make the code difficult to read.
We use structural modeling to construct a 2:1 multiplexer from a pair of tristate buffers.
Building logic out of tristates is not recommended, however.

## Slide 23: Structural Modeling
module mux2_8(input logic [7:0] d0, d1, input logic s, output logic [7:0] y); mux2 lsbmux(d0[3:0], d1[3:0], s, y[3:0]); mux2 msbmux(d0[7:4], d1[7:4], s, y[7:4]); endmodule
Used 4 bit 2:1 muxes to create an 8 bit 2:1 wider mux
General rule – describe complex systems hierarchically. Overall system is described structurally from its building blocks and so forth recursively until the pieces are simple enough to describe behaviorally.
Example: building 2:1 8 bit mux from 2:1 4 bit muxes.
Advice: avoid mixing structural and behavioral descriptions inside single module.

## Slide 24: Sequential Logic
HDL synthesizers recognize certain idioms and turn them into specific sequential circuits.
This section presents the proper idioms to describe registers and latches. Other coding styles may simulate correctly but synthesize into circuits with blatant or subtle errors.

## Slide 25: Registers
module flop(input logic clk, input logic [3:0] d, output logic [3:0] q); always_ff @(posedge clk) q <= d; endmodule
In general, a SystemVerilog always statement is written in the form always @(sensitivity list) statement; The statement is executed only when the event specified in the sensitivity list occurs. In this example, the statement is q <= d (pronounced “q gets d”). Hence, the flip-flop copies d to q on the positive edge of the clock and otherwise remembers the old state of q. Note that sensitivity lists are also referred to as stimulus lists. <= is called a nonblocking assignment. Think of it as a regular = sign for now; Note that <= is used instead of assign inside an always statement. always statements can be used to imply flip-flops, latches, or combinational logic, depending on the sensitivity list and statement. Because of this flexibility, it is easy to produce the wrong hardware inadvertently. SystemVerilog introduces always_ff, always_latch, and always_comb to reduce the risk of common errors. always_ff behaves like always but is used exclusively to imply flip-flops and allows tools to produce a warning if anything else is implied.
Vast majority of modern commercial systems are built with registers using positive edge-triggered D flip-flops
Example here shows the SystemVerilog constructs for such register

## Slide 26: Resettable Registers
module flopra(input logic clk, input logic reset, input logic [3:0] d, output logic [3:0] q); // asynchronous reset always_ff @(posedge clk, posedge reset) if (reset) q <= 4'b0; else q <= d; endmodule module floprs(input logic clk, input logic reset, input logic [3:0] d, output logic [3:0] q); // synchronous reset always_ff @(posedge clk) if (reset) q <= 4'b0; else q <= d; endmodule
Multiple signals in an always statement sensitivity list are separated with a comma or the word or. Notice that posedge reset is in the sensitivity list on the asynchronously resettable flop, but not on the synchronously resettable flop. Thus, the asynchronously resettable flop immediately responds to a rising edge on reset, but the synchronously resettable flop responds to reset only on the rising edge of the clock.
When power is first applied to a circuit, the output of a flip-flop is unknown.
It is good practice to use resettable registers so that on power-up you can put system in a known state. Reset can be either synchronous or asynchronous
It is difficult to distinguish between sync and async reset in a sechmatic. Usually, async is at the bottom of the flip-flop while syn reset is at the left side (as an input).
Notes: Asynchronous reset occurs immediately
Synchronous reset occurs on the next rising edge of the clock
<number>

## Slide 27: Enabled Registers
module flopenr(input logic clk, input logic reset, input logic en, input logic [3:0] d, output logic [3:0] q); // asynchronous reset always_ff @(posedge clk, posedge reset) if (reset) q <= 4'b0; else if (en) q <= d; endmodule
Enabled registers respond to the clock only when enable is asserted
Example herewith shows an asynchronously resettable enabled register that retains its old value if both reset and en are FALSE.

## Slide 28: Multiple Registers
module sync(input logic clk, input logic d, output logic q); logic n1; always_ff @(posedge clk) begin n1 <= d; // nonblocking q <= n1; // nonblocking end endmodule
Notice that the begin/end construct is necessary because multiple statements appear in the always statement. This is analogous to {} in C or Java. The begin/end was not needed in the flopra or floprs example because if/else counts as a single statement.
A single always statement can be used to describe multiple pieces of hardware.
Consider a synchronizer made out of two back to back flip-flops. On the risign edge of the clk, d is copied to n1. At the same time, n1 is copied to q.

## Slide 29: Latches
module latch(input logic clk, input logic [3:0] d, output logic [3:0] q); always_latch if (clk) q <= d; endmodule
always_latch is equivalent to always @(clk, d) and is the preferred idiom for describing a latch in SystemVerilog. It evaluates any time clk or d changes. If clk is HIGH, d flows through to q, so this code describes a positive level sensitive latch. Otherwise, q keeps its old value. SystemVerilog can generate a warning if the always_latch block doesn’t imply a latch.
A positive level D latch is transparent when the clock is HIGH, allowing data to flow from input to output. The latch becomes opaque when the clock is LOW, retaining its old state
Not all synthesis tools support latches well. Unless you know that your tool does support latches and you have a good reason to use them, avoid them and use edge-triggered flip-flops instead.

## Slide 30: More Combinatorial Logic
We used assignment statements to describe combinational logic behaviorally.
always statements are used to describe sequential circuits because they remember the old state when no new state is prescribed
always statements can also be used to describe combinatorial logic behaviorally if the sensitivity list is written to respond to changes in all of the inputs and the body prescribes the output value for every possible input commination

## Slide 31: Inverter using always
module inv(input logic [3:0] a, output logic [3:0] y); always_comb y = ~a; endmodule
always_comb reevaluates the statements inside the always statement any time any of the signals on the right hand side of <= or = in the always statement change. In this case, it is equivalent to always @(a), but is better because it avoids mistakes if signals in the always statement are renamed or added. If the code inside the always block is not combinational logic, SystemVerilog will report a warning. always_comb is equivalent to always @(*), but is preferred in SystemVerilog. The = in the always statement is called a blocking assignment, in contrast to the <= nonblocking assignment. In SystemVerilog, it is good practice to use blocking assignments for combinational logic and nonblocking assignments for sequential logic.
SystemVerilog supports blocking and nonblocking assignments in an always statement
  A group of blocking assignments (represented with =) are evaluated in the order they appear in the code, similar to a standard programming language
  A group of nonblocking assignments (represented with <=) are evaluated concurrently. All the statements are evaluated before any of the signals in the left hand side are updated.
Notes: Do not confuse either type with continuous assignment using the assign statement. assign statements must be used outside always statements and are also evaluated concurrently.
<number>

## Slide 32: Full Adder revisited
module fulladder(input logic a, b, cin, output logic s, cout); logic p, g; always_comb begin p = a ^ b; // blocking g = a & b; // blocking s = p ^ cin; // blocking cout = g ¦ (p & cin); // blocking end endmodule
In this case, always @(a, b, cin) would have been equivalent to always_comb. However, always_comb is better because it avoids common mistakes of missing signals in the sensitivity list. It is best to use blocking assignments for combinational logic. This example uses blocking assignments, first computing p, then g, then s, and finally cout.
Do not confuse either blocking or nonblocking type with continuous assignment using the assign statement. assign statements must be used outside always statements and are also evaluated concurrently.

## Slide 33: case Statements
module sevenseg(input logic [3:0] data, output logic [6:0] segments); always_comb case(data) // abc_defg 0: segments = 7'b111_1110; 1: segments = 7'b011_0000; 2: segments = 7'b110_1101; 3: segments = 7'b111_1001; 4: segments = 7'b011_0011; 5: segments = 7'b101_1011; 6: segments = 7'b101_1111; 7: segments = 7'b111_0000; 8: segments = 7'b111_1111; 9: segments = 7'b111_0011; default: segments = 7'b000_0000; endcase endmodule
The case statement checks the value of data. When data is 0, the statement performs the action after the colon, setting segments to 1111110. The case statement similarly checks other data values up to 9 (note the use of the default base, base 10). The default clause is a convenient way to define the output for all cases not explicitly listed, guaranteeing combinational logic. In SystemVerilog, case statements must appear inside always statements.
case statement must appear inside an always/process statement.
The case statement performs different actions depending on the value of its input. A case statement implies combinational logic if all possible input combinations are defined; otherwise it implies sequential logic (because the output will keep its old value in the undefined cases).
Depending on used tools, the seven segment will most likely synthesize into a read-only memory (ROM) containing the 7 outputs for each of the 16 possible inputs.

## Slide 34: if Statements
module decoder3_8(input logic [2:0] a, output logic [7:0] y); always_comb case(a) 3'b000: y = 8'b00000001; 3'b001: y = 8'b00000010; 3'b010: y = 8'b00000100; 3'b011: y = 8'b00001000; 3'b100: y = 8'b00010000; 3'b101: y = 8'b00100000; 3'b110: y = 8'b01000000; 3'b111: y = 8'b10000000; default: y = 8'bxxxxxxxx; endcase endmodule
always statements may contain if statements. The if statement may be followed by an else statement. If all possible comninations of inputs are handled, the statement implies combinatorial logic. Otherwise it produces sequential logic. The default statement isn’t strictly necessary for logic synthesis in this case because all possible input combinations are defined, but it is prudent for simulation in case one of the inputs is an x or z.
Example: 3 bit to 8 bit decoder

## Slide 35: More if statement
module priorityckt(input logic [3:0] a, output logic [3:0] y); always_comb if (a[3]) y <= 4'b1000; else if (a[2]) y <= 4'b0100; else if (a[1]) y <= 4'b0010; else if (a[0]) y <= 4'b0001; else y <= 4'b0000; endmodule
In SystemVerilog, if statements must appear inside of always statements.
Example: 4 bit priority circuit – sets the output TRUE that corresponds to the most significant input that is TRUE

## Slide 36: Truth Tables with Don’t Cares
module priority_casez(input logic [3:0] a, output logic [3:0] y); always_comb casez(a) 4'b1???: y <= 4'b1000; 4'b01??: y <= 4'b0100; 4'b001?: y <= 4'b0010; 4'b0001: y <= 4'b0001; default: y <= 4'b0000; endcase endmodule
The casez statement acts like a case statement except that it also recognizes ? as don’t care.
Truth tables may include don’t care’s to allow more logic simplification.
Example shows how to describe a priority circuit with don’t cares.
Same circuit as in the previous example is being synthesized.

## Slide 37: Blocking and Nonblocking Assignments
1. Use always_ff @(posedge clk) and nonblocking assignments to model synchronous sequential logic.
always_ff @(posedge clk)
begin
n1 <= d; // nonblocking
q <= n1; // nonblocking
end
2. Use continuous assignments to model simple combinational logic.
assign y = s ? d1 : d0;
3. Use always_comb and blocking assignments to model more complicated combinational logic where the always statement is helpful.
always_comb
begin
p = a ^ b; // blocking
g = a & b; // blocking
s = p ^ cin;
cout = g | (p & cin);
end
4. Do not make assignments to the same signal in more than one always statement or continuous assignment statement.

## Slide 38: Finite State Machines Modeling
Recall that a finite state machine (FSM) consists of a state register and two blocks of combinational logic to compute the next state and the outputs given the current state and the input
Descriptions of state machines are correspondingly divided into three parts to:
  Model the state register
  Model the next state logic, and
  Model the output logic.

## Slide 39: Divide by 3 FSM
module divideby3FSM(input logic clk, input logic reset, output logic y); typedef enum logic [1:0] {S0, S1, S2} statetype; statetype [1:0] state, nextstate; // state register always_ff @(posedge clk, posedge reset) if (reset) state <= S0; else state <= nextstate; // next state logic always_comb case (state) S0: nextstate <= S1; S1: nextstate <= S2; S2: nextstate <= S0; default: nextstate <= S0; endcase // output logic assign y = (state== S0); endmodule
Synthesized circuit is represented with a block diagram and a state transition diagram for the state machine. It doesn’t show the logic gates or the inputs/outputs on arcs/states. It is an synthesis tool choice (Synplify Premier).
The typedef statement defines statetype to be a two-bit logic value with three possibilities: S0, S1, or S2. state and nextstate are statetype signals (two bit signals). The enumerated encodings default to numerical order: S0 = 00, S1 = 01, and S2 = 10. The encodings can be explicitly set by the user; however, the synthesis tool views them as suggestions, not requirements. Notice how a case statement is used to define the state transition table. Because the next state logic should be combinational, a default is necessary even though the state 2'b11 should never arise. The output, y, is 1 when the state is S0. The equality comparison a == b evaluates to 1 if a equals b and 0 otherwise. The inequality comparison a != b does the inverse, evaluating to 1 if a does not equal b.

## Slide 40: Pattern 01 Detector – Moore FSM
module patternMoore(input logic clk, input logic reset, input logic a, output logic y); typedef enum logic [1:0] {S0, S1, S2} statetype; statetype state, nextstate; // state register always_ff @(posedge clk, posedge reset) if (reset) state <= S0; else state <= nextstate; // next state logic always_comb case (state) S0: if (a) nextstate = S0; else nextstate = S1; S1: if (a) nextstate = S2; else nextstate = S1; S2: if (a) nextstate = S0; else nextstate = S1; default: nextstate = S0; endcase // output logic assign y = (state==S2); endmodule
Note how nonblocking assignments (<=) are used in the state register to describe sequential logic, whereas blocking assignments (=) are used in the next state logic to describe combinational logic.
Moore FSM – outputs depend only on the current state

## Slide 41: Pattern 01 Detector – Mealy FSM
module patternMealy(input logic clk, input logic reset, input logic a, output logic y); typedef enum logic {S0, S1} statetype; statetype state, nextstate; // state register always_ff @(posedge clk, posedge reset) if (reset) state <= S0; else state <= nextstate; // next state logic always_comb case (state) S0: if (a) nextstate = S0; else nextstate = S1; S1: if (a) nextstate = S0; else nextstate = S1; default: nextstate = S0; endcase // output logic assign y = (a & state==S1); endmodule
Mealy FSM – outputs depend on inputs and current state

## Slide 42: Signed vs Unsigned
// unsigned multiplier module multiplier(input logic [3:0] a, b, output logic [7:0] y); assign y =a * b; endmodule // signed multiplier module multiplier(input logic signed [3:0] a, b, output logic signed [7:0] y); assign y =a * b; endmodule
In SystemVerilog, signals are considered unsigned by default. Adding the signed modifier (e.g., logic signed [3:0] a) causes the signal a to be treated as signed.
Most operations such as addition, subtraction, and Boolean logic are identical whether a number is signed or unsigned.
However, magnitude comparison, multiplication, and arithmetic right shifts are performed differently for signed two’s complement numbers than for unsigned binary numbers. These operations will be examined in latter.
This example describes how to indicate that a signal represents a signed number.

## Slide 43: Parametrized Modules
So far all of our modules have had fixed-width inputs and outputs. For example, we had to define separate modules for 4bit and 8bit wide 2:1 multiplexers.
HDLs (including SystemVerilog) permit variable bit widths using parameterized modules

## Slide 44: Parametrized N-BIT 2:1 Mux
module mux2 #(parameter width = 8) (input logic [width–1:0] d0, d1, input logic s, output logic [width–1:0] y); assign y = s ? d1 : d0; endmodule
SystemVerilog allows a #(parameter . . . ) statement before the inputs and outputs to define parameters. The parameter statement includes a default value (8) of the parameter, in this case called width. The number of bits in the inputs and outputs can depend on this parameter.
module mux4_8(input logic [7:0] d0, d1, d2, d3, input logic [1:0] s, output logic [7:0] y); logic [7:0] low, hi; mux2 lowmux(d0, d1, s[0], low); mux2 himux(d2, d3, s[0], hi); mux2 outmux(low, hi, s[1], y); endmodule
The 8-bit 4:1 multiplexer instantiates three 2:1 multiplexers using their default widths.
module mux4_12(input logic [11:0] d0, d1, d2, d3, input logic [1:0] s, output logic [11:0] y); logic [11:0] low, hi; mux2 #(12) lowmux(d0, d1, s[0], low); mux2 #(12) himux(d2, d3, s[0], hi); mux2 #(12) outmux(low, hi, s[1], y); Endmodule
In contrast, a 12-bit 4:1 multiplexer, mux4_12, would need to override the default width using #( ) before the instance name, as shown below. Note: Do not confuse the use of the # sign indicating delays with the use of #(. . .) in defining and overriding parameters.
This example declares a parameterized 2:1 multiplexer with a default width of 8, then uses it to create 8bit and 12bit 4:1 multiplexers

## Slide 45: Parametrized N to 2N Decoder
module decoder #(parameter N = 3) (input logic [N–1:0] a, output logic [2**N–1:0] y); always_comb begin y = 0; y[a] = 1; end endmodule
2**N indicates 2N.
Example shows a decoder, which is an even better application of parameterized modules. A large N:2N decoder is cumbersome to specify with case statements, but easy using parameterized code that simply sets the appropriate output bit to 1.
Specifically, the decoder uses blocking assignments to set all the bits to 0, then changes the appropriate bit to 1.

## Slide 46: N input AND function
module andN #(parameter width = 8) (input logic [width–1:0] a, output logic y); genvar i; logic [width–1:0] x; generate assign x[0] = a[0]; for(i=1; i<width; i=i+1) begin: forloop assign x[i] = a[i] & x[i–1]; end endgenerate assign y = x[width–1]; endmodule
Produces an N input AND function from cascades of 2 input AND gates. The for statement loops thrugh i = 1, 2, … , width–1 to produce many consecutive AND gates. The begin in a generate for loop must be followed by a : and an arbitrary label (forloop, in this case).
HDLs also provide generate statements to produce a variable amount of hardware depending on the value of a parameter.
generate supports for loops and if statements to determine how many of what types of hardware to produce.

## Slide 47: Testbenches
A testbench is an HDL module that is used to test another module, called the device under test (DUT).
The testbench contains statements to apply inputs to the DUT and, ideally, to check that the correct outputs are produced.
The input and desired output patterns are called test vectors.

## Slide 48: Testbench for sillyfunction
module testbench1(); logic a, b, c, y; // instantiate device under test sillyfunction dut(a, b, c, y); // apply inputs one at a time initial begin a = 0; b = 0; c = 0; #10; c = 1; #10; b = 1; c = 0; #10; c = 1; #10; a = 1; b = 0; c = 0; #10; c = 1; #10; b = 1; c = 0; #10; c = 1; #10; end endmodule
The initial statement executes the statements in its body at the start of simulation. In this case, it first applies the input pattern 000 and waits for 10 time units. It then applies 001 and waits 10 more units, and so forth until all eight possible inputs have been applied. initial statements should be used only in testbenches for simulation, not in modules intended to be synthesized into actual hardware. Hardware has no way of magically executing a sequence of special steps when it is first turned on.
Consider testing the sillyfunction module that computes y = a’b’c’ + ab’c’ + ab’c. This is a simple module, so we can perform exhaustive testing by applying all eight possible test vectors.
The example herewith demonstrates a simple testbench. It instantiates the DUT, then applies the inputs. Blocking assignments and delays are used to apply the inputs in the appropriate order. The user must view the results of the simulation and verify by inspection that the correct outputs are produced. Testbenches are simulated the same as other HDL modules. However, they are not synthesizeable.

## Slide 49: Testbench with self checking
module testbench2(); logic a, b, c, y; // instantiate device under test sillyfunction dut(a, b, c, y); // apply inputs one at a time and checking results initial begin a = 0; b = 0; c = 0; #10; assert (y === 1) else $error("000 failed."); c = 1; #10; assert (y === 0) else $error("001 failed."); b = 1; c = 0; #10; assert (y === 0) else $error("010 failed."); c = 1; #10; assert (y === 0) else $error("011 failed."); a = 1; b = 0; c = 0; #10; assert (y === 1) else $error("100 failed."); c = 1; #10; assert (y === 1) else $error("101 failed."); b = 1; c = 0; #10; assert (y === 0) else $error("110 failed."); c = 1; #10; assert (y === 0) else $error("111 failed."); end endmodule
The SystemVerilog assert statement checks if a specified condition is true. If not, it executes the else statement. The $error system task in the else statement prints an error message describing the assertion failure. assert is ignored during synthesis.
Checking for correct outputs is tedious and error-prone. Moreover, determining the correct outputs is much easier when the design is fresh in your mind; if you make minor changes and need to retest weeks later, determining the correct outputs becomes a hassle. A much better approach is to write a self-checking testbench, shown in this example.
In SystemVerilog, comparison using == or != is effective between signals that do not take on the values of x and z. Testbenches use the === and !== operators for comparisons of equality and inequality, respectively, because these operators work correctly with operands that could be x or z.
Notes: In SystemVerilog, comparison using == or != is effective
between signals that do not take on the values of x and z.
Testbenches use the === and !== operators for comparisons of
equality and inequality, respectively, because these operators
work correctly with operands that could be x or z.
<number>

## Slide 50: Testbench with loading test vectors from file
module testbench3(); logic clk, reset; logic a, b, c, y, yexpected; logic [31:0] vectornum, errors; logic [3:0] testvectors[10000:0]; // instantiate device under test sillyfunction dut(a, b, c, y); // generate clock always begin clk = 1; #5; clk = 0; #5; end // at start of test, load vectors and pulse reset initial begin $readmemb("example.tv", testvectors); vectornum = 0; errors = 0; reset = 1; #27; reset = 0; end // apply test vectors on rising edge of clk always @(posedge clk) begin #1; {a, b, c, yexpected} = testvectors[vectornum]; end // check results on falling edge of clk always @(negedge clk) if (~reset) begin // skip during reset if (y ! == yexpected) begin // check result $display("Error: inputs = %b", {a, b, c}); $display(" outputs = %b (%b expected)", y, yexpected); errors = errors + 1; end vectornum = vectornum + 1; if (testvectors[vectornum] === 4'bx) begin $display("%d tests completed with %d errors", vectornum, errors); $finish; end end Endmodule
Testbench generates clockusing always statement. Although the clock and reset aren’t necessary to test combinational logic, they are included because they would be important to testing a sequential DUT
Writing code for each test vector also becomes tedious, especially for modules that require a large number of vectors. A better approach is to place the test vectors in a separate file. The testbench simply reads the test vectors from the file, applies the input test vector to the DUT, waits, checks that the output values from the DUT match the output vector, and repeats until reaching the end of the test vectors file.
Contents of example.tv that contains the inputs and expected outputs written in binary:
000_1
001_0
010_0
011_0
100_1
101_1
110_0
111_0
Notes: New inputs are applied on the rising edge of the clock, and the output
is checked on the falling edge of the clock. Errors are reported as they
occur. At the end of the simulation, the testbench prints the total number
of test vectors applied and the number of errors detected.
The testbench3 is overkill for such a simple circuit.
However, it can easily be modified to test more complex circuits by
changing the example.tv file, instantiating the new DUT, and changing a
few lines of code to set the inputs and check the outputs.
<number>

## Slide 51: Summary
Hardware description languages (HDLs) are extremely important tools for modern digital designers. Once you have learned SystemVerilog or VHDL, you will be able to specify digital systems much faster than if you had to draw the complete schematics.
The debug cycle is also often much faster, because modifications require code changes instead of tedious schematic rewiring.
However, the debug cycle can be much longer using HDLs if you don’t have a good idea of the hardware your code implies.
HDLs are used for both simulation and synthesis. Logic simulation is a powerful way to test a system on a computer before it is turned into hardware. Simulators let you check the values of signals inside your system that might be impossible to measure on a physical piece of hardware.
Logic synthesis converts the HDL code into digital logic circuits.
The most important thing to remember when you are writing HDL code is that you are describing real hardware, not writing a computer program.

## Slide 52: References
  „Digital Design and Computer Architecture“, David Harris & Sarah Harris, ISBN: 978-0-12-394424-5