## Slide 1: I/O Sub-System
CT101 – Computing Systems

## Slide 2: Contents
Overview
Peripheral Devices and IO Modules
Programmed I/O
Interrupt Driven I/O
DMA
Notes: <number>

## Slide 3: Overview
I/O devices are very different (i.e. keyboard and HDD performs totally different functions, yet they are both part of the I/O subsystem).
The interfaces between the CPU and I/O devices are very similar.
Each I/O device needs to be connected to:
  Address bus – to pass address to peripheral
  Data bus – to pass data to and from peripheral
  Control bus – to control signals to peripherals

## Slide 4: Problems
Wide variety of peripherals
  Delivering different amounts of data
  At different speeds
  In different formats
All slower than CPU and RAM
Need I/O modules
  Interface with the processor and memory via system buses or central switch
  Interface to one or more peripheral devices using specific data links/interfaces

## Slide 5: I/O Module
Interface to CPU and Memory
Interface to one or more peripherals

## Slide 6: Peripheral Devices Types & Block Diagram
Human readable
  Screen, printer, keyboard
Machine readable
  Monitoring and control
Communication
  Modem
  Network Interface Card (NIC)
Notes: <number>

## Slide 7: More about I/O Modules
I/O Module Functions
Control & Timing
CPU Communication
Device Communication
Data Buffering
Error Detection
I/O CPU Steps
CPU checks I/O module device status
I/O module returns status
If ready, CPU requests data transfer
I/O module gets data from device
I/O module transfers data to CPU
Variations for output, DMA, etc.

## Slide 8: I/O Module Diagram & Design Decisions
Hide or reveal device properties to CPU
Support multiple or single device
Control device functions or leave for CPU
Also O/S decisions
  e.g. Unix treats everything it can as a file
Notes: <number>

## Slide 9: I/O Mapping
Memory mapped I/O
  Devices and memory share an address space
  I/O looks just like memory read/write
  No special commands for I/O
    Large selection of memory access commands available
Isolated I/O
  Separate address spaces
  Need I/O or memory select lines
  Special commands for I/O
  Special CPU control signals
  Devices and Memory can have overlapping adresses
Notes: <number>

## Slide 10: Addressing I/O Devices
I/O data transfer is very like memory access (CPU viewpoint)
Each device given unique identifier
CPU commands contain identifier (address)
The IO Module should contain address decoding logic
Notes: <number>

## Slide 11: Input Devices
When the values of the address/control buses are correct (the I/O device is addressed) the buffers are enabled and the data passes on to the data bus; the CPU reads this data
When the conditions are not right, the logic bloc (enable logic) will not enable the buffers; no data on the data bus
The example shows an I/O device mapped at address 1111 0000 on a computer with 8 bit address bus and RD and IO/M’ control signals
Notes: <number>
The key to this design is the enable logic. Just as every memory location has a unique address, each I/O device has also a unique address. The enable logic should not enable the buffers unless it receives the correct address from the data bus. For an input device, RD and IO/M’ signals must be asserted (in systems which isolates I/O devices)

## Slide 12: Output Devices
Since the output devices read data from the data bus, they don’t need the buffers; data will be made available to all the devices
Only the correctly decoded one (addressed) will read in the data
Example shows an output device mapped at 11110000 address in a 8 bit address bus computer, with WR and IO/M’ signals
Notes: <number>
Some variations of this design include buffers instead of the registers. The limitation there is that the output device has to read the data while the buffers are enabled, otherwise it will loose the data.

## Slide 13: Bidirectional Devices (1)
Bidirectional devices require actually two interfaces, one for input and the other for output.
Same gates could be used to generate the enable signal (for both the tri state buffers and the registers); the difference between read and write are made through the control signals (RD, WR)
The example shows a combined interface for 1111 0000 address.
Notes: <number>
Some devices are used for both input and output (i.e. a HDD in a Personal Computer)

## Slide 14: Bidirectional Devices (1)
In real systems, we need to access more than just one output and one input data register
Usually peripherals are issued with commands by the processor and they take some action and in response present data
Up to how the processor knows if the peripheral device is ready after a command, we can have:
  Programmed I/O (or also known as Polled I/O)
  Interrupt driven I/O

## Slide 15: Input / Output Techniques

## Slide 16: Programmed I/O
Overview
CPU has direct control over I/O
  Sensing status
  Read/write commands
  Transferring data
CPU waits for I/O module to complete operation
Wastes CPU time
Operations
CPU requests I/O operation
I/O module performs operation
I/O module sets status bits
CPU checks status bits periodically
I/O module does not inform CPU directly
I/O module does not interrupt CPU
CPU may wait or come back later

## Slide 17: Interrupt Driven I/O
Overview
Overcomes CPU waiting
No repeated CPU checking of device
I/O module interrupts when ready
Operations
CPU issues read command
I/O module gets data from peripheral whilst CPU does other work
I/O module interrupts CPU
CPU requests data
I/O module transfers data

## Slide 18: Simple Interrupt Processing

## Slide 19: CPU Viewpoint
Issue read command
Do other work
Check for interrupt at end of each instruction cycle
If interrupted:
  Save context (registers)
  Process interrupt
    Fetch data & store
  Restore context (registers)
Notes: <number>

## Slide 20: Changes in Memory and Registers for an Interrupt
Notes: <number>

## Slide 21: Design Issues
How do you identify the module issuing the interrupt?
How do you deal with multiple interrupts?
  i.e. an interrupt handler being interrupted
Notes: <number>

## Slide 22: Identifying Interrupting Module
Different line for each module
  Limits number of devices
Software poll
  CPU asks each module in turn
  Slow
Daisy Chain or Hardware poll
  Interrupt Acknowledge sent down a chain
  Module responsible places vector on bus
  CPU uses vector to identify handler routine
Bus Arbitration (e.g. PCI & SCSI)
  Module must claim the bus before it can raise interrupt, thus only one module can rise the interrupt at a time
  When processor detects interrupt, processor issues an interrupt acknowledge
  Device places its vector on the data bus
Notes: <number>

## Slide 23: Multiple Interrupts
Each interrupt line has a priority
Higher priority lines can interrupt lower priority lines
Interrupt_Handler
saveProcessorState();
for (i=0; i<Number_of_devices; i++)
if (device[i].done ==1) goto device_handler(i);
/* If here, then something went wrong*/
Unified Interrupt Handling Example
Notes: <number>

## Slide 24: Direct Memory Access
Interrupt driven and programmed I/O require active CPU intervention
  Transfer rate is limited by the speed of processor testing and servicing a device
  CPU is tied up in managing an I/O transfer. A number of instructions must be executed for each I/O transfer.
DMA is the answer when large amounts of data need to be transferred.
Notes: <number>

## Slide 25: DMA Function and Module
DMA controller able to mimic the CPU and take over for I/O transfers
CPU tells DMA controller:
  Operation to execute
  Device address involved in the I/O operation (sent on data lines)
  Starting address of memory block for data (sent on data lines) and stored in the DMA address register
  Amount of data to be transferred (sent on data lines) and stored into the data count
CPU carries on with other work
DMA controller deals with transfer
DMA controller sends interrupt when finished

## Slide 26: DMA Transfer Cycle Stealing
DMA controller takes over bus for a cycle
Transfer of one word of data
Not an interrupt
  CPU does not switch context
CPU suspended just before it accesses bus
  i.e. before an operand or data fetch or a data write
Slows down CPU but not as much as CPU doing transfer
Notes: <number>

## Slide 27: DMA and Interrupt Breakpoints During an Instruction Cycle

## Slide 28: Q
What effect does processor caching have on DMA?
Notes: <number>

## Slide 29: DMA Configurations (1)
Single Bus, Detached DMA controller
Each transfer uses bus twice
  I/O to DMA then DMA to memory
CPU may be suspended twice
Notes: <number>

## Slide 30: DMA Configurations (2)
Single Bus, Integrated DMA controller
Controller may support >1 device
Each transfer uses bus once
  DMA to memory
CPU may be suspended once
Notes: <number>

## Slide 31: DMA Configurations (3)
Separate I/O Bus
Bus supports all DMA enabled devices
Each transfer uses bus once
  DMA to memory
CPU may be suspended once
Notes: <number>

## Slide 32: DMA Operation Example
Separate I/O Bus

## Slide 33: References
“Computer Systems Organization & Architecture”, John D. Carpinelli, ISBN: 0-201-61253-4
“Computer Organization and Architecture”, William Stallings, 8th Edition

## Slide 34
Additional slides

## Slide 35: 82C59A Interrupt Controller
Intel x86 processors have only one interrupt request line and one interrupt acknowledge line, thus they require an external interrupt controller
82C59A supports 8 sources of interrupt and can be configured as stand alone or in a master/slave configuration
Sequence of events:
  82C59A accepts interrupt requests from modules, determines which has priority, signals the processor (INTR).
  Processor acknowledges (INTA).
  82C59A will place vector information on data bus as a response to INTA.
  Processor proceeds to handle the interrupt and communicates directly with the I/O module that generated the interrupt
82C59A is programmable by the processor. The processor decides what is the interrupt schema out of few possible:
  Fully nested – interrupts are served according to priority from 0 (INT0) to 7 (INT7)
  Rotating – after being serviced, a device is placed into the lowest priority in the group
  Special masks – processor can inhibit certain priorities from certain devices
Notes: <number>

## Slide 36: Intel 82C55A I/O Module
24 I/O programmable lines by means of control registers
  3 8 bit groups ABC
  Group C is further divided into Ca and Cb subgroups that can be used in conjunction with A and B ports
D0-D7 bidirectional data I/F with x86 processor
A0,A1 specify one of the three I/O ports or control register for data transfer
A transfer takes place only when CS is enabeld together with either Read or Write

## Slide 37: Keyboard/Display Interfaces to 82C55A
Group C signals are used for interrupt request and handshacking
  Data Ready Line used to indicate that the data is reay on the I/O lines
  Acknowledge is used to indicate to the device that it can reuse the I/O lines (clear and/or place new data on them)
  Interrupt request tied to the system interrupt controller
Note that two of the 8 bit inputs from the keyboard/display are special purpose pins. However, they will be treated as normal signals by the I/O module. They will only be interpreted by the Keyboard/Display driver.