## Slide 1: Introduction to Computing Systems
CT101 – Computing Systems
Notes: <number>

## Slide 2: Computing Systems in a Nutshell
 | Application Software
 | Operating Systems
 | CPU Architecture & Microarchitecture
 | Sequential & Combinatorial Digital Logic
 | Physics & Devices

## Slide 3: Input -> Process -> Output model
Computer system is suppose to perform a useful operation, such as word processing, retrieval and manipulation of data, bookkeeping, etc.
  i.e. a credit card transaction operation
Regardless of the type of operation to be performed, the work of a computer can be characterized as an input->process->output model:
  the program retrieves input from a disk file, mouse, keyboard or other type of input,
  processes the input
  produces the output to a disk, terminal, printer or some other type of output device
All of the above operations are repetitive in nature
Notes: <number>

## Slide 4
File Edit Workflow
Notes: <number>

## Slide 5: Computing System Components
Hardware – provides the physical mechanisms to input and output data, manipulating data and controlling the various input, output, storage and communication components
Software – both application and system, which provides instructions that tell the hardware exactly what tasks are to be performed and in what order
Data being manipulated – can be alphanumeric, graphic or any other form. In all cases it is represented in a form that the computer will understand and manipulate
Notes: <number>

## Slide 6: Architecture versus Organization
Architecture
  Refers to those attributes of a system visible to a programmer
    The architecture of a CPU is actually its instruction set, number of bits used for data representation, addressing techniques, etc…
Organization
  Refers to the operational units and their interconnections that realize the architectural specifications
    Hardware details transparent to the programmer, such as control signals between different functional units, memory type (i.e. dynamic RAM or static RAM, etc…), registers type (static or dynamic), etc..
It is an architectural issue whether a computer will have or not a specific instruction (i.e. multiply), but it is an organization issue whether that instruction will be implemented by a special arithmetic unit or it will be implemented using the adder of the system by repetitive add operations
Notes: <number>
In the computing world, a distinction is often made between computer architecture and computer organization. It is somewhat difficult to give precise definitions, but a consensus exists about the area covered by each.
Architecture
  Refers to those attributes of a system visible to a programmer or in other words, those attributes that have a logical impact on the execution of a program
  The architecture of a CPU is actually its instruction set, number of bits used for data representation, addressing techniques, etc…
Organization
  Refers to the operational units and their interconnections that realize the architectural specifications
  Hardware details transparent to the programmer, such as control signals between different functional units, memory type (i.e. dynamic RAM or static RAM, etc…), registers type (static or dynamic), etc..

## Slide 7: Computing Systems Description
Top down approach
  starting from a top view and decomposing the system into its subparts
Bottom up approach
  starting from the bottom and building up a complete description
Top-down approach seem to be the clearest and most effective.
  However we will use both approaches trying to apply the best approach to a specific area

## Slide 8: Structure versus Function
Computing systems are complex machines made out of millions and millions of different components.
  How can one clearly describe them??
  The key is to recognize the hierarchical nature of most complex systems, including the computer.
  Hierarchical system organized in a number of levels. Each level is characterized by structure and function:
Structure: the way the components are interconnected
Function: the operation of each individual component as part of the structure
Notes: <number>
Computing systems are complex machines made out of millions and millions of different components. How can one clearly describe them?? The key is to recognize the hierarchical nature of most complex systems, including the computer.
The hierarchical nature of a system is important at both their design and their description. The designer need only to deal with a particular level at a time. At each level, the designer is concerned with structure and function

## Slide 9: Computing Systems Function
Data Processing
  Fundamental types of data
  Fundamental types of processing
Data Storage
  Short term storage
  Long term storage
Data Movement
  Input/Output for devices directly connected (peripherals)
  Data communication for moving data over long distances
Control
  External (users)
  Internal (manage resources)
Notes: <number>
The computer should be able to process the data. The data may take a wide variety of forms and the range of processing requirements is broad. However, we shall see that there are only fundamental methods or types of data processing.
It is essential that a computer is able to store data. Even if the computer is processing data on the fly, then the computer must store at least those pieces of data that are worked at any given moment during the processing time. Therefore, there is at least short term data storage function. Equally important, the computer performs a long term data storage function. Files or data are stored on the computer for subsequent retrieval and update.
The computer must be able to move data between itself and the outside world. The computer’s operating system environment consists of devices that servers as either sources or destinations of data. When data is received from or delivered to a device that is directly connected to a computer, the process is known as Input/output, and the device is known as a peripheral. If data is moved over long distances, the process is known as data communication.
There must be a control of those functions. Two types of control is involved: control from individuals (who provide the computing system with instructions of what to perform) and internal control (control unit manages the computer’s internal resources and internal components in response to instructions from the individuals).

## Slide 10: Computing System Structure
Notes: <number>
There are four main structural components:
Central Processing Unit – or processor, controls the operation of the computer and performs its data processing functions
Main Memory – stores data
Input/Output – moves data between the computer and its external environment
System Bus – or system interconnection consists of set of tracks or electrical wires, with a certain organization that provides communication between CPU, main memory and I/O
In a computing system there may be one or more of the above enumerated components. Traditionally in a computing system used to be just one CPU, but modern computers may could have two or more CPUs.
Each of those components will be examined in detail during this course. However, the most interesting and complex is the CPU.

## Slide 11: CPU Structure
Notes: <number>
The major components of the CPU are the following;
Control Unit – controls the operation of the CPU
Arithmetic and Logic Unit – ALU performs the computer’s data processing functions
Registers – provide storage internal to the processor or CPU
CPU Bus – interconnections that provide for communication among CPU, ALU and registers

## Slide 12: Computing Systems Software
Application software
  Performs specific tasks for users: spreadsheets, database systems, desktop publishing, program development, games, etc…
System software
  Provides infrastructure for application software
  Consists of operating system and utility software
Notes: <number>

## Slide 13: Operating System Components
kernel
Memory
Manager
File
Manager
Device I/O
Manager
User Interface
Application Programming Interface
Notes: <number>
User Interface – allows the user to execute programs, enter commands, manipulate files, etc.. It also does the output presentation on the display. On some systems, the output might be only text, but more likely, the output system is represented by a windows based system.
Application Programming Interface – acts as in interface for application programs and utilities to access the internal services provided by the operating system. Those includes file services, I/O services, data communication services, user interface services, program execution services and many more.
Kernel – is the core of the operating system. In conjunction with Memory Manager provides memory management services (by locating and allocating memory space to programs that need it), schedules time for each application to execute, manages and arranges services and resources that are provided by other modules and provides communication between the other modules and processes.
File Manger – allocates and manages secondary storage space and translates file requests from their name-based from into specific device I/O requests. The actual storage and retrieval of the files is performed by the I/O drivers that comprise the I/O component. Each I/O driver controls one or more hardware devices of similar type.
The operating system is almost always stored on a hard-disk, but there are also exceptions. For instance, for embedded systems, the operating system is actually provided in a ROM (Read Only Memory) storage. In other cases, the operating system may be loaded from a network resource. In both cases, the IPL (Initial Program Load) is stored locally. Once this is loaded, it provides tools to test and load the remainder of the operating system from the disk, ROM or network.

## Slide 14: Review Question 1
Architecture of a CPU refers to:
  Instruction set and way of interaction with the programmer
  Details on how the instructions are implemented
  Details on how various subsystems (Arithmetic and Logic Unit, Registers and Control Unit) are interconnected
  I don’t know

## Slide 15: Review Question 2
Out of a few possible options below, identify one that is NOT a function of a computing system
  Data storage
  Power consumption
  Data processing
  Data movement

## Slide 16: Review Question 3
Out of the possible options below, identify the one that is NOT part of a computing system structure
  CPU
  Memory
  Buses
  Data

## Slide 17: References
“The Architecture of Computer Hardware and Systems Software”, Irv Englander, ISBN: 0-471-36209-3
“Computer Systems”, J Stanley Warford, ISBN: 0-7637-16633-2
Notes: <number>