## Slide 1: Memory Sub-System
CT101 – Computing Systems

## Slide 2: Memory Subsystem
Memory Hierarchy
Types of memory
Memory organization
Memory Hierarchy Design
Cache

## Slide 3: Memory Hierarchy
Registers
  In CPU
Internal or Main memory
  May include one or more levels of cache
  “RAM”
External memory
  Backing store
Notes: <number>

## Slide 4: Internal Memory Types
Memory Type | Category | Erasure | Write Mechanism | Volatility
Random-access memory (RAM) | Read-write memory | Electrically, byte-level | Electrically | Volatile
Read-only memory (ROM) | Read-only memory | Not possible | Masks | Nonvolatile
Programmable ROM (PROM) |  |  | Electrically | 
Erasable PROM (EPROM) | Read-mostly memory | UV light, chip-level |  | 
Electrically Erasable PROM (EEPROM) |  | Electrically, byte-level |  | 
Flash memory |  | Electrically, block-level |  | 

## Slide 5: External Memory Types
HDD
  Magnetic Disk(s)
  SDD (Solid State Disk(s))
Optical
  CD-ROM
  CD-Recordable (CD-R)
  CD-R/W
  DVD
Magnetic Tape
Notes: <number>

## Slide 6: Random Access Memory (RAM)
Misnamed as all semiconductor memory is random access
Read/Write
Volatile
Temporary storage
Static or dynamic

## Slide 7: Types of RAM
Dynamic RAM (DRAM) – are like leaky capacitors; initially data is stored in the DRAM chip, charging its memory cells to maximum values. The charge slowly leaks out and eventually would go to low to represent valid data; before this happens, a refresh circuitry reads the contents of the DRAM and rewrites the data to its original locations, thus restoring the memory cells to their maximum charges
Static RAM (SRAM) – is more like a register; once the data has been written, it will stay valid, it doesn’t have to be refreshed. Static RAM is faster than DRAM, also more expensive. Cache memory in PCs is constructed from SRAM memory.

## Slide 8: Dynamic RAM
Bits stored as charge in capacitors
  Charges leak
  Need refreshing even when powered
Simpler construction
Smaller per bit than SRAM
  Less expensive
Need refresh circuits
Slower
Used for main memory in computing systems
Essentially analogue
  Level of charge determines value
Notes: <number>

## Slide 9: DRAM Structure & Operation
Address line active when bit read or written
  Transistor switch closed (current flows)
Write
  Voltage to bit line
    High for 1 low for 0
  Then signal address line
    Transfers charge to capacitor
Read
  Address line selected
    transistor turns on
  Charge from capacitor fed via bit line to sense amplifier
    Compares with reference value to determine 0 or 1
  Capacitor charge must be restored

## Slide 10: DRAM Refreshing
Refresh circuit included on chip
  Disable memory array chip
  Count through rows and select each in turn
  Read contents & write it back (restore)
Takes time
Slows down apparent performance
Notes: <number>

## Slide 11: Static RAM
Bits stored as on/off switches
No charges to leak
No refreshing needed when powered
More complex construction
Larger per bit
  More expensive
Does not need refresh circuits
Faster
  Cache
Digital
  Uses flip-flops
Notes: <number>

## Slide 12: Static RAM Structure & Operation
Transistor arrangement gives stable logic state
State 1
  C1 high, C2 low
  T1 T4 off, T2 T3 on
State 0
  C2 high, C1 low
  T2 T3 off, T1 T4 on
Address line transistors T5 T6 is switch
Write – apply value to B & compliment to B
Read – value is on line B

## Slide 13: SRAM v DRAM
Both volatile
  Power needed to preserve data
Dynamic cell
  Simpler to build, smaller
  More dense
  Less expensive
  Needs refresh
  Larger memory units
Static
  Faster
  Cache

## Slide 14: Read Only Memory (ROM)
Provides permanent storage (nonvolatile)
Used for: microprogramming, library subroutines (code) and constant data, systems programs (BIOS for PC or entire application + OS for certain embedded systems)
Types
  Written during manufacture (very expensive for small runs)
  Programmable (once) PROM (needs special equipment to program)
  Read “mostly”
    Erasable Programmable (EPROM) - Erased by UV
    Electrically Erasable (EEPROM) - Takes much longer to write than read
    Flash memory - Erase whole memory electrically
Notes: <number>

## Slide 15: Internal linear organization
8X2 ROM chip
As the number of locations increases, the size of the address decoder needed, becomes very large
Multiple dimensions of decoding can be used to overcome this problem

## Slide 16: Internal two-dimensional organization
High order address bits (A2A1) select one of the rows
The low order address bit selects one of the two locations in the row

## Slide 17: Memory Subsystems Organization (1)
Two or more memory chips can be combined to create memory with more bits per location (two 8X2 chips can create a 8X4 memory)

## Slide 18: Memory Subsystems Organization (2)
Two or more memory chips can be combined to create more locations (two 8X2 chips can create 16X2 memory)

## Slide 19: Memory Hierarchy Design (1)
Since 1987, microprocessors performance improved 55% per year and 35% until 1987
This picture shows the CPU performance against memory access time improvements over the years
  Clearly there is a processor-memory performance gap that computer architects must take care of

## Slide 20: Memory Hierarchy Design (2)
It is a tradeoff between size, speed and cost and exploits the principle of locality.
Register
  Fastest memory element; but small storage; very expensive
Cache
  Fast and small compared to main memory; acts as a buffer between the CPU and main memory: it contains the most recent used memory locations (address and contents are recorded here)
Main memory is the RAM of the system
Disk storage - HDD

## Slide 21: Memory Hierarchy Design (3)
Comparison between different types of memory
size:
speed:
$/Mbyte:
32 - 256 B
1-2 ns
Register
Cache
Memory
32KB - 4MB
2-4 ns
$20/MB
1000 MB
60 ns
$0.2/MB
1000 GB
6-8 ms
$0.001/MB
larger, slower, cheaper
HDD

## Slide 22: Memory Hierarchy Design (4)
Where can a block be placed in the upper level?
  BLOCK PLACEMENT
How is a block found if it is in the upper level?
  BLOCK IDENTIFICATION
Which block should be replaced on a miss?
  BLOCK REPLACEMENT
What happens on a write?
  WRITE STRATEGY

## Slide 23: Cache (1)
Is the first level of memory hierarchy encountered once the address leaves the CPU
  Since the principle of locality applies, and taking advantage of locality to improve performance is so popular, the term cache is now applied whenever buffering is employed to reuse commonly occurring items
We will study caches by trying to answer the four questions for the first level of the memory hierarchy

## Slide 24: Cache (2)
Every address reference goes first to the cache;
  If the desired address is not here, then we have a cache miss; The contents are fetched from main memory into the indicated CPU register and the content is also saved into the cache memory
  If the desired data is in the cache, then we have a cache hit; The desired data is brought from the cache, at very high speed (low access time)
Most software exhibits temporal locality of access, meaning that it is likely that same address will be used again soon, and if so, the address will be found in the cache
Transfers between main memory and cache occur at granularity of cache lines or cache blocks, around 32 or 64 bytes (rather than bytes or processor words). Burst transfers of this kind receive hardware support and exploit spatial locality of access to the cache (future access are often to address near to the previous one)

## Slide 25: Cache Organization

## Slide 26: Cache/Main Memory Structure

## Slide 27: Where can a block be placed in Cache? (1)
Our cache has eight block frames and the main memory has 32 blocks
Notes: <number>
Real caches contain hundreds of block frames and real memories contain millions of blocks. Those numbers are chosen for simplicity.
Assume that there is nothing in the cache and the block address in question (address that is accessed by processor falls within the block address number 12 in the main memory), then we can have three types of caches (from a block placement point of view):
Fully associative – where block 12 from the lower level memory can go into any of 8 block frames of the cache
Direct mapped – where block 12 from the lower level memory can go only into block frame 4 (12 mod 8)
Set associative – where block 12 from the lower level memory can go anywhere into set 0 (12 mod 4, if our memory has four sets). With two blocks per set, that means that the block 12 can go anywhere into block frame 0 or block frame 1 of the cache

## Slide 28: Where can a block be placed in Cache? (2)
Direct mapped Cache
  Each block has only one place where it can appear in the cache
  (Block Address) MOD (Number of blocks in cache)
Fully associative Cache
  A block can be placed anywhere in the cache
Set associative Cache
  A block can be placed in a restricted set of places into the cache
  A set is a group of blocks into the cache
  (Block Address) MOD (Number of sets in the cache)
    If there are n blocks in the cache, the placement is said to be n-way set associative

## Slide 29: How is a Block Found in the Cache?
Caches have an address tag on each block frame that gives the block address. The tag is checked against the address coming from CPU
  All tags are searched in parallel since speed is critical
  Valid bit is appended to every tag to say whether this entry contains valid addresses or not
Address fields:
  Block address
    Tag – compared against for a hit
    Index – selects the set
  Block offset – selects the desired data from the block
Set associative cache
  Large index means large sets with few blocks per set
  With smaller index, the associativity increases
Full associative cache – index field is not existing
Notes: <number>
The comparison can be made on the full address, but there is no need because of the following:
Checking the index would be redundant, since it was used to select the set to be checked. For instance, an address stored in set 0, must have 0 in the index field or it couldn’t have been stored in set 0
The offset is unnecessary in the comparison since the entire block is present or not in the cache, so all the block offsets should match.

## Slide 30: Which Block should be Replaced on a Cache Miss?
When a miss occurs, the cache controller must select a block to be replaced with the desired data
  Benefit of direct mapping is that the hardware decision is much simplified
Two primary strategies for full and set associative caches
  Random – candidate blocks are randomly selected
    Some systems generate pseudo random block numbers, to get reproducible behavior useful for debugging
  LRU (Least Recently Used) – to reduce the chance that information that has been recently used will be needed again, the block replaced is the least-recently used one.
    Accesses to blocks are recorded to be able to implement LRU

## Slide 31: What Happens on a Write?
Two basic options when writing to the cache:
  Writhe through – the information is written to both, the block in the cache an the block in the lower-level memory
  Write back – the information is written only to the cache
    The modified block of cache is written back into the lower-level memory only when it is replaced
To reduce the frequency of writing back blocks on replacement, an implementation feature called dirty bit is commonly used.
  This bit indicates whether a block is dirty (has been modified since loaded) or clean (not modified). If clean, no write back is involved

## Slide 32: Alpha Processors Cache Example
1 – the address comes from the CPU, being divided into 29 bit block address and 5 bit offset. The block address is further divided into 21 bit tag and 8 bit index
2 – the cache index selects the tag to be tested to see if the desired block is in the cache. The size of the index depends on the cache size, block size and the set associativity
3 – after reading the tag from the cache, it is compared with the tag from the address from the CPU. The valid bit must be set, otherwise, the result of comparison is ignored.
4 – assuming the tag does match, the final step is to signal the CPU to load the data from the cache.
Notes: <number>
8KB cache direct mapped with 32byte blocks.
1 – the address comes from the CPU, being divided into 29 bit block address and 5 bit offset. The block address is further divided into 21 bit tag and 8 bit index
2 – the cache index selects the tag to be tested to see if the desired block is in the cache. The size of the index depends on the cache size (8KB in our case), block size (32 byte blocks) and the set associativity (direct mapped = 1)
3 – after reading the tag from the cache, it is compared with the tag from the address from the CPU. The valid bit must be set, otherwise, the result of comparison is ignored.
4 – assuming the tag does match, the final step is to signal the CPU to load the data from the cache.
The alpha processor is using a write through technique for writing. The first three steps are the same. If a match, then the processor will write in both places, cache and the write buffer. The write buffer is used to cache multiple writes, so the write process would be more efficient.

## Slide 33: References
“Computer Architecture – A Quantitative Approach”, John L Hennessy & David A Patterson, ISBN 1-55860-329-8
“Computer Systems Organization & Architecture”, John D. Carpinelli, ISBN: 0-201-61253-4
“Computer Organization and Architecture”, William Stallings, 8th Edition

## Slide 34
Additional slides

## Slide 35: Detailed Direct Mapping Example
Cache of 64kByte
Cache block of 4 bytes
  i.e. cache is 16k (214) lines of 4 bytes
16MBytes main memory
  24 bit address (224=16M)
Address is in two parts
  Least Significant w bits identify unique word
  Most Significant s bits specify one memory block
  The MSBs are split into a cache line field r and a tag of s-r (most significant)

## Slide 36: Direct Mapping Example - Address Structure
Tag s-r
Line (Index) r
Word w
8
14
2
24 bit address
  2 bit word identifier (4 byte block)
  22 bit block identifier
    8 bit tag (=22-14)
    14 bit slot or line
No two blocks in the same line have the same Tag field
Check contents of cache by finding line and checking Tag
Notes: <number>

## Slide 37: Direct Mapping Cache Organization
Mapping function
i = j mod m
Notes: <number>
I = cache line number
M = Number of lines in the cache
J = Main memory block number

## Slide 38: Direct Mapping Example
Notes: <number>

## Slide 39: Detailed Fully Associative Mapping Example
Cache of 64kByte
  Cache block of 4 bytes
  i.e. cache is 16k (214) lines of 4 bytes
16MBytes main memory
  24 bit address (224=16M)
A main memory block can load into any line of cache
Memory address is interpreted as tag and word
  Tag uniquely identifies block of memory
  Every line’s tag is examined for a match
Cache searching gets expensive
Notes: <number>

## Slide 40: Fully Associative Mapping Example - Address Structure
Tag 22 bit
Word
2 bit
22 bit tag stored with each 32 bit block of data
Compare tag field with tag entry in cache to check for hit
Least significant 2 bits of address identify which word is required from 32 bit data block
e.g.
  Address Tag Data Cache line
  FFFFFC FFFFFC 0x24682468 3FFF
Notes: <number>

## Slide 41: Fully Associative Cache Organization
Notes: <number>

## Slide 42: Associative Mapping Example
Notes: <number>

## Slide 43: Detailed Set Associative Mapping Example
Cache of 64kByte
  Cache block of 4 bytes
  i.e. cache is 16k (214) lines of 4 bytes
16MBytes main memory
  24 bit address (224=16M)
Cache is divided into a number of sets (v)
  Each set contains a number of lines (k)
A given block maps to any line in a given set
  e.g. Block B can be in any line of set i
Mapping function
  i = j mod v (where total lines in the cache m = v * k)
    J – main memory block
    I – cache set number
e.g. 2 lines per set
  2 way associative mapping (k = 2)
  A given block can be in one of 2 lines in only one set
Notes: <number>

## Slide 44: Example Set Associative Mapping - Address Structure
Use set field to determine cache set to look in
Compare tag field to see if we have a hit
e.g
  Address Tag Data Set
  1FF 7FFC 1FF 12345678 1FFF
  001 7FFC 001 11223344 1FFF
Tag 9 bit
Set (Index) 13 bit
Word
2 bit
Notes: <number>

## Slide 45: K-Way Set Associative Cache Organization
Notes: <number>

## Slide 46: Two Way Set Associative Mapping Example
Notes: <number>