## Slide 1: Sequential Logic Design
CT101 – Computing Systems Organization

## Slide 2: Contents
Basic Sequential Components
  FlipFlop, Latches, Counters
Programmable Logic Devices
  PLD, PLA, CPLDs & FPGAs
Finite State Machine Model
  Generic Model
  Synchronous Model
  Mealy & More FSMs

## Slide 3: Overview
The most fundamental sequential components are the latch and flip-flop
They store one bit of data and make it available to other components
The main difference between a latch and a flip-flop is that the first are level triggered and the latter are edge triggered
Flip-flops and latches have a clock input

## Slide 4: Clock
It is usually derived from an oscillator or other circuitry that alternates its output between 1 and 0
It is used to synchronize the flow of data in a digital system

## Slide 5: D flip-flop
Flip-flop:
  One data input D
  When the clock input changes from 0 to 1 (positive edge), the data on the D input is loaded
  The data is made available via output Q and its complement via Q’
  Some variations have also a load signal (LD) that has to be high (active) in order for data to be loaded into the flip-flop
Notes: <number>
Flip-flop:
  One data input D
  When the clock input changes from 0 to 1 (positive edge), the data on the D input is loaded
  The data is made available via output Q and its complement via Q’
  Some variations have also a load signal (LD) that has to be high (active) in order for data to be loaded into the flip-flop
Please note in the truth table that the output changes on the rising edge of the clock (when the clock makes its transition from 0 to 1). Also note that Q0 represents that Q retains its previous value, regardless of whether that value was 0 or 1.
This type of flip-flop is called positive edge triggered because its output changes only on the rising (positive) edge of the clock.

## Slide 6: D latch
Positive level triggered latch
  It loads data as long as both its clock and load signals are 1. If both are one, the value of data D is passed to the Q output. If D changes while clock and load are 1, then the output changes accordingly
  If either the clock or load signals go to 0, the Q value is latched and held

## Slide 7: D latch with clear/set capabilities
Some variants of D latch and flip-flops have asynchronously set and clear capabilities – they can be set and clear regardless of the value of the other inputs to the latch (including the clock and load inputs)

## Slide 8: SR latch
The S input sets the latch to 1 and the R input resets the latch to 0
  When both S and R are 0 the output remains unchanged
Doesn’t have a clock input
  Only sequential component without a clock input
  The output of the latch is undefined when both the S and R are 1; the designer has to ensure that S and R inputs are never set to 1

## Slide 9: JK flip-flop
Resolves the problem of undefined outputs associated with SR latch
  J=1 sets the output to 1 and K=1 resets the output to 0. JK=11 inverts the stored current value of the output
It is often used instead of SR latch

## Slide 10: T (toggle) flip-flop
The T input doesn’t specify a value for its output, it specifies only whether or not the output should be changed
On the rising edge of the clock, if T = 0 then the output of the flip-flop is unchanged; if T=1, the output is inverted.

## Slide 11: Observations
All of the flip-flops and latches shown so far are positive edge triggered or positive level triggered. They also have active high load, set and clear inputs.
It is possible for those components to be negative edge triggered or negative level triggered and have active low control signals as well.
Flips-flops and latches can be combined in parallel to store data with more than one bit

## Slide 12: 4 bit D flip-flop
Control signals are tied together
Act as one unified data register
They usually output only the data (not the complement of the data as the 1 bit flip-flops)

## Slide 13: Counters
Store a binary value and when signaled to do so, it increments or decrements its value
Can be loaded with an externally supplied value
INC=1
Current Counter Value: 1111
Next Counter Value: 0000
Notes: <number>

## Slide 14: Up/down counter with parallel load
Ability to load external data as well as count
Down counter decrements its value rather than increment and generates a borrow rather than a carry out
Up/down counter can do both operations according with the signal U/D’

## Slide 15: Shift Registers
Can shift its data one bit position to the right or left
It is useful for hardware multipliers/dividers
It may shift left, right or both directions under certain control conditions (like the up/down counter)

## Slide 16: Programmable Logic Devices
Most of the circuits presented so far are available on a TTL IC chip. Circuits can be constructed using these chips and wiring them together
An alternative to this method would be to program all the components into a single chip, saving wiring, space and power
One type of such device is PLA (Programmable Logic Array) that contains one or more and/or arrays.

## Slide 17: PLA
The inputs and their complements are made available to several AND gates.
  An X indicates that the value is input to the AND gate
  The output from the AND gates are input into the OR gates, which produce the chip’s outputs
Functions:
  b = X2’ + X1’X0’+X1X0
  c = X2 + X1’ + X0

## Slide 18: PAL
Programmable Array of Logic – its OR blocks are not programmable
  Certain AND gates serve as input to specific OR gates
  Same b and c function implementation:
  b = X2’ + X1’X0’+X1X0
  c = X2 + X1’ + X0
PLA and PAL are limited because they can implement only combinatorial logic, they don’t contain any latches nor flip-flops

## Slide 19: PLD
Programmable Logic Device is a more complex component that is needed to realize sequential circuits
It is usually made up of logic blocks with the possibility to interconnect them.
Each logic bloc is made out of macro cells, that may be equivalent to a PAL with an output flip-flop
The input/output pins of an PLD can be configured to the desired function (unlike for PLA or PAL, where they are fixed)
Used in more complex design than the PAL or PLA

## Slide 20: CPLDs
Array of PLDs
Has global routing resources for connections between PLDs and between PLDs to/from IOs

## Slide 23: FPGAs
Field Programmable Gate Array is one of the most powerful and complex programmable circuit available
Contain an array of cells, each of which can be programmed to realize a function
There are programmable interconnects between the cells, allowing connect to each other
Includes flip-flops allowing the design and implementation of complex sequential circuit on a chip (of a complexity of a processor)
Often contains the equivalent of 100k to a few million simple logic gates on a single chip

## Slide 24: FPGAs
Configuration Memory
Programmable Logic Blocks (PLBs)
Programmable Input/Output Cells
Programmable Interconnect
Typical Complexity = 5M - 100M transistors

## Slide 25: Basic FPGA Operation
1110011010001000100101010001011100010100101010101001001000100010101001001001100100100001111000110010100010000110010001010001001001001000101001010101001001001010001010010100010100101001000100101010111010101010101010101010101111011111000000000000001101001111100001001110000011100100101000000001111100100100010100111001001010000111100011100010010101010101010101010010100101010100100101010101010101001001001
Load Configuration Memory
  Defines system function (Input/Output Cells, Logic in PLBs, Connections between PLBs & I/O cells)
Changing configuration memory => changes system function
Can change at anytime
  Even while system function is in operation
  Run-time reconfiguration (RTR)

## Slide 26: Programmable Logic Blocks
PLBs can perform any logic function
  Look-Up Tables (LUTs)
    Combinational logic
    Memory (RAM)
  Flip-flops
    Sequential logic
  Special logic
    Add, subtract, multiply
    Count up and/or down
    Dual port RAM
#PLBs per FPGA: 100 to 500,000
LUT/
RAM
FF
LUT/
RAM
FF
LUT/
RAM
FF
LUT/
RAM
FF
PLB architecture

## Slide 27: Programmable Interconnect
Wire segments & Programmable Interconnect Points (PIPs)
  cross-point PIPs – connect/disconnect wire segments
    To turn corners
  break-point PIPs – connect/disconnect wire segments
    To make long and short signal routes
  multiplexer (MUX) PIPs select 1 of many wires for output
    Used at PLB inputs
    Primary interconnect media for new FPGAs
configuration
memory
element
wire A
wire B
cross-point PIP
wire A
wire B
wire A
wire B
break-point PIP
wire A
wire B
output
multiplexer PIP
wire C

## Slide 28: References
“Computer Systems Organization & Architecture”, John D. Carpinelli, ISBN: 0-201-61253-4