## Slide 1: Computer Organization
CT213 – Computing Systems Organization

## Slide 2: Overview
Review of computer organization
  Generic organization
  Von Neumann vs. Harvard architectures
  Components: buses, CPU, memory, I/O subsystem
Programs
  Development tools
  High level programming languages
  Assembly programming language
  Machine language
Operating System
  Multiprogramming
  Protection
  Privileged mode
Overview of the processor, memory subsystem and I/O subsystem

## Slide 3: Basic Computer Organization
Notes: <number>
Most computer systems can be divided into three subsystems: the processor (known also as CPU), the memory and the Input/Output subsystem. The processor is responsible for executing programs, the memory is responsible for storage space for programs and data they reference and the I/O subsystem allows the processor to control devices that interact with outside world (such as CDROM, Monitor, Keyboard, etc..)

## Slide 4: Computer organization
Notes: <number>
In most computer systems, the processor has a single data buss that connects to a switch module, such as the PCI bridge found in many PC systems. Some processors do integrate the switch module onto the same chipset as the processor itself, to reduce the number of systems required to build a computer system, and thus the system cost.
The switch communicates with the memory through a memory bus, a dedicated set of wires that transfer data between these two systems. A separate I/O bus connects the switch to the I/O devices. Separate memory and I/O buses are used because the I/O system is generally designed for maximum flexibility while the memory system is design for maximum speed. The goal of the I/O bus is to allow for a large number of different devices to be connected to the processor, while the memory system is designed for maximum throughput.

## Slide 5: Programs
Sequences of instructions that tell computer what to do
To the computer, a program is made out of a sequence of numbers that represent individual operations.
  those operations are known as machine instructions or just instructions
  A set of instructions that a processor can execute is known as instruction set

## Slide 6: Program Development Tools
High level languages
  Hide all of the details about the computer and the operating system
  Platform independent
    Same code can be compiled for different platforms
Assembly language
  Platform dependent
    Code written for a processor will not run on a different family of processors, with an incompatible instruction set
  Processors are made usually backwards compatible
    See x86 family (code written for 286 will still run on Pentium machines)
Machine languages
  Contain the binary values that cause the processor to perform certain operations
  Platform specific
    When a microprocessor reads and executes an instruction, it is a machine language instruction

## Slide 7: Compiling programs
Notes: <number>
Compiler:
Checks to make sure every line in the code is valid
Once the program is syntax error free, it will finish compile the source code and generates object code
Object code is the machine language equivalent to the source code
At this point, the program has been complied successfully, but is not ready to execute.
Linking:
Some programs need object code from other programs or libraries (other object files)
A linker combines your object code with any other required object code
The combined code is stored as executable file, the code that the computer runs.
A loader copies the executable file into the memory, and then the microprocessor runs the code contained in that file.
One high level language statement is converted into one or more machine code instructions. There may be more than just one valid conversion for a statement, which complicates the compiler. This is not the case with the assembler. With assembler, one assembly instruction corresponds to exactly one machine code instruction. For this reason, assemblers are much less complicated than an compiler

## Slide 8: Assembling programs
Assembly language is specific to one microcontroller
Converts the source code into object code
The linker will combine the object code of your program with any other required object code to produce executable code
Loader will load the executable code into memory, for execution
Notes: <number>
In some cases, where there is no need for an operating system (i.e. in some of the consumer appliances), the code generated by the assembly operation is the final executable code.
Assembly language is sometime used to optimize pieces of code written in high level languages. Certain functions from a C++/C program may be written in assembly to optimize the execution time. Of course, the program is no longer portable between platforms.

## Slide 9: Java – different way of processing
Notes: <number>
Java programming language, is a high level programming language. Unlike the other high level programming languages, the code is not compiled into machine specific code that can be executed by a microprocessor. Instead, the java programs are compiled into something called bytecode. The bytecode is input to a JAVA Virtual Machine (JVM) , which interprets and executes the code. The JVM can be a hardware chip, but it is usually a program itself, often part of a web browser (to interpret applets).
The bytecode is platform independent. So, the JVM is specific for each platform, but the bytecode for the program remains the same across different platforms. This is a very nice feature of JAVA. Of course there is always a trade off….that refers to the execution speed.

## Slide 10: Operating System
Responsible for managing the physical resources of complex systems (PCs, workstations, mainframe computers)
Responsible for loading and executing programs and interfacing with the users
Usually no operating system for small embedded systems
  Computers designed for one specific task
It is a program that runs on the computer, that knows about all the hardware and usually runs in privileged (or supervisor) mode, having access to physical resources that user programs can’t control and has the ability to start and stop user programs
Notes: <number>

## Slide 11: Multiprogramming (1)
Technique that allows the system to present the illusion that multiple programs are running on the computer simultaneously
  Protection between programs is very important
Many multiprogrammed computers are multiuser
  Allow multiple persons to be logged on at a time
  Beside protection, data privacy is also important
Multiprogramming is achieved by switching rapidly between programs.
  Each program is allowed to execute for a fixed amount of time – timeslice
Notes: <number>
The user programs don’t need to know that other programs are running on the system. The operating system in combination with the hardware provide protection for programs, preventing any program from accessing another’s program data unless the two programs have special arrangements to do so.

## Slide 12: Multiprogramming (2)
When a program timeslice ends, the OS stops it, removes it and gives another program control over processor – this is a context switch
  To do a context switch the OS copies the content of current program register file into memory, restores the contents of the next program’s register file into the processor and starts executing the next program.
  From the program point of view, they can’t tell that a context switch has been performed
Notes: <number>
Old computers used to context switch about 60 times per second. This gives the illusion, if a relative small number of processes are executing on the computer, that each individual program is having full control over the machine. Now-days, the modern computers are actually switching more often between programs.

## Slide 13: Protection (1)
The result of any program running on a muliprogrammed computer must be the same as if the program was the only program running on the computer
Programs must not be able to aces other program’s data and must be confident that their data will not be modified by other programs.
Programs must not interfere with other program’s use of I/O devices

## Slide 14: Protection (2)
Protection is achieved by having the operating system to have full control over the resources of the system (processor, memory and I/O devices)
Virtual memory is one of the techniques used to achieve protection between programs
  Each program operates as if it were the only program on the computer, occupying a full set of the address space in its virtual space. The OS is translating memory addresses that the program references into physical addresses used by the memory system.
  As long as two program’s addresses are not translated to same address space, programs can be written as they were the only ones running on the machine

## Slide 15: Privileged Mode
To ensure that the operating system is the only one that can control the physical resources it executes in privileged mode
  User programs execute in user mode
When user mode programs want to execute something that requires privileged rights, it sends a request to the OS, known as system call, that asks the OS to do the operation for them
OS is also responsible for low level UI
  Keys are pressed, the OS is responsible to determine which program should receive the input
  When a program wants to display some output, the user program executes some system call that displays the data

## Slide 16: The Processor - Instruction Cycles
The instruction cycle is the procedure of processing an instruction by the microprocessor:
  Fetches or reads the instruction from the memory
  Decodes the instruction, determining which instruction is to be executed (which instruction has been fetched)
  Executes the instruction – performs the operations necessary to complete what the instruction is suppose to do (different from instruction to instruction, may read data from memory, may write data to memory or I/O device, perform only operations within CPU or combination of those)
Each of the functions fetch -> decode -> execute consist of a sequence of one or more operations inside the CPU (and interaction with the subsystems)

## Slide 17: Processor Organization
Notes: <number>
Any processor is made up of execution unit(s), control unit and register file.
Registers:
  PC (program counter) keeps the address of the next instruction
  IR (instruction register) keeps the instruction being executed

## Slide 18: Execution Unit Example
//Code for a = b + c
LD R3, b //copy value b from memory to R3
LD R4, c //copy value c from memory to R4
add R3, R4 //sum placed in R3
ST R3, a //store the result into memory
Notes: <number>
Execution unit – performs various arithmetic and logic operations (such as add, multiply, etc..) on binary representation of numbers (integers or floating point numbers). Computations are performed by loading the values into general purpose registers, perform the arithmetic on the registers and then saving the results back into the memory
Status registers are used by various parts of the CPU to store status of the operations. One of the roles of the status registers is to hold data where CPU keeps information about the computations being executed (such as the result of the last function unit operation was zero).

## Slide 19: Control Unit
The control unit controls the execution of the instructions stored in the main memory (retrieve and execute them)
Notes: <number>
The control unit has three components:
A component that brings the instruction from the main memory into the internal registers of the CPU, called Fetch Unit
A component that identifies what instruction is – the Decode Unit
Another component that signals the other parts of the computer to execute the instruction
The Program Counter register contains the memory address of the instruction is currently processing. The program counter register is incremented in the fetch stage (so it is very often referred as holding the next instruction address)
The Instruction Register holds the current instruction, once it has been fetched from the main memory.
When the machine is initially started, the PC is loaded with the address of the first instruction to be executed (usually a hardwired address). There many variations on how the computing system can start. One usual way is where the memory (usually ROM) will contain initialization code and a program called bootstrap loader that will load the operating system from a peripheral storage or from the network.

## Slide 20: The Memory Subsystem (1)
ROM (Read Only Memory)
  Used to store the BIOS and/or a bootstrap or boot loader program
  Nonvolatile
RAM
  Read/write memory used to hold the programs, operating system and data required by the computer
  Volatile
Memory is divided into a set of storage locations which can hold data. Those are numbered and the number of a storage location (its address) is used to tell the memory which location the processor wants to access

## Slide 21: The Memory Subsystem (2)
The width of address limits the amount of memory that a computer can address
  Most current computers use 32 bit address, which means that the maximum number of locations is 232, about 4 GB.
Memory subsystem supports two operations:
  Load (or read) – address of the data location to be read
  Store (or write) – address of the location and the data to be written
Memory subsystem allows for more than 1 byte to be read or written at a time
  Read and write operations operate at the width of system’s data bus, usually 32 bit (4 bytes)
  The address contains the address of the lowest byte to be addressed
  i.e. a 4 byte read operation from address 0x1000 would return bytes stored at addresses: 0x1000, 0x1001, 0x1002 and 0x1003

## Slide 22: The Memory Subsystem (3)
Some systems want addresses to be aligned
  address of a memory reference must be multiple of the size of data being read or written
Order in which the bytes are written to memory
  Little endian systems (PC)
    LSB written at lowest address byte
  Big endian systems (Apple computers: G3, G4)
    MSB written at lowest address byte
Notes: <number>
In general programmers don’t need to know about these conventions, if the data bit length for the read/write operations is the default one. If they are using read and writes of different lengths than the default ones, than the results on different architectures (little endian vs. big endian architectures) would be different.

## Slide 23: The I/O Subsystem
Contains devices that the computer uses to communicate with outside world and to store data
I/O devices are usually communicating with the processor using and I/O bus
  PCs are using PCI bus for their I/O bus
  OS needs a device driver to access a given I/O device
    Program that allows the OS to control the I/O device

## Slide 24: I/O read/write operations
The I/O read and write operations are similar to the memory read and write operations.
A processor may use:
  memory mapped I/O (when the address of the I/O device is in the direct memory space, and the sequence to read/write data in the device are the same with the memory read/write sequence)
  isolated I/O – the process is similar, but the processor has a second set of control signals to make the distinction between a memory access and an I/O access (memory locations and I/O devices can be located at the same address, which makes this extra control signal necessary); for I/O operations, the processor holds IO/M’ (or similar) signal high for the duration of the I/O operation
Notes: <number>
The I/O read and write operations are similar to the memory read and write operations.
A processor may use either memory mapped I/O (when the address of the I/O device is in the direct memory space, and the sequence to read/write data in the device are the same with the memory read/write sequence) or isolated I/O

## Slide 25: References
“Computer Systems Organization & Architecture”, John D. Carpinelli, ISBN: 0-201-61253-4