## Slide 1: Device Management
CT213 – Computing system Organization

## Slide 2: Content
Device management approaches
I/O system organization
Direct I/O and Memory Mapped I/O
  Direct I/O with polling
  Interrupt driven direct I/O
Direct memory access
Buffering
Device drivers

## Slide 3: Device Management Approaches (1)
Direct I/O – CPU software explicitly transfer data to and from the controller’s data registers
  Direct I/O with polling – the device management software polls the device controller status register to detect completion of the operation; device management is implemented wholly in the device driver, if interrupts are not used
  Interrupt driven direct I/O – interrupts simplify the software’s responsibility for detecting operation completion; device management is implemented through the interaction of a device driver and interrupt routine

## Slide 4: Device Management Approaches (2)
Memory mapped I/O – device addressing simplifies the interface (device seen as a range of memory locations);
  Memory mapped I/O with polling – the device management software polls the device controller status register to detect completion of the operation; device management is implemented wholly in the device driver.
  Interrupt driven I/O – interrupts simplify the software’s responsibility for detecting operation completion; device management is implemented through the interaction of a device driver and interrupt routine
Direct memory access – involves designing of hardware to avoid the CPU perform the transfer of information between the device (controller’s data registers) and the memory

## Slide 5: I/O system organization
An application process uses a device by issuing commands and exchanging data with the device management (device driver).
Device driver responsibilities:
  Implement communication APIs that abstract the functionality of the device
  Provide device dependent operations to implement functions defined by the API
API should be similar across different device drivers, reducing the amount of info an application programmer needs to know to use the device
Since each device controller is specific to a particular device, the device driver implementation will be device specific, to
  Provide correct commands to the controller
  Interpret the controller status register (CSR) correctly
  Transfer data to and from device controller data registers as required for correct device operation
Notes: <number>

## Slide 6: Direct I/O versus memory mapped I/O
copy_in R3, 0x012, 4
will cause the machine to copy the contents of data register 4 in the controller with address 0x012 into CPU register R3
Store R3, 0xFFFF0124
The device is associated with logical memory locations; each component of the device that is referenced by software is located at a normal memory address
Notes: <number>
Traditionally, the instruction set includes special instructions to work with I/O devices; each instruction refers to the device’s address through a unique identifier
  input device_address
    Causes the read command to be placed in command register of the given controller (at the specified address)
  output device_address
    Causes the write command to be placed in the command register of the given controller
  copy_in CPU_register, device_address, controller_reg
  copy_out CPU_register, device_address, controller_reg
    Copy into or out of a CPU register from /to the designated data register of the I/O controller identified by device_address address.

## Slide 7: I/O with polling
Each I/O operation requires that the software and hardware coordinate their operations to accomplish desired effect
In direct I/O pooling this coordination is done in the device driver;
While managing the I/O, the device manager will poll the busy/done flags to detect the operation’s completion; thus, the CPU starts the device, then polls the CSR to determine when the operation has completed
With this approach is difficult to achieve high CPU utilization, since the CPU must constantly check the controller status;

## Slide 8: I/O with polling - read
Application process requests a read operation
The device driver queries the CSR to determine whether de device is idle; if device is busy, the driver waits for it to become idle
The driver stores an input command into the controller’s command register, thus starting the device
The driver repeatedly reads the content of CSR to detect the completion of the read operation
The driver copies the content of the controller's data register(s) into the main memory user’s process’s space.
Notes: <number>

## Slide 9: I/O with polling - write
1. The application process requests a write operation
2. The device driver queries the CSR to determine if the device is idle; if busy, it will wait to become idle
3. The device driver copies data from user space memory to the controller’s data register(s)
4. The driver stores an output command into the command register, thus starting the device
5. The driver repeatedly reads the CSR to determine when the device completed its operation

## Slide 10: Interrupt driven I/O
In a multiprogramming system the wasted CPU time (in polled I/O) could be used by another process; because the CPU is used by other processes in addition to the one waiting for the I/O operation completion, in multiprogramming system may result a sporadic detection of I/O completion; this may be remedied by use of interrupts
The reason for incorporating the interrupts into a computer hardware is to eliminate the need for a device driver to constantly poll the CSR
Instead polling, the device controller “automatically” notifies the device driver when the operation has completed.

## Slide 11
1 - the application process requests a read operation
2 - the device driver queries the CSR to find out if the device is idle; if busy, then it waits until the device becomes idle
4 – when this part of the device driver completes its work, it saves information regarding the operation it began in the device status table; this table contains an entry for each device in system
5 – the device completes the operation and interrupts the CPU, therefore causing an interrupt handler to run
3 - the driver stores an input command into the controller’s command register, thus starting the device
6 – the interrupt handler determines which device caused the interrupt; it then branches to the device handler for that device
7 – the device driver retrieves the pending I/O status information from the device status table
8a, 8b – the device driver copies the content of the controller’s data register(s) into the user process’s space
9 – the device handler returns the control to the application process (knowing the return address from the device status table)
Notes: <number>
1 - the application process requests a read operation
2 - the device driver queries the CSR to find out if the device is idle; if busy, then it waits until the device becomes idle
3 - the driver stores an input command into the controller’s command register, thus starting the device
4 – when this part of the device driver completes its work, it saves information regarding the operation it began in the device status table; this table contains an entry for each device in system; the information written into this table contains the return address of the original call and any special parameters for the I/O operation; the CPU, after is doing this, can be used by other program, so the device manager invokes the scheduler part of the process manager. It then terminates
5 – the device completes the operation and interrupts the CPU, therefore causing an interrupt handler to run
6 – the interrupt handler determines which device caused the interrupt; it then branches to the device handler for that device
7 – the device driver retrieves the pending I/O status information from the device status table
8a, 8b – the device driver copies the content of the controller’s data register(s) into the user process’s space
9 – the device handler returns the control to the application process (knowing the return address from the device status table)
Same sequence (or similar) of operations will be accomplished for an output operation.

## Slide 12: Overlapping CPU execution with device operation
The software interface to an I/O device usually enables the operating system to execute alternative processes when any specific process is waiting for I/O to complete, while preserving serial execution semantics for an individual process
That means that whenever the programmers will use read statement in a program, they will know that the next instruction will not execute until the read instruction has completed.
Consider the following code:
…
read (device, “%d”, x);
y=f(x);
….
Notes: <number>
If the CPU was to execute the assignment (y = f(x)) before the I/O operation has completed, it will result in an error; thus, the operating system explicitly blocks the process that is executing the sample code, until the I/O read call is completed.

## Slide 13: Direct memory access
Traditional I/O
  Polling approach:
    CPU transfer data between the controller data registers and the primary memory
    Output operations - device driver copies data from the application process data area to the controller; vice versa for input operations
  Interrupt driven I/O approach - the interrupt handler is responsible for the transfer task

## Slide 14: Direct memory access
DMA controllers are able to read and write information directly from /to primary memory, with no software intervention
The I/O operation has to be initiated by the driver
DMA hardware enables the data transfer to be accomplished without using the CPU at all
The DMA controller must include an address register (and address generation hardware) loaded by the driver with a pointer to the relevant memory block; this pointer is used by the DMA hardware to locate the target block in primary memory

## Slide 15: Typical DMA
Mimics the processor
Transfers data to/from memory over system bus
Notes: <number>
It can use the system bus only when the processor doesn’t need it or when the processor is temporarily suspended.
DMA OPERATION (when the processor wants to read/write a block of data), it issues a command to the DMA module by sending the DMA module the following information:
Whether a read or a write is requested, using the read or write control line between the processor and DMA module
The address of the I/O device involved, communicated on the data lines
The starting address in the memory to read from or write to, communicated on the data lines, and stored by the DMA controller in its address register
The number of words to be read or written, communicated over the data lines and stored in the count register.
Then the processor continues with other work. The DMA module transfers the entire block of data, one word at a time, directly to or from the main memory, without going through the processor. When the transfer is completed, the DMA generates an interrupt to the processor to let it know the transfer has finished. Thus, the processor is involved only in the beginning and end of the DMA transfer.

## Slide 16: Alternative DMA configurations
Notes: <number>
Option b is more efficient, because each word transfer consumes only one bus cycle, vs. a) where each word transfer consumes two bus cycles.

## Slide 17: Design Objectives
Efficiency
  Most I/O devices are extremely slow compared with the processor and the main memory
    Buffering is one way to deal with this issue
Generality
  It is desirable to handle all devices in a uniform and consistent manner
  Applies for both
    The way the user processes see the devices
    The way the operating system manages the I/O devices and operations

## Slide 18: I/O System Organization – detailed
COMMUNICATION ARCHITECTURE – logical I/O module is replaced by communication architecture, which may itself consist of a number of layers. An example here is TCP/IP.
LOGICAL I/O - deals with the device as a logical resource and is not concerned with the details of actually controlling the device. The logical I/O module is concerned with managing general I/O functions in behalf of user process, allowing them to deal with the device in terms of device identifier and simple commands such as open, close, read, write.
DEVICE I/O- the requested operations and data (buffered characters, records, etc) are converted into appropriate sequences of I/O instructions, channel commands and controller orders/commands. Buffering may be used to improve the efficiency.
SCHEDULING AND CONTROL - the actual queuing and scheduling of I/O operations occur at this level, as well as the control of the operations. Thus, interrupts are handled at this layer and I/O status is collected and reported. This is the layer software that interacts with the I/O module an hence the device hardware.
DIRECTORY MANAGEMENT - symbolic file names are converted to identifiers that either reference the file. This layer is also concerned with user operations that modify the directory of files: add, delete, reorganize, etc…
FILE SYSTEM - this layer deals with logical structure of files and with the operations that can be specified by users upon a file: open, close, read, write. Access rights are also managed at this layer.
PHYSICAL ORGANIZATION- logical references to files and records must be converted to physical secondary storage addresses (in a similar way as virtual address reference should be converted to physical address through segmentation/paging). During this translation, physical track and sector structure of the secondary storage is taken into account. This layer takes care of allocation of secondary storage space.
Notes: <number>
There are three main types of devices: local peripheral devices, communication devices and storage devices.
LOGICAL I/O
Deals with the device as a logical resource and is not concerned with the details of actually controlling the device. The logical I/O module is concerned with managing general I/O functions in behalf of user process, allowing them to deal with the device in terms of device identifier and simple commands such as open, close, read, write.
DEVICE I/O
The requested operations and data (buffered characters, records, etc) are converted into appropriate sequences of I/O instructions, channel commands and controller orders/commands. Buffering may be used to improve the efficiency.
SCHEDULING AND CONTROL
The actual queuing and scheduling of I/O operations occur at this level, as well as the control of the operations. Thus, interrupts are handled at this layer and I/O status is collected and reported. This is the layer software that interacts with the I/O module an hence the device hardware.
COMMUNICATION ARCHITECTURE
Logical I/O module is replaced by communication architecture, which may itself consist of a number of layers. An example here is TCP/IP.
DIRECTORY MANAGEMENT
At this layer, symbolic file names are converted to identifiers that either reference the file. This layer is also concerned with user operations that modify the directory of files: add, delete, reorganize, etc…
FILE SYSTEM
This layer deals with logical structure of files and with the operations that can be specified by users upon a file: open, close, read, write. Access rights are also managed at this layer.
PHYSICAL ORGANIZATION
Logical references to files and records must be converted to physical secondary storage addresses (in a similar way as virtual address reference should be converted to physical address through segmentation/paging). During this translation, physical track and sector structure of the secondary storage is taken into account. This layer takes care of allocation of secondary storage space.

## Slide 19: Buffering
Buffering is the technique by which the device manager can keep slower I/O devices busy during times when a process is not requiring I/O operations.
Input buffering is the technique of having the input device read information into the primary memory before the process requests it.
Output buffering is the technique of saving information in memory and then writing it to the device while the process continues execution
Notes: <number>
Buffering is the technique by which the device manager can keep slower I/O devices busy during times when a process is not requiring I/O operations.
Input buffering is the technique of having the input device read information into the primary memory before the process requests it.
Output buffering is the technique of saving information in memory and then writing it to the device while the process continues execution

## Slide 20: Hardware level buffering
Consider a simple character device controller that reads a single byte form a modem for each input operation.
  Normal operation: read occurs, the driver passes a read command to the controller; the controller instructs the device to put the next character into one-byte data controller’s register; the process calling for byte waits for the operation to complete and the retrieves the character from the data register
Add a hardware buffer to the controller to decrease the amount of time the process has to wait
  Buffered operation: the next character to be read by the process has already been placed into the data register, even the process has not yet called for the read operation
Notes: <number>
Consider a simple character device controller that reads a single byte form a modem for each input operation.
Normal operation: read occurs, the driver passes a read command to the controller; the controller instructs the device to put the next character into one-byte data controller’s register; the process calling for byte waits for the operation to complete and the retrieves the character from the data register
Buffered operation: the next character to be read by the process has already been placed into the data register, even the process has not yet called for the read operation

## Slide 21: Driver level buffering
This is generally called double buffering
One buffer is for the driver to store the data while waiting for the higher layers to read it
The other buffer is to store data from the lower level module
This technique can be used for the block-oriented devices (buffers must be large enough to accommodate a block of data)

## Slide 22: Using multiple buffers
The number of buffers is extended from two to n
The data producer (controller in read operations, CPU in write operations) is writing into buffer i while the data consumer (the CPU in read operations, the controller in write operations) is reading form buffer j
In this configuration buffers j+1 to n-1 and 0 to i-1 are full
This is known as circular buffering technique

## Slide 23: Device manager design
Designing the device manager involves to invoke controller specific I/O operations while satisfying:
  Create an API that implements the I/O functions available to the device, still compliant with interfaces implemented by other drivers; this is called device driver interface
  Achieve correct coordination among the application processes, drivers and device controllers
  Optimize the overall machine performance with correct driver strategies

## Slide 24: Device driver interface
Each operating system defines an architecture for its device management system
The designs are different from operating system to operating system; there is no universal organization
Each operating system has two major interfaces to the device manager:
  The driver API
  The interface between a driver and the operating system kernel

## Slide 25: Driver API
Provides a set of functions that an programmer can call to manage a device (usually comms or storage)
The device manager
  Must track the state of the device: when it is idle, when is being used and by which process
  Must maintain the information in the device status table
  May maintain a device descriptor to store other information about the device
open/close functions to allow initiate/terminate of the device’s use
  open – allocates the device and initializes the tables and the device for use
  close – releases dynamic tables entries and releases the device
read/write functions to allow the programmer to read/write from/to the device
  A consistent way to do these operations across all the devices is not possible; so a concession by dividing the devices into classes is made:
    such as character devices or block devices
    Sequential devices or randomly accessed devices
ioctl function to allow programmers to implement device specific functions

## Slide 26: The driver - kernel interface
The device driver must execute privileged instructions when it starts the device; this means that the device driver must be executed as part of the operating system rather than part of a user program
The driver must also be able to read/write info from/to the address spaces of different processes, since same device driver can be used by different processes
Two ways of dealing with the device drivers
  Old way: driver is part of the operating system, to add a new device driver, the whole OS must have been complied
  Modern way: drivers installation is allowed without re-compilation of the OS by using reconfigurable device drivers; the OS dynamically binds the OS code to the driver functions
    A reconfigurable device driver has to have a fixed, standardized API
    The kernel has to provide an interface to the device driver to allocate/de-alocate space for buffers, manipulate tables in the kernel, etc…

## Slide 27: Reconfigurable device drivers
The OS uses an indirect reference table to access the different driver entry points, based on the device identifier and function name
The indirect reference table is filled with appropriate values whenever the device driver loads (because the detection of a PnP device or at boot time)
When a process performs a system call, the kernel passes the call onto the device driver via the indirect reference table

## Slide 28: References
“Operating Systems”, William Stallings, ISBN 0-13-032986-X
“Operating Systems – A modern perspective”, Garry Nutt, ISBN 0-8053-1295-1