## Slide 1: CT542
Networking Overview
Notes: <number>

## Slide 2: Content
Computer Networks vs. Distributed Systems
Uses of computer networks
Network Hardware
Network Software
Network Technologies
Notes: <number>

## Slide 3: Computer Networks
Computer network – collection of autonomous computers interconnected by a single type of technology
  Networks come in many sizes, shapes and forms
Internet – not a network. It is a network of networks
World Wide Web – not a network. It is a distributed system that runs in the top of Internet
Notes: <number>
Two computers are said to be INTERCONNECTED if they are able to exchange information. The connection can be copper wire, optical fiber, wireless, etc…

## Slide 4: Computer Networks vs. Distributed System
Distributed System – collection of computers appear to the user in a single, coherent system.
  Often a layer of software, in the top of OS, called middleware, is implementing this model
  Example: World Wide Web, looks to the user like a document (web page)
Computer Network – this coherence is absent.
  Users are exposed to the actual machines
  If the machines have different hardware and different operating system, this is visible to the users
  If a user wants to run a program on the remote machine, has to log and run it there
Notes: <number>
In effect, a distributed system is a system built in the top of a network. The software that implements it gives it a degree of cohesiveness and transparency. THE DISTINCTION BETWEEN A COMPUTER NETWORK AND A DISTRIBUTED SYSTEM LIES IN SOFTWARE RATHER THAN IN HARDWARE.

## Slide 5: Uses of Computer Networks
  Business Applications
  Home Applications
  Mobile Users
Notes: <number>
We will start with looking into why people are interested in computer networks. If there would have been no interest, very few computer networks would have been built.

## Slide 6: Business Applications of Networks (1)
Resource sharing
  Printers, storage servers, databases, etc…
Communication between companies
  E-Mail
  Instant messaging
Stock management
E-Commerce
  Electronic Commerce – business with consumers over Internet
  This sector is expected to grow very quickly
Notes: <number>

## Slide 7: Business Applications of Networks (2)
Client – Server Model
Example - A network with two clients and one server.
Notes: <number>
CLIENT – SERVER model is employed in business applications. The Server is a powerful machine that can have multiple concurrent clients accessing its resources at the same time. Clients are simpler machines that just interpret the information provided by a server.

## Slide 8: Business Applications of Networks (3)
The client-server model involves requests and replies.
Client – Server model employs at least two processes: one running on the server and one running on the client
Notes: <number>

## Slide 9: Home Network Applications (1)
Access to remote information
  Newspapers, publications, etc..
Person-to-person communication
  Instant messaging, e-mail, chat rooms, peer to peer communication (napster, kaaza, etc..)
Interactive entertainment
  Network games, video on demand, audio on demand, etc…
Electronic commerce
Notes: <number>
KEN OLSEN – president of Digital (second big computer vendor in the world, after IBM, in 1977) said “ There is no reason for any individual to have a computer in his home”. History proved otherwise, and Digital is gone.
Why people buy computers? Initially for WORD PROCESSING and for GAMES. Recently for access to INFORMATION, for PERSON TO PERSON COMMUNICATION, for interactive ENTERTAINMENT and for E-COMMERCE. All based on networking technologies in one way or another.

## Slide 10: Home Network Applications (2)
In peer-to-peer system there are no fixed clients and servers.
Notes: <number>
Napster – 50 millions members in 2000. It’s been shut down for copyright infringement. Used a centralized db with info about its users and shared files.
Newer peer to peer systems don’t have anymore a centralized db. Lookup of the content is coming from local db-s maintained by each of the members. Beside content, each user maintains a list of other users as well.

## Slide 11: Home Network Applications (3)
Some forms of e-commerce.
Notes: <number>

## Slide 12: Mobile Network Users
Combinations of wireless networks and mobile computing.
Notes: <number>
WIRELESS NETWORKS and MOBILE COMPUTING are related, but not the same thing. Here is a distinction between fixed wireless networks and mobile wireless. Even notebook computers are sometimes wired. Some mobile computing equipment is not necessarily wireless (i.e. notebook in a hotel room) while not all wireless networks are mobile (network of desktop computers in a unwired building)

## Slide 13: Network Hardware
Local Area Networks
Metropolitan Area Networks
Wide Area Networks
Wireless Networks
Home Networks
Internetworks
Notes: <number>

## Slide 14: Networks (1)
By transmission technology
  Broadcast links – single communication channel is shared by all machines in the network
    Packets (containing addresses) are exchanged
    Ability to address all destinations (broadcast)
    Ability to address a group of machines (multicast)
  Point-to-point links – many connections between individual pairs of machines
    A packet from source to destination may have to visit multiple machines
    As a rule: small networks (size wise) use broadcast technologies, while large networks are usually point to point
Notes: <number>
Two main criteria are used to classify network hardware: Transmission Technology and Scale.

## Slide 15: Networks (2)
By scale.
Notes: <number>

## Slide 16: Local Area Networks
Types
Bus
Ring
Star
Notes: <number>
Local Area Networks are privately owned networks within a single building or camps, up to a few km in size. Are restricted in size, which means that worst case transmission time is bounded and known in advance.
LANs use very often same cable to which all the machines are attached. Speeds ranging from 10Mb/s to about 10Gb/s. Various TOPOLOGIES are possible for broadcast LANs: BUS, STAR (most popular here is Ethernet) and RING are mostly used.
ETHERNET – bus based network, bus and/or star topology, broadcast decentralized network, usually operating at 10Mb/s to 10Gb/s. Computers in Ethernet can transmit whenever they want; if two packets collide, each computer just waits a random time and tries again latter.
TOKEN RING – ring based network, copper cable based, operating at 4Mb/s and 16Mb/s. Typically each packet circumnavigates the entire ring. As with other types of broadcast networks, different methods to arbitrate the access to the ring are required.
FDDI – ring based network, optical fiber based.
Channel allocation can be static or dynamic. Static – divide time in intervals and allocate an interval per machine, using a round robin algorithm. This would let machines broadcast only when it is its turn. This method wastes time when machines don’t have anything to transmit. Dynamic channel allocation – could be centralized or decentralized.

## Slide 17: Metropolitan Area Networks
A metropolitan area network based on cable TV.
Notes: <number>
Metropolitan Area Network (MAN) covers a city. Best known example of a MAN is the cable TELEVISION NETWORK available in many cities. Until late 1990’s they were intended for television only. After that, the cable providers realized that they could offer two way Internet in the unused parts of the spectrum. This transformed the TV network in a metropolitan area network.

## Slide 18: Wide Area Networks (1)
Relation between hosts on LANs and the subnet.
Notes: <number>
A Wide Area Network (WAN) spans over a large area, often a country or a continent. It contains a number of machines (called HOSTS in the networking context) that are connected by a communication SUBNET. The hosts are usually owned by people, while the subnet is owned by the telecom providers or Internet providers.
The job of the subnet is to carry messages from host to host. Separation of the pure communication aspects of the network (the subnet) from the application aspects (hosts) simplifies the complete network design.
Subnets contain two components:
TRANSMISSION LINES – move bits between machines (copper, optical fiber, radio, etc)
SWITCHING COMPONENTS – specialized computers that connect three or more transmission lines. When data comes on one of the lines, the switching element has to choose an ongoing line to forward the data. ROUTER is the technical name for those switching elements.

## Slide 19: Wide Area Networks (2)
A stream of packets from sender to receiver.
Notes: <number>
A STORE-AND-FORWARD or PACKET SWITCHED subnet is one where the packets are received entirely at intermediate routers, stored until some outgoing transmission line is free and then forwarded to the next router. When packets are small and all the same size, they are called cells.
When a process on a host wants to send a message to another host in the network, the sending host cuts the message into packets, each one caring some sort of sequence number. Those packets are then injected into the network, one at a time, in quick succession. The packets are delivered over the network and delivered to the receiving host, where they are reassembled and delivered to the receiving process.
In this figure, all the packets from sender to receiver followed same route ACE. In some subnets, the packets must follow always same path, in other subnets, the packets can follow different paths (they are routed separately). When the packet is getting to router A, the decision to follow path C or path B is made locally. This decision is made by A and how this decision is made is calling routing algorithm.
Some other type of WANs are the satellite systems. They are broadcast networks and all routers can here the output from the satellite.

## Slide 20: Wireless Networks
Categories of wireless networks:
  System interconnection
  Wireless LANs
  Wireless WANs
Notes: <number>

## Slide 21: Wireless Networks (2)
(a) Bluetooth configuration
(b) Wireless LAN
Notes: <number>
BLUETOOTH is an example of system interconnection network and it is referring to interconnecting computer components (monitor, mouse, keyboard, etc…). It is a master slave topology. The master tells the slaves what addresses to use, when they can broadcast, how long they can transmit, what frequencies they can use and other information.
WIRELESS LANs – each computer has a radio modem and antenna with which it can communicate with other systems. IEEE 802.11 is a basic standard for wireless LAN. A number of newer, derivate standards are in place now.
WIRELESS WANs – cellular phone networks: Analog, GSM, GPRS, G3

## Slide 22: Wireless Networks (3)
(a) Individual mobile computers
(b) A flying LAN
Notes: <number>

## Slide 23: Home Network Categories
Computers (desktop PC, PDA, shared peripherals
Entertainment (TV, DVD, VCR, camera, stereo, MP3)
Telecomm (telephone, cell phone, intercom, fax)
Appliances (microwave, fridge, clock, etc..)
Telemetry (utility meter, burglar alarm, babycam).
Notes: <number>
Home networking has a different set of requirements and properties than other network types:
INSTALLATION must to be easy. Customers expect their home equipment to work 100% of the time.
The network and the networked devices have to be FOOLPROOF IN OPERATION. Simple interfaces have to be provided
LOW PRICE is essential
Network needs sufficient CAPACITY, since some of the appliances will involve audio and video
EXPANSION of the network should be possible (by starting with one or two devices and expand the network gradually). The network interface has to be stable over the years. Switching form FireWire to USB may not be well received by the end customers.
SECURITY and RELIABILITY are very important

## Slide 24: Internetworks
Collection of interconnected networks is called internetwork or internet.
Internet is one specific internet or internetwork
A common form of internet is a collection of LANs interconnected by a WAN
An internetwork is formed when distinct networks are interconnected
Notes: <number>

## Slide 25: Network Software
Protocol Hierarchies
Design Issues for the Layers
Connection-Oriented and Connectionless Services
Service Primitives
The Relationship of Services to Protocols
Notes: <number>

## Slide 26: Protocol Hierarchies
Layers, protocols, and interfaces.
Notes: <number>
To reduce complexity of design, networks are organized as layer, each one build upon the one below it. The number of layers, the name of each layer, the contents and function of each layer differ from network to network.
The purpose of each layer is to create services for the layers above, hiding to those layers the details of how those services are actually implemented. The fundamental idea is that a particular piece of software (or even hardware) provides a service to its users, but keeps the details of its internal state and algorithms hidden from them.
Layer n on a machine carries a conversation with layer n on another machine. The rules and conventions used in this conversation are known as layer n protocol. In essence, a PROTOCOL is an agreement between the communicating parties on how communication is to proceed. The entities that implement the protocol at different layers level are called PEERS. It is peers that communicate using the protocol.
In reality, no data is directly transferred from layer n on one machine on layer n on the other machine. In effect, each layer passes data and control information to the layer below it, until the lowest layer is reached. Below Layer 1 is the physical medium, through the communication occurs.
Between each pair of adjacent layers there is an interface. The interface defines which primitive operations and services the lower layer makes available to the upper one. Most difficult design issue is to define clean interfaces between layers.
A set of layers and protocols is called a NETWORK ARCHITECTURE (it has to contain enough information to allow hardware and software engineers to design hardware and software that would obey the right protocol). A list of protocols used by certain systems, one protocol per layer, is called a PROTOCOL STACK.

## Slide 27: Protocol Hierarchies (2)
The philosopher-translator-secretary architecture.
Notes: <number>
Layer3 – two philosophers (peer processes), one speaks English and the other one speaks French. Since they have no common language, they engage a translator (peer processes at Layer 2). The translators, each contact a secretary (peer process Layer 1). Translators have agreed on a common language that both know (Dutch).
Note that each protocol is completely independent of the other ones. If at any time, the translators decide to change the language, all they have to do is to agree between each other. None of the interfaces with layer 3 or layer 1 will be changed. Similarly, the secretary could choose to use a different transmission medium (say e-mail), without disturbing or even informing the other layers.

## Slide 28: Protocol Hierarchies (3)
Example information flow supporting virtual communication in layer 5.
Notes: <number>
A message is produced by an application process running at layer 5. Message M is then given to layer 4 for transmission. Layer 4 puts a header in the front of the message to identify the message and pass the result to layer 3. The header includes control information, such as sequence numbers to allow layer 4 on destination to deliver messages in the right order, if the lower layers do not maintain sequence. In some layers, headers can also contain sizes, times and other control fields.
At layer 3 there is a limit on the size of the packet that can be transmitted. So layer 3 will break the incoming message into smaller parts, packets, adding header H3 corresponding to layer 3 on each packet. In this example, message M is split into M1 and M2.
Layer 3 decides which outgoing lines to use and passes the message to layer 2. Layer 2 adds not only a header to each piece, but also a trailer and gives the resulting units to layer 1 for physical transmission.
At the receiving machine, the message moves upwards, from layer to layer, with headers being stripped off as it progresses.

## Slide 29: Design Issues for the Layers
Addressing
  consequence of having multiple destinations
Error Control
  The receiver should be able to inform sender which data was received correctly
Flow Control
  Keep sender from swamping slow receiver with data
  Keep the sender from swamping with data slow networks
Multiplexing
  Use same communication channel for multiple, unrelated conversations
Routing
  When multiple paths between source and destination, one path must be chosen
Notes: <number>

## Slide 30: Connection-Oriented and Connectionless Services
Layers can offer two types of services to the layers above: connection oriented services and connection-less services
Connection oriented services
  Reliable message stream (sequence of pages)
  Reliable byte stream (remote login, file transfer, etc..)
  Unreliable connection (digitized voice or video)
Connection-less
  Datagram service (in analogy with telegram service)
  Acknowledged datagram service
  Request-reply service
Notes: <number>
CONNECTION ORIENTED SERVICE – modeled after the phone systems. The service users establishes a connection, uses the connection and then releases the connection. The main idea, is that the connection acts as a PIPE, at one end data is pushed and at the other end data is received. In most of the cases, the order is preserved. Sometime, during the connection establishment phase, a NEGOTIATION is employed (for establishing some parameters of the connection)
CONNECTION-LESS SERVICE – modeled after the postal system. Each message (letter) carries the full destination address, each one being routed through the system independent of the others. It is possible that the messages will arrive at the destination in out of order.
Each service is characterized by QUALITY OF SERVICE. Some services are reliable in the sense that they never loose data. Usually, reliability is implemented with acknowledgements from the receiver that it received data. This introduces overhead and delays in the communication, which sometime is OK, but sometime is not (in real time voice and video communication).

## Slide 31: Service Primitives (1)
A Service is formally specified by a set of primitives
Five service primitives for implementing a simple connection-oriented service.
Notes: <number>
Primitives are available to the user process to access the service. These primitives tell the service to perform some action or report on some action taken by the peer entity. If the protocol stack is located in the operating system, those primitives are usually system calls. These calls cause a trap in the kernel mode, which then turns control of the machine over to the operating system to transfer the necessary packets.
The set of primitives are different from service to service. Fundamentally, the primitives for connection oriented services are different from primitives of connection less services. The table above presents a minimum set of primitives to provide a connection oriented reliable byte stream service.

## Slide 32: Service Primitives (2)
Packets sent in a simple client-server interaction on a connection-oriented network.

## Slide 33: Services to Protocols Relationship
Service – set of primitives (operations) that a layer provides to the layer above it; relate to the interfaces between layers
Protocol – set of rules governing the format and meaning of packets exchanged by peer entities within a layer; relate to the packets that are sent between peer entities between different machines

## Slide 34: Reference Models
The OSI Reference Model
The TCP/IP Reference Model
A Comparison of OSI and TCP/IP
A Critique of the OSI Model and Protocols
A Critique of the TCP/IP Reference Model

## Slide 35: OSI Reference Model (1)
OSI (Open Systems Interconnect) – Network architecture based on a proposal developed by ISO (International Standards Organization) to standardize the protocols used in various layers
Notes: <number>
Design principles that arrived to seven layer design are as follows:
A layer should be created where a different abstraction is needed
Each layer should perform a well defined function
The function of each layer should be chosen with an eye toward defining internationally standardized protocols
The layer boundaries should be chosen to minimize the information flow across the interfaces
The number of layers should be large enough to avoid throwing together separate, distinct functions out of necessity and small enough to avoid inefficiency

## Slide 36: OSI Reference Model (2)
Physical Layer
  Transmitting raw bits over communication channel
  Typical questions that are addressed:
    How many volts used to represent a “1” and how many for “0”
    How many nanoseconds a bit last
    Full duplex transmission or not (both directions)
    How initial connection is established and how is torn down when both sides are finished
    How many pins the network connector will have and what is each pin used for
  Design issues – sending one bit “1” on one side has to get in the other side as “1” not as “0”
    Mechanical, electrical and timing interfaces
    Physical transmission medium

## Slide 37: OSI Reference Model (3)
Data Link Layer
  Transform the raw transmission facility (offered by the physical layer) into a line that appears free of undetected transmission errors to the network layer
  Design issues
    Error detection and correction
      The sender breaks up the input data into data frames (typically a few hundred or thousands bytes) and transmits the frames sequentially. If the service is reliable, the receiver has to confirm the correct receipt of each frame
    Flow control – keep a fast transmitter drowning a slow receiver with data
      Some traffic regulation mechanism is often needed to let the transmitter know how much buffer space the receiver has at the moment. Usually, this is integrated with the error handling mechanism
    Broadcast networks have an additional issue in the data-link layer: how to control access to the shared channel. A special sub-layer of the data-link layer, the medium access control sub-layer deals with this problem

## Slide 38: OSI Reference Model (4)
Network Layer
  Controls the operation of the subnet
  Design issues
    Routing - how packets are routed from source to destination
    Congestion control – if too many packets are present in the subnet at the same time
    Allow heterogeneous networks to be interconnected
    In broadcast networks, the routing problem is thin or non existent

## Slide 39: OSI Reference Model (5)
Transport Layer
  Accepts data from the above layer, split it into smaller units and pass them to the network layer. Ensures that those pieces arrive correctly at the other end
  Determines what type of service to provide
    Most popular type of transport connection is error free, point to point channel that delivers messages or bytes in the order in which they were sent
    Other type of transport services: delivering datagrams with no guarantee about the order of delivery, broadcasting messages
  It is a true end-to-end layer, all the way from source to the destination
Notes: <number>
The Transport layer has to perform its function in a way that isolates the upper layers from the inevitable changes in the hardware technology
Layers one to three are chained, while layers four to seven are END to END layers.

## Slide 40: OSI Reference Model (6)
Session Layer
  Allows users on different machines to establish sessions between them
  Sessions offer different services:
    Dialog control – keeping track of those whose turn is to transmit
    Token management – preventing two parties from attempting same critical operation at the same time
    Synchronization – marking long transmissions to make sure they can be resumed from where they were when a crash happened

## Slide 41: OSI Reference Model (7)
Presentation Layer
  It is not concerned with moving bits around, but with checking the syntax and semantics of data that is being moved by the layers below
  In order to make it possible for computers with different data representations to communicate, the data structures to be exchanged can be defined in an abstract way, along with an standard encoding to be used on the wire.
  It manages these abstract data structures and allows higher-level data structures to be defined and exchanged

## Slide 42: OSI Reference Model (8)
Application Layer
  The application layer contains a number of different protocols and applications that are needed by the users.
  A good example of widely used application protocol is HTTP (HyperText Transfer Protocol), which is the basis for Wide World Web distributed system.
  When a browser wants a page, it sends the name of the page, to a web server, using HTTP protocol
  Other application: FTP, e-Mail, news, etc…

## Slide 43: TCP/IP Reference Model (1)
Used by Internet, packet switching network (of networks) based on a connectionless internetwork layer
Notes: <number>

## Slide 44: TCP/IP Reference Model (2)
Internet Layer
  Permits the hosts to inject packets into any network and have them travel independently to the destination (potentially using different paths or networks). The packets may arrive in a different order. It is the job of the higher layer to rearrange them
  It defines an official packet format and protocol, called IP (Internet Protocol). The job of internet layer is to deliver IP packets where they want to go
    Packet routing is one of the biggest issues
    Avoiding congestion is another big issue
Notes: <number>
Analogy with the snail mail system

## Slide 45: TCP/IP Reference Model (3)
The Transport Layer
  Designed to allow peer entities on the source and destination to carry on a conversation
  Two end to end protocols: TCP and UDP
    Transmission Control Protocol – end to end reliable connection oriented protocol that allows a byte stream originating from one machine to be delivered with no error on another machine in the Internet
    User Datagram Protocol – unreliable connectionless protocol for applications that don’t want TCP’s sequencing flow control and want to provide theirs (or to apps that don’t want connection overhead)

## Slide 46: TCP/IP Reference Model (3)
Application Layer – contains all the high level protocols: Telnet, file transfer, e-mail, domain name system, etc…

## Slide 47: TCP/IP Reference Model (3)
Host to Network Layer
  Below the Internet Layer, in TCP/IP reference model is a great void
  The model doesn’t say much about it, except that the host has to connect to the network using some protocol, so it can send IP packets to it
  This protocol is not defined and varies from host to host and from network to network

## Slide 48: Comparing OSI and TCP/IP (1)
Concepts central to the OSI model
  Services
  Interfaces
  Protocols
TCP/IP model didn’t make a clear distinction between services, interfaces and protocols
Notes: <number>
We are only comparing the models, not the corresponding protocol stacks. Both OSI and TCP/IP models have much in common. Both are based on a concept of a stack of independent protocols. Also the functionality of the layers is somehow similar.
OSI has three concepts that are central, and perhaps the biggest contribution of OSI was to make the explicit distinction between the three concepts:
SERVICES – tells what the layer does, not how entities above it access it, nor how the layer works. It defines the layer’s semantics.
INTERFACES – tells the processes above it how to access it. It specifies what the parameters are and what result to expect. It says nothing about how the layer works inside.
PROTOCOLS – are peer layers own business. A layer can use any protocol as long as it gets the job done (provides the offered services). The protocols can change without affecting the software in the higher layer.
TCP/IP Model did not originally make a clear distinction between services, interfaces and protocols. People have tried to retrofit after the specifications, to make it look more like OSI. I.e. the only real services offered by the IP layer are: SEND_IP_PACKET and RECEIVE_IP_PACKET. As a consequence, protocols in OSI model are better hidden than in TCP/IP model and can be replaced a lot easier (as the technology changes), without disturbing the layers above.

## Slide 49: Comparing OSI and TCP/IP (2)
OSI reference was described before the protocols were invented
  It means that the model is not biased towards a set of protocols, but is rather generic
  Downside is that designers didn’t have much experience (what function to put in which layer)
TCP/IP protocols came first. The model was done just as a description of the protocols
  The protocols did fit perfectly the model
  The problem was that the model didn’t fit any other protocols, useless to describe other types of networks than TCP/IP based.

## Slide 50: Comparing OSI and TCP/IP (3)
OSI has 7 layers, TCP/IP has only 4 layers
Connection less vs. connection oriented communication
  OSI model – supports connection less and connection oriented services at the network layer, while at transport layer supports only one type of connection oriented service
  TCP/IP model – supports only connection less services at the network layer, while at the transport layer offers both connection oriented and connection less services, giving the users a choice

## Slide 51: A Critique of the OSI Model and Protocols
Why OSI did not take over the world
  Bad timing
  Bad technology
  Bad implementations
  Bad politics

## Slide 52: Bad Timing
The apocalypse of the two elephants.
Notes: <number>
Standards have to be written between the research phase and investment phase. With OSI didn’t happen. Partially because the two phases were too close, partially because the competing TCP/IP model was already used in the research institutions, and companies already started to offer TCP/IP based products.

## Slide 53: Bad Technology
Two of the layers in OSI were nearly empty (session and presentation) while two others were overcrowded (network and data-link)
The protocols and service definitions are very complex. They were almost incomprehensible.
Some of the functions (such as addressing, flow control and error control) reappear again and again at different layers. This is unnecessary and inefficient

## Slide 54: Bad Implementation
Given the complexity of the protocols, the implementations were huge and inefficient
People started to associate OSI with poor quality because the implementations were slow
In contrast, one of the first implementations of TCP/IP was part of Berkeley UNIX and was quite good (also free). People begun to use it -> improvements -> large community -> more improvements

## Slide 55: Bad Politics
OSI was created by European Telecommunications ministries and USA Government – this has been seen (perceived) as a bunch of bureaucrats trying to push an inferior standard on the throats of researchers and scientists, that already had a working solution (TCP/IP)
Of course, this was only partially true, but enough for TCP/IP model to get a lot of supporters

## Slide 56: A Critique of the TCP/IP Reference Model
Problems:
  Service, interface, and protocol not distinguished
  Not a general model
  Host-to-network “layer” not really a layer
  No mention of physical and data link layers
  Minor protocols deeply entrenched, hard to replace

## Slide 57: Example Networks
The Internet (internetwork implementing TCP/IP protocol stacks with various types of underlying networks – ETH, WiFi, TokenRing, etc..)
Ethernet LANs: 802.3
Wireless LANs: 802:11

## Slide 58: Network Standardization
Telecommunications World
  ITU (International Telecommunication Union)
    Radiocommunication Sector (ITU-R)
    Telecommunications Standardization Sector (ITU-T)
    Development Sector (ITU-D)
International Standards World
  ISO (International Standards Organization)
    ANSI (American National Standards Institute), BSI (British Standards Institute), etc…
  IEEE (Institute of Electrical and Electronics Engineers)
    i.e. IEEE 802 group standardize LAN standards
Internet Standards World
  ITB (Internet Architecture Board)
    RFC (Request for comments) for different standards
  Got divided into:
    IRTF (Internet Research Task Force)
    ITEF (Internet Engineering Task Force)

## Slide 59: References
Andrew S. Tanenbaum – Computer Networks, ISBN 0-13-066102-3