## Slide 1: CT542 – Host to Netowork
Ethernet, WiFi, Token Ring
Notes: <number>

## Slide 2: Contents
Ethernet
  Classical Ethernet (cabling, encoding, frame format, channel access protocol)
  Switched Ethernet
  Fast Ethernet
  Gigabit Ethernet
Wireless LANs
Notes: <number>
This presentation deals with broadcast networks and their protocols.

## Slide 3: Ethernet
Architecture of the original Ethernet.
Notes: <number>
Initially the transmission medium was a thick coaxial cable. Latter on, it has been replaced with thin coax and UTP cabling. It was using a transmission schema called CSMA/CD (CARIER SENSE MULTIPLE ACCESS/COLLISION DETECTION). Each computer listens to the medium before transmitting. If the medium is busy, it will hold transmission until the cable Is not busy.
If two or more computers start transmission at the same time, collision will happen. The machines are able to detect collision and will retry latter in time. The algorithm is known as EXPONENTIAL BACK OFF ALGORITHM. If a second collision will happen, the random time is doubled and so on. Ethernet become IEEE 802.3 (with two minor changes), in 1983.
Initial Ethernet allowed for cable segments up to 500 meters. One network could have five segments, interconnected by repeaters (four repeaters, connecting 5 X 500m segments results in a maximum length of 2.5 KM). The speed was 10Mbps.
Ethernet continued to develop and is still developing. Data rates of 100Mbps, 1Gbps and recently 10Gbps have been achieved. Cabling has improved, switching has been added, etc.
Other types of LANS do exist. Token Bus (802.4) and Token Ring (802.5) have been also standardized.

## Slide 4: Ethernet Cabling
The most common kinds of Ethernet cabling.
Notes: <number>
10Base5 or Thick Ethernet. Connections onto the cable are done using some vampire taps.
10 represents the speed
Base represents the transmission method (base or broadband)
5 represents the maximum length of a single, non amplified sector (500 meters or 200 meters).

## Slide 5: Ethernet Cabling (2)
Three kinds of Ethernet cabling.
(a) 10Base5, (b) 10Base2, (c) 10Base-T.
Notes: <number>
In 10Base5 the transceiver and the interface board are separated. The interface board goes inside the computer, while the transceiver goes on the cable (close to the vampire tap). The transceiver contains the electronics that handle the collision detection.
In 10Base2, the connection to the cable is just a passive BNC T junction. The transceiver electronics are situated onto the controller board (inside the PC).
In 10BaseT there is no shared cable at all, just the hub. Each station is connected to the hub, using a dedicated, non shared cable.

## Slide 6: Ethernet Cabling (3)
Cable topologies. (a) Linear, (b) Spine, (c) Tree, (d) Segmented.
Notes: <number>
Each version of Ethernet has a maximum cable length per segment. To allow larger networks, multiple cables can be connected by repeaters. A repeater is a physical layer device. It just amplifies and restores the shape of the digital signals, in both directions.
A system may contain multiple cable segments and multiple repeaters, but no two transceivers can be more than 2.5 KM away. No path between any two transceivers may traverse more than four repeaters.
A linear cable running through the building with stations tapped onto it
A spine cable running from top of the building to the basement, with each floor connected onto it through repeaters
Tree cable topology, using hubs. Most used
Multiple cables connected by repeaters, to allow for larger networks.

## Slide 7: Ethernet Cabling (4)
(a) Binary encoding, (b) Manchester encoding, (c) Differential Manchester encoding.
Notes: <number>
None of Ethernet variants use binary encoding with 0V for a 0 and 5V for a 1, since it leads to ambiguities on the bus. IF one station sends the bit string 00010000 others might falsely interpret it as 10000000 or 01000000 or other combinations, because they cannot tell the difference between an idle sender (0V) and a 0 bit (0V).
To overcome this, +1V could be used for 1 and -1V for 0, but we still have the problem of synchronization between the sender and the receiver, where different clock speeds could get the receiver and the sender to desynchronize.
Manchester encoding (two variants) provides a way of precisely determine the start, end or middle of each bit without reference to an external clock.
MANCHESTER ENCODING (b) ensures that every bit has a transition in the middle, making it easy for the receiver to synchronize with the sender:
each bit period is divided into two equal intervals
A binary 1 is sent by having the voltage set high during the first interval and low in the second one
A binary 0 is sent by having the voltage set low during the first interval and high in the second one
A disadvantage of Manchester encoding is that it needs twice as much bandwidth as binary encoding, because the pulses are half the width.
DIFERENTIAL MANCHESTER ENCODING:
A binary 1 is indicated by an absence of a transition at the beginning of the interval
A binary 0 is indicated by the presence of a transition at the starting of the interval
In any case, there is a transition in the middle as well, to help the receiver synchronize its clock.
Ethernet is using Manchester encoding. Differential Manchester encoding is used by Token Ring.

## Slide 8: Ethernet MAC Sublayer Protocol (1)
Frame formats. (a) DIX Ethernet, (b) IEEE 802.3.
Each frame starts with Preamble of 8 bytes, each containing the bit pattern 10101010. The Manchester encoding on this pattern produces a 10MHz square wave for 6.4 us to allow the receiver's clock to synchronize with the sender. The clock will stay in sync for the rest of the frame, using the transitions in the middle of the bit boundaries for adjustment.
IEEE 802.3 is using a 7 bytes preamble and 1 byte start of frame (SOF)
Frame continues with two address fields. 6 byte addresses for destination and source are used. The high order bit is 0 for normal addresses and 1 for group addresses. The address with all 1 is reserved for broadcast. Second high order bit is 1 if the address is local or 0 if the address is global.
46 bits available for address space (about 70T unique addresses are possible). The idea is that any station can address other station by giving the 48 bit number
Type field in DIX: - tells to the receiver what to do with the frame. Multiple network protocols could be supported. So this field is unique for each network protocol. It is used to dispatch the incoming frames.
IEEE 802.3 changed the type field in Length field – the type is handled as part of the data itself, in a small header. The length field contains the length in bytes of the data, up to 1500 bytes.
Data, up to 1500 bytes. This limit was chosen arbitrarily at the time DIX was released. It was based on the fact that a transceiver needed enough RAM to hold an entire data frame and RAM was expensive back in 1978.
There is also a minimum frame length, related to the collision detection. The explanation is given in the next slide. The minimum Ethernet frame length is 64 bytes (without the preamble), and if the data portion is less than 46 bytes (64 – headers + checksum) then the PAD field is used to fill the frame to the minimum size.
Checksum is a 32 bit hash code of the data, computed with a CRC algorithm, having a 32 order generator polynomial. It just does error detection, no forward error correction.
Notes: <number>
There are two variants of Ethernet. The initial one (DIX, initiated by Xerox, Intel and DEC) and the IEEE 802.3 standard. The differences are minor and they are interoperable.
Each frame starts with Preamble of 8 bytes, each containing the bit pattern 10101010. The Manchester encoding on this pattern produces a 10MHz square wave for 6.4 us to allow the receiver's clock to synchronize with the sender. The clock will stay in sync for the rest of the frame, using the transitions in the middle of the bit boundaries for adjustment.
Ethernet addresses:
High order bit distinguishes between normal and group addresses (1 for group, 0 for normal) (allow multiple stations to listen to one address, when a frame is sent to a group address, all the stations in that group receive it).
Second high order bit distinguishes between local and global addresses (1 for local, 0 for global)
All 1 is reserved fro broadcast address.
Type field in DIX: - tells to the receiver what to do with the frame. Multiple network protocols could be supported. So this field is unique for each network protocol. It is used to dispatch the incoming frames.
IEEE 802.3 changed the type field in Length field – the type is handled as part of the data itself, in a small header. The length field contains the length in bytes of the data, up to 1500 bytes.
Data, up to 1500 bytes. This limit was chosen arbitrarily at the time DIX was released. It was based on the fact that a transceiver needed enough RAM to hold an entire data frame and RAM was expensive back in 1978.
There is also a minimum frame length, related to the collision detection. The explanation is given in the next slide. The minimum Ethernet frame length is 64 bytes (without the preamble), and if the data portion is less than 46 bytes (64 – headers + checksum) then the PAD field is used to fill the frame to the minimum size.
Checksum is a 32 bit hash code of the data, computed with the CRC algorithm presented in the Data Link Layer, having a 32 order generator polynomial. It just does error detection, no forward error correction.

## Slide 9: Ethernet MAC Sublayer Protocol (2)
Notes: <number>
The strongest reason why there is a minimum length for the Ethernet frame is to allow the CSMA/CD protocol to work properly. In other words, the collisions should be detected by the transmitting station, or preventing a transmitting station to finish the transmission of a frame until the first bit reached the far end of the cable, where it may collide with another frame.
If we have a collision an time t, the station B (that detected the collision first) issues a 48 bit noise burst (known as jam signal) to warn the other stations. At about 2t time, the sender (station A) will see the noise burst and aborts its transmission too. It waits a random time until it tries again.
For a 2500 meters LAN with 4 repeaters, the round trip time (the propagation time for a signal to travel from one end of the LAN to the other end of the LAN and back) is about 50us. That is equivalent to about 500 bit times (one bit time for 10Mbps network is 100ns). Therefore, a station should be in transmit mode for at least 500 bit times, which gives us the minimum Ethernet frame of about 500 bits. The standard’s choice was 512 bits or 64 bytes minimum frame.
So frames with fewer than 64 bytes will be padded out to 64 bytes.
As the network speed goes up, the minimum frame length goes up too.

## Slide 10: Binary Exponential Backoff Algorithm
After a collision the time is divided in discrete slots (equal to worst round trip propagation, which is 512 bits time or 51.2 us)
After the first collision, each station waits 0 or 1 slot time before tries again
  If two station collide and they pick same number, they will collide again
After a second collision, each station waits 0, 1, 2 or 3 at random and waits that number of slot times.
After a third collision will happen, the next number to pick is between 0 and 23 -1 and that number of slots is skipped.
After 10 collisions have been reached, the number interval is frozen at 0 – 1023.
After 16 collisions, the station gives up to send the frame and reports the failure. Further recovery it is up to the higher layers.

## Slide 11: Switched Ethernet
Way to deal with saturated Ethernet LANs
Switch – contains a high speed backplane
  switches frames from incoming ports to destination ports
  Avoids collisions
Notes: <number>
More stations added on an Ethernet, the traffic will go up. Eventually, at one point the LAN will saturate.
Switches are typically devices that have 4 to 32 plug-in cards, each with one to 8 Ethernet connectors (RJ45). When a station wants to send an Ethernet frame, the plug-in card getting the frame will check to see if the destination address is of one of the cards connected onto one of its ports. If yes, then the packet is copied onto that port. If not, then, using a multi-gigabit per second back plane, the frame is copied to the card containing the destination port.

## Slide 12: Fast Ethernet
Approved as IEEE 802.3 u standard in 1995
Keeps all the old frame formats, interfaces and procedural rules
Reduces the bit time from 100ns to 10ns
It is based only on the 10Base-T wiring
  It is using only hubs and switches; drop cables with vampire taps and BNC connectors are not possible
It supports both UTP Cat 3 (for backwards compatibility with preinstalled infrastructure) and UTP Cat 5 cables

## Slide 13: Fast Ethernet - Cabling
The original fast Ethernet (802.3u) cabling.
Notes: <number>
Anyone who understands classic Ethernet already understands much about Fast Ethernet. Fast Ethernet uses the same cabling and access method as 10Base-T. With certain exceptions, Fast Ethernet is simply regular Ethernet, just ten times faster.
Probably the most popular form of Fast Ethernet is 100BASE-TX. 100BASE-TX runs on UTP Category 5 unshielded twisted pair, sometimes called UTP-5. It uses the same pair and pin configurations as 10Base-T, and is topologically similar in running from a number of stations to a central hub.
As an upgrade to 10Mbps Ethernet over Multimode fiber (10Base-F), 100BASE-FX is Fast Ethernet over fiber. Distances up to 2km are supported.
Fast Ethernet is possible on Category 3 UTP with 100BASE-T4. There is a popular misconception that Fast Ethernet will only run on Category 5 cable. That is true only for 100BASE-TX. If you have Category 3 cable with all four pairs (8 wires) connected between station and hub, you can still use it for Fast Ethernet by running 100BASE-T4.
100BASE-T4 sends 100Mbps over the relatively slow UTP-3 wire by fanning out the signal to three pairs of wire. This "demultiplexing" slows down each byte enough that the signal won't overrun the cable. Category 3 cable has four pairs of wire, eight wires total, running from point to point. 10Base-T only uses four wires, two pairs. Some cables only have these two pairs connected in the RJ-45 plug. If the category 3 cabling at your site has all four pairs between hub and workstation, you can use Fast Ethernet by running 100BASE-T4.

## Slide 14: Fast Ethernet – 100Base-TX (1)
Is using only two pairs out of the 4 available in the UTP cable (one for transmit and one for receive)
For 100 Mbps, the waveform frequency would peak at 50MHz, while with Manchester encoding would pick at 100MHz
  Category 5 UTP is only rated at 100MHz, so Fast Ethernet would be difficult to implement using Manchester encoding
100BASE-TX uses two encoding techniques:
  4B/5B coding schema is used to avoid loss of synchronization
  To decrease the frequency on UTP cable, MLT-3 (Multiple Level Transition - 3 levels) encoding is used
Notes: <number>
The primary difficulty with 100 Mbps transmission of data is that high-frequency signals don't propagate well over either twisted pair or fiber. 10 Mbps Ethernet uses Manchester encoding to include a clock signal with every data bit. However, the clocking almost doubles the rate of transmission, so a worst-case scenario would transmit 10Mbps of data with a 10MHz waveform. For 100 Mbps, the waveform frequency would peak at 100MHz. Category 5 UTP is only rated at 100MHz, so Fast Ethernet would be difficult to implement.
100BASE-FX uses NRZI (Non-Return-to-Zero, Invert-on-one). To decrease the frequency even further on UTP, 100BASE-TX adds a variation of NRZI at the PMD sub-layer called either MLT-3 (Multiple Level Transition - 3 levels) or NRZI-3.

## Slide 15: Fast Ethernet –100Base-TX (2)
In order to send information using 4B5B encoding, the data byte to be sent is first broken into two nibbles.
  If the byte is 0E, the first nibble is 0 and the second nibble is E.
Next each nibble is remapped according to the 4B5B table
  Hex 0 is remapped to the 4B5B code 11110.
  Hex E is remapped to the 4B5B code 11100.
The 4B5B replacement happens at the Physical layer, followed by MLT-3 encoding
4B5B Encoding Table:
Data | Binary | 4B/5B code
0 | 0000 | 11110
1 | 0001 | 01001
2 | 0010 | 10100
… |  | 
E | 1110 | 11100
F | 1111 | 11101

## Slide 16: Fast Ethernet –100Base-TX (3)
MLT-3 (Multiple Level Transition) encoding
It is using three voltage levels: +1V, 0V and -1V
Encodes a bit as a presence or lack of transition
  1 encoded as a presence of transition
  0 as a lack of transition
Notes: <number>
MLT-3 encodes a bit as presence or lack of transition, exactly as in NRZI. What makes MLT-3 different is that the base waveform is a 3-state alternating wave. Rather than alternating between 0 and 1 as in Manchester encoding and NRZI, MLT-3 alternates from -1 to 0 to +1, back to 0, then back to -1, repeating indefinitely. A zero is encoded as a halt in the back-and-forth progression. It may be useful to think of MLT-3 as a stop-and-go sine wave, encoding 0 as stop and 1 as go. Using MLT-3, it is therefore possible to represent four or more bits with every complete waveform, at 0, +1, 0, and -1
With 4B/5B encoding, the data rate of the cable goes up to 125Mb. After the MLT-3 encoding the base frequency of the encoded signal goes down by 4 (due to the way the encoding works), therefore the signal that is transmitted over the cable will have a maximum frequency component of about 31.25Mhz, which is handled very well by the UTP5 cable.
The data being transmitted in this example is the hexadecimal byte "0E". First, the byte is broken down into four bit "nibbles", giving a nibble of "0" and a nibble of "E". Then, each nibble is looked up in a table to find the byte code associated with that hexadecimal number. The code for "0" hex is "11110" and the code for "E" hex is "11100". Finally, the byte codes are transmitted onto the wire using MLT-3 encoding.

## Slide 17: Fast Ethernet – 100Base-TX (4)
Why 4B/5B encoding before MLT-3?
  MLT-3 solve the problem of slowing down the data frequency but it presents the risk of losing clock-signal encoding.
  A steady stream of zeros, not uncommon in data, would be represented MLT-3 as a total lack of transitions. With no transitions, the receiving station has no clear incoming signal. With no incoming signal, the receiving station can’t recover the clock signal.
  If enough drift is introduced into the perceived clock, the station can perceive false data from the data stream.
  To combat this problem, data is first encoded using 4B5B translation, replacing every 4 bits of data with a 5-bit code specified in 802.3u. Every possible 4-bit pattern is assigned a 5-bit code. Instead of sending the actual 4 bits across the wire, the 5-bit code is transmitted.
  The used combinations are carefully chosen to provide enough transitions so the clock synchronization can be maintained

## Slide 18: Fast Ethernet – 100BaseT4
Is using all 4 pairs available in the UTP Cat 3 cable (one for transmit, one for receive and two that are switch-able with the data flow)
Cat 3 UTP cable can handle only about 16MHz signal
  With encoding techniques used over Cat 5 cable, this is not enough to carry 31.25MHz signal.
It is using a coding technique known as 8B/6T

## Slide 19: Fast Ethernet – 100BaseT4 (2)
In order to send information using 8B6T encoding, the value of the data byte is converted to the values in the 8B6T table.
  Every possible byte has a unique 6T code, a set of 6 tri-state symbols.
  Unlike 4B5B, 8B6T completely prepares the data for transmission; no further encoding is required.
100BASE-T4 is currently the only technology which uses 8B6T encoding. It performs 8B6T encoding at the Physical layer.
100BASE-T4 then de-multiplexes the 6T codes onto three wire pairs.

## Slide 20: Fast Ethernet – 100BaseT4 (3)
8B6T encoding replaces each 8-bit byte with a code of only 6 tri-state symbols.
  To represent 256 different bytes (28 combinations), 729 tri-state symbols are possible (36 combinations).
  Unlike MLT-3, no progression from 1 to 0 to -1 is required: 8B6T allows an arbitrary use of these three states. 256 symbols have been chosen as a one-to-one remapping of every possible byte, similar to 4B5B.
  The remapping table is listed in IEEE 802.3u standard, and an example is presented here:
Data (hex) | Binary | 8B/6T code
0x00 | 0000 0000 | +-00+-
1x01 | 0000 0001 | 0+-+-0
… | … | …
0x0E | 0000 1110 | -+0-0+
… | … | …
0xFF | 1111 1111 | +0-+00

## Slide 21: Fast Ethernet – 100BaseT4 (4)
The fastest waveform required in 8B6T is alternating extreme states, +1 to -1, encoding two tri-state symbols in a single wavelength. Unlike 4B5B, the carrier wave frequency only needs to be 3/4 the speed of the bit stream, as only 6 signals are used to communicate 8 bits.
The fastest possible waveform base frequency is 37.5MHz (3/4 * 50MHz – max base frequency in a binary signal for a 010101… pattern), which is still too fast for UTP-3, so one more technique is needed – de-multiplexing data on three separate channels
The final slowdown in 8B6T comes from fanning the transmitted signal out to three cable pairs instead of a single pair. This is called "T4 Multiplexing"
The maximum speed waveform required is now only 12.5 MHz, slow enough for even Category 3 twisted pair (which has a limit of 16MHz).

## Slide 22: Fast Ethernet – 100BaseT4(5)
Data is transmitted by the Ethernet card and de-multiplexed out onto three pairs of the Category 3 Cable.
Bytes are multiplexed at the receiving end and placed back in the correct order. The fourth pair of the wire is used for collision detection.
In this way, each wire only has to carry 33.3 Mbps, for an aggregate throughput of 100 Mbps. This is how 100 Mbps Ethernet can run on Category 3 unshielded twisted-pair cable

## Slide 23: Fast Ethernet – 100BaseFX (1)
Is using optical fiber
100BASE-FX uses two encoding techniques:
  4B/5B coding schema is used to avoid loss of synchronization
  NRZI (Non-Return-To-Zero, Invert-on-one) encoding is used
The distance between a station and a hub can be up to 2 KM.

## Slide 24: Fast Ethernet – 100BaseFX (2)
NRZI uses the presence or absence of a transition to signify a bit
  indicating a logical 1 by inverting the state and a 0 by maintaining the state.
NRZI uses a half-wave to encode each bit (having a better usage of the bandwidth)
  Rather than transition through ground at each bit like Manchester encoding,
Notes: <number>
The data being transmitted in this example is the hexadecimal byte "0E". First, the byte is broken down into four bit "nibbles", giving a nibble of "0" and a nibble of "E". Then, each nibble is looked up in a table to find the byte code associated with that hexadecimal number. The code for "0" hex is "11110" and the code for "E" hex is "11100". Finally, the byte codes are transmitted onto the wire using NRZI encoding.

## Slide 25: Gigabit Ethernet (1)
IEEE 802.3z approved in 1998
All configurations are point to point rather than multidrop as in classical Ethernet
Supports two modes of operation:
  Full Duplex mode (the normal mode of operation)
    All the stations are connected through a switch that allows traffic in both directions at the same time
    CSMA/CD is not employed anymore
    Max cable length is governed by propagation issues
  Half duplex mode
    All stations are connected through a hub, that internally electrically connects all the lines, simulating a multidrop environment as with classic Ethernet electrically connects all the lines
    CSMA/CD protocol is required
    Max cable length is still governed by CSMA/CD protocol
Notes: <number>
It supports two modes of operation:
  Full Duplex mode
    All the stations are connected through a switch that allows traffic in both directions at the same time
    Since all possible connections are point to point, the CSMA/CD protocol is not employed anymore
    Since on the line between the computer and the switch, no other devices are present
    The max length of the cable is now governed by signal propagation issues rather than the round trip propagation
  Half duplex mode
    All stations are connected through a hub, that internally electrically connects all the lines, simulating a multidrop environment as with classic Ethernet electrically connects all the lines

## Slide 26: Gigabit Ethernet (2)
Half Duplex Mode Max Cable length extended using:
  Carrier extension
    Hardware adds its own padding to extend the frame to 512 bytes; since this padding is added by sending hardware and removed by the receiving hardware, the software is not aware of it
  Frame Bursting
    Allows the sender to transmit a concatenated sequence of multiple frames in one single transmission; if the total length of burst is less then 512 bytes, the hardware pads it again.
Those techniques extend the radius of the network to 200 meters
Notes: <number>
Since 25 meters is not an acceptable radius (to maintain the minimum 64 bytes frame), two methods have been adopted by the standards committee:
Carrier extension
Frame bursting

## Slide 27: Gigabit Ethernet (3)
A two-station Ethernet. (b) A multi-station Ethernet

## Slide 28: Gigabit Ethernet (4)
Gigabit Ethernet cabling.

## Slide 29: Wireless LANs (1)
(a) Wireless networking with a base station.
(b) Ad hoc networking.
Notes: <number>
802.11 is the standard for wireless LAN and it is an IEEE standard, released in 1997. A common marketing name for it is WIFI.
It works in the presence of a base station (called access point) or in absence of a base station (peer to peer mode or ad hoc networking).

## Slide 30: Wireless LANs (2)
The range of a single radio may not cover the entire system.
Notes: <number>
HIDDEN NODE PROBLEM – CSMA/CD from Ethernet doesn’t work so well in wireless. So 802.11 had to solve this problem with a transmission schema called CSMA/CA (CARRIER SENSE MULTIPLE ACCESS/COLLISION AVOIDANCE).
MULITPATH FADING – effects caused by reflection of the signal, and as result, the receiver will get same signal a few times (delayed in time).
ROAMING – ability of mobile computers to change access from one base station to another, as they move along

## Slide 31: Collision-Free Protocols (1)
The basic bit-map protocol.
If station j has a frame to send, it will transmit a 1 in j-th contention slot
Notes: <number>
Each contention period consists of exact N slots. If station 0 has a frame to send, then it transmits a slot during zero-th contention slot. No other station is allowed to transmit during this slot. Regardless of what station 0 does, station 1 gets the opportunity to transmit a 1 bit during the contention slot 1, but only if it wants to send a frame (has a queued frame).
After all N slots have passed, each station has complete knowledge of which stations whish to transmit. Al that point they begin transmitting in numerical order. Since everyone agrees who goes next, there is no collisions.
Protocols like this are called RESERVATION PROTOCOLS.

## Slide 32: Collision-Free Protocols (2)
The binary countdown protocol. A dash indicates silence.
Notes: <number>
A problem with bit map protocols is that the overhead per station is fixed (on bit), therefore it is not scaling well with large number of stations.
In binary countdown protocol, all stations will have same length addresses. A station wanting to use the channel broadcasts its address as a binary bit string, starting with the high order bit. The bits in each address position, from each station are BOOLEAN OR-ed together. This is called binary countdown. All the stations will see the result of the OR operation instantaneously. So an station that placed an 0 on the channel sees a 1, than it will stop trying. A higher priority station wants to transmit therefore it has to stop trying this time.
In other words, as soon as a station has seen that a high order bit in its address with value 0 has been overwritten with a 1, it gives up.
Consider the stations 0010, 0100, 1001 and 1010 are all trying to get the channel. Station having address 1010 gets the channel (due to the fact that this protocol is giving priority to the stations with higher address).

## Slide 33: Wireless LAN Protocols (1)
A wireless LAN. (a) A transmitting. (b) B transmitting.
Notes: <number>
CSMA doesn’t work because of the hidden station problem.
It is important to realize that in a wireless LAN system not all stations are within the range of the others. Due to this, HIDDEN STATION PROBLEM can occur (when A transmits, C can’t sense it and it can transmit too … the frame from A to B gets garbled if C decides to transmit at the same time). Therefore a simple CSMA approach will not work for wireless LANs.
EXPOSED STATION PROBLEM can also occur (the reverse situation – B transmits to A. If C senses the medium, it will hear an ongoing transmission and falsely conclude that may not send to D, when in fact such transmission would cause bad reception only in regions between B and C.
In conclusion, before starting a transmission, a station wants to know if there is activity around the receiver.

## Slide 34: Wireless LAN Protocols (2)
The CSMA/CA protocol. (a) A sending an RTS to B.
(b) B responding with a CTS to A.
Notes: <number>
CSMA/CA (Carrier Sense Multiple Access with Collision Avoidance) – the sender stimulates the receiver to output a short packet, so the stations around it will hear it and understand to avoid transmission during the upcoming (large) data frame.
In this slide we have station A wanting to send data to station B. A short exchange of packets RTS (Request to Send) and CTS (Clear To Send) takes place. RTS (short frame, less than 30 bytes) contains the length of the data that is about to be transferred (data frame). This data is copied also into the CTS frame by the receiver.
When A receives the CTS frame, it begins the transmission of the data frame.

## Slide 35: WMACA
Improved MACA by adding:
  ACK after each successful data frame
  Added carrier sensing in the eventuality that two given nearby stations wanted to send RTS packets to same destination.
  Run the back-off algorithm per each data stream (source-destination pair) rather than for each station
  Added mechanisms to deal with congestion

## Slide 36: Wireless LANs (3)
A multicell 802.11 network (ETH & WiFi).
Notes: <number>
Roaming between base stations of the same network.

## Slide 37: References
Andrew S. Tanenbaum – Computer Networks, ISBN 0-13-066102-3