## Slide 1: The Network Layer
CT542

## Slide 2: Content
Network Layer Functions (Context of the operation of network layer protocols, Services provided to the transport layer, Connectionless Services, Connection oriented services)
Networking Devices (Repeaters, Bridges, Routers, Gateways)
The Network Layer in the Internet
  The IP protocol
  IP Addressing
  IP subnet design
    CIDR (Classless InterDomain Routing)
    NAT (Network Address Translation)
  Internet Control Protocols
    ICMP (Internet Control Message Protocol)
    ARP (Address Resolution Protocol)
    RARP (Reverse Address Resolution Protocol)
    BOOTP (BOOTstrap Protocol, alternative to RARP)
    DHCP (Dynamic Host Configuration Protocol
  IPv6

## Slide 3: Network layer
It is the lowest layer that deals with end-to-end transmission
Concerned with getting packets from the source all the way to the destination
Should know about the topology of the communication subnet and choose appropriate paths through it
It should choose routes to avoid overloading some of the communication lines and routers while leaving others idle
When source and destination are in different networks, new problems occur…it is up to this layer to deal with them

## Slide 4: Network layer
An interface between the transport layer and the data link/physical layer:
  services should be independent of the router technology
    must be able to communicate across all types of network
  transport layer should not know about the subnet structure, number, type and topology of the routers present
  The network address made available to the transport layer should use a uniform numbering plan, even across LANs and WANs

## Slide 5: Network layer
Decide between:
    connectionless service – strong support by Internet community argues that the network layer should just move packets around and nothing more; the network service should be connectionless with primitives SEND_PACKET and RECEIVE_PACKET; no packet ordering nor flow control should be performed, since hosts are going to do it anyway (Internet)
    connection orientated – strong support in the telephone companies argue that network should provide reliable, connection oriented services; they saying that quality of service is the dominant factor, and without connections in subnet, it is very difficult to achieve it (ATM)

## Slide 6: Connectionless service
Packets (called datagrams) are injected into the subnet (datagram subnet) individually and routed independently
No advance setup is needed
Notes: <number>
Process P1 has a long message for P2:
Hands the message to transport layer, with instructions to move the message to process P2 on Host H2;
Transport layer code runs on H1, typically within the operating system; it adds a transport header to the front of the message and hands the result to the network layer
Network layer (probably another procedure within the operating system) will see if the message is larger than the maximum MTU … assume that the message is four times bigger than the MTU of the network layer; the network layer has to break the message into four packets and send each of them to router A using some sort of point to point protocol (i.e. PPP).
Carrier takes over the delivery:
Every router has an internal table telling it where to send packets for each possible destination
Each table entry is a pair consisting of a destination and the outgoing line to use for that destination
Only directly connected lines can be used (i.e. router A has only two outgoing lines: B and C, so every incoming packets will have to go over those lines, even if the destination is some other router)
As packets 1, 2 and 3 arrived to A, each of them will be forwarded to C (according to the initial routing table of A). Packets are then forwarded to E and then to F. When they will get to F, they will be encapsulated in a data link frame and sent to H2 over the LAN.
Packet 4 can follow a different route if A’s routing table will change. The next router in the path (according to A’s later routing table) is B, because probably A router learned that somewhere along the line, the route ACE got jam. The algorithms that manages the tables and makes the routing decisions is called routing algorithm.

## Slide 7: Connection oriented service
A path from the source router to the destination router must be established before sending any data
This connection is called VC (virtual circuit) and the subnet is called virtual circuit subnet.
Avoid having a new route for every packet sent; when a connection is established, a route from the source to the destination is chosen as part of the connection setup and stored in the tables inside the routers; when the connection is released, the virtual circuit is also terminated; each packet has an ID telling which VC belongs to.
Notes: <number>
H1 has established connection 1 with host H2. It is remembered as first entry in each of the routing tables. The first line of A’s table says that if a packet, bearing connection identifier 1, comes from H1 it is to be sent to router C and given connection identifier 1. Similarly, the first entry in C’s table routes the packet to E, also with connection identifier 1. Same happens in E router.
H3 wants to establish a connection with H2. It chooses connection identifier 1 (since it is the first connection that is initiated from host H3) and tells the subnet to establish the virtual circuit. Note that we have a conflict here because, even if A can distinguish between connection 1 from H1 and connection 1 from H3, C can’t do this anymore. For this reason, A assigns a different connection identifier to the outgoing traffic for the second connection. Avoiding conflicts of this kind is why routers need to be able to change the connection identifiers in outgoing packets. In some context, this is called label switching.

## Slide 8: Virtual Circuit vs Datagram subnets

## Slide 9: Networking devices
An internet (or internetwork) is a collection of individual networks (do not confuse with Internet, that is a worldwide network)
To create an internet we need internetworking devices called repeaters, bridges, routers and/or gateways
Those devices are acting at different layers of the OSI/TCP IP models.
Notes: <number>
When

## Slide 10: Networking devices
Repeaters – act only upon the electrical components of a signal and are therefore active only at the physical layer
Bridges – utilize addressing protocols and can affect the flow control of a single LAN; they are most active at the data link layer
Routers – provide links between two separate but same-type LANs and are most active at the network layer
Gateways – provide translation services between incompatible LANs or applications and are active in all of the layers.
Each of these internetworking devices also operates in all of the layers below the one in which it is most active

## Slide 11: The network layer in the Internet

## Slide 12: Principles that drove the design
Make sure it works – first test and then write specs
Keep it simple – fight features (leave out non essential features)
Make clear choices – if multiple ways to do same thing, choose just one
Exploit modularity – have protocol stacks
Expect heterogeneity – different types of hardware, etc..
Avoid static options and parameters – negotiate a value than define a fixed one (where absolutely needed)
Look for a good design, not need to be perfect – do a god design, don’t complicate it to handle special wired cases
Be strict when sending, tolerant when receiving – comply with the standards when sending, try to accommodate errors when receiving
Think about scalability – systems that have to use millions of users don’t accommodate well centralized databases
Consider performance and cost – a solution that is either expensive or performs poorly is not usable

## Slide 13: Internet – collection of subnets

## Slide 14: Internet Protocol (IP)
The glue that holds together the Internet
Provides a best-efforts (not guaranteed) way to transport datagrams from source to destination
Workflow:
  The transport layer takes the data streams and breaks them into datagrams (in theory they can be up to 64KB, but in practice they are no more than 1500 bytes to map naturally on the ETH payload)
  Each datagram is transmitted through the Internet (possible being fragmented into smaller pieces as it goes)
  When all pieces get to the destination machine, they are reassembled by the network layer into the original datagram
  This datagram is handed to the transport layer which inserts it into the receiving process input stream

## Slide 15: Format of the IP datagram
Versioning (keeps track of the versioning control). Currently we can have IPV4 (0100) or IPV6 (0110)
Header Length – how long the header is in 32 bit-words; the minimum value is 5, which applies when no option is present; maximum value is 15 giving a maximum of 60 bytes for the header, when options are present (thus options field is limited to 40 bytes)
Type of service – defines how the datagram should be handled; it includes bits that define priority of the datagram; it also include bits that define the type of service the sender desires, such as level of throughput, reliability and delay; most of the times, this filed is completely ignored by routers
Total length – includes everything in the datagram, both header and data; the maximum length is 65,535 bytes; at this stage, this limit is OK, but with future gigabit networks, larger datagrams may be needed
Identification – is needed to allow the destination host to determine which datagram a newly arrived fragment belongs to. All the fragments of the datagram contains the identification field.
DF – bit specifying Don’t Fragment; this is helpful for systems that can’t put back together the fragments of a datagram
MF – stands for More Fragments; all fragments except the last one have this bit set. It is needed to know when the fragments of a datagram have arrived
Fragment offset – tells where in the current datagram the current fragments belongs. All fragments, except the last one have to be multiple of 8 bytes (elementary fragment unit); since 13 bits are provided, there are a number of 8192 fragments per datagram, giving a maximum datagram length of 65536 bytes
Time to live – is a counter used to limit the packets life times; it is suppose to count time in seconds, allowing a maximum life time of 255 seconds, but in practice it counts only hops. When it hits 0, the packet is discarded and a warning packet is sent back to the host; this feature prevents datagrams from going around forever.
Protocol – tells which transport process to give it to…in other words is specifies the transport layer protocol (TCP, UDP, etc…)
Header checksum – verifies only the header; the algorithm is to add up all 16 bit half words as they arrive, using one’s complement arithmetic and then take one’s complement result; the header checksum must be computed at each hope, since there are values in the header that modifies (i.e. hops count)
Source address and destination address indicate the network number and host number; we will see next what that means;
Options – was designed to allow designers and implementers of network protocols an escape mechanism; this option value allows for subsequent version of the protocols to include information not present in the original specs; the options are variable length, each of them beginning with one byte identifying the option.
Notes: <number>
IP packet is transferred in big endian : from left to right, with the high order bit of the version control going first. All 8086 based machines are little endian, so whenever sending or receiving, a conversion is required
Versioning (keeps track of the versioning control). Currently we can have IPV4 (0100) or IPV6 (0110)
Header Length – how long the header is in 32 bit-words; the minimum value is 5, which applies when no option is present; maximum value is 15 giving a maximum of 60 bytes for the header, when options are present (thus options field is limited to 40 bytes)
Type of service – defines how the datagram should be handled; it includes bits that define priority of the datagram; it also include bits that define the type of service the sender desires, such as level of throughput, reliability and delay; most of the times, this filed is completely ignored by routers
Total length – includes everything in the datagram, both header and data; the maximum length is 65,535 bytes; at this stage, this limit is OK, but with future gigabit networks, larger datagrams may be needed
Identification – is needed to allow the destination host to determine which datagram a newly arrived fragment belongs to. All the fragments of the datagram contains the identification field.
DF – bit specifying Don’t Fragment; this is helpful for systems that can’t put back together the fragments of a datagram
MF – stands for More Fragments; all fragments except the last one have this bit set. It is needed to know when the fragments of a datagram have arrived
Fragment offset – tells where in the current datagram the current fragments belongs. All fragments, except the last one have to be multiple of 8 bytes (elementary fragment unit); since 13 bits are provided, there are a number of 8192 fragments per datagram, giving a maximum datagram length of 65536 bytes
Time to live – is a counter used to limit the packets life times; it is suppose to count time in seconds, allowing a maximum life time of 255 seconds, but in practice it counts only hops. When it hits 0, the packet is discarded and a warning packet is sent back to the host; this feature prevents datagrams from going around forever.
Protocol – tells which transport process to give it to…in other words is specifies the transport layer protocol (TCP, UDP, etc…)
Header checksum – verifies only the header; the algorithm is to add up all 16 bit half words as they arrive, using one’s complement arithmetic and then take one’s complement result; the header checksum must be computed at each hope, since there are values in the header that modifies (i.e. hops count)
Options – was designed to allow designers and implementers of network protocols an escape mechanism; this option value allows for subsequent version of the protocols to include information not present in the original specs; the options are variable length, each of them beginning with one byte identifying the option.

## Slide 16: IP Options
Security – i.e., a military router might use this field not to route through certain countries; in practice, all of the routers ignore it, so it can be used to spy easily on interesting stuff …
Strict source routing – gives the complete path from source to destination, as a list of IP address (sequence). The datagram is forced to follow that exact route; useful when routing tables are corrupted or for timing measures.
Loose source routing – requires the packet to traverse the list of routers specified, and in the specified order; it allows a pass through other routers on the way; this is useful when avoiding or force passing through certain countries (economical or political reasons)
Record route – tells the routers along the way to append their address to the option list. This allows tracking down of bugs in routing algorithms. At first, ARPANET was having at most 9 routers…so 40 bytes was plenty…but now this is too short.
Time stamp – same with the Record route option, but beside the IP address, the routers have to record also a 32 bit time stamp value; this option is mostly for debugging routing algorithms.
Notes: <number>
Security – i.e., a military router might use this field not to route through certain countries; in practice, all of the routers ignore it, so it can be used to spy easily on interesting stuff …
Strict source routing – gives the complete path from source to destination, as a list of IP address (sequence). The datagram is forced to follow that exact route; useful when routing tables are corrupted or for timing measures.
Loose source routing – requires the packet to traverse the list of routers specified, and in the specified order; it allows a pass through other routers on the way; this is useful when avoiding or force passing through certain countries (economical or political reasons)
Record route – tells the routers along the way to append their address to the option list. This allows tracking down of bugs in routing algorithms. At first, ARPANET was having at most 9 routers…so 40 bytes was plenty…but now this is too short.
Time stamp – same with the Record route option, but beside the IP address, the routers have to record also a 32 bit time stamp value; this option is mostly for debugging routing algorithms.

## Slide 17: IP Addressing
Three fields of variable sizes (dependent on the class of the address)
  Class Type field defines the class (5 possible classes that an internet address is part off)
  Network ID – up the class type, this field can be anywhere between 7 and 24 bits
  Host ID – up to the class type it can be anywhere between 8 and 24 bits
ICANN (Internet Corporation for Assigned Names and Numbers), non profit corporation that manages the assignment of IP address space to various regional authorities that deal with IP address assignment

## Slide 18: Internet Classes
10011101 10001111 11111100 11001111 (Class B)
11011101 10001111 11111100 11001111 (Class C)
01111011 10001111 11111100 11001111 (Class A)
11101011 10001111 11111100 11001111 (Class D)
11110101 10001111 11111100 11001111 (Class E)
Class A, B are full; class C still has available addresses; D is reserved for multicasting and class E is reserved for future use

## Slide 19: Dotted decimal notation
Used to make the form shorter and easier to read
Internet addresses are usually written using this form
Looking at the first byte of an address in decimal form will allow us to determine which class the particular address belongs (for the example it belongs to class B)

## Slide 20: Class ranges for Internet addresses

## Slide 21: Special IP addresses
Loopback – the packets sent to these addresses are not sent over the wire;
  they are treated as incoming packets and processed locally
  Very useful for testing/debugging an TCP/IP stack

## Slide 22: A sample internet
Notes: <number>
Three LANs
One Token Ring
G – gateway
R – router

## Slide 23: Two levels of hierarchy
As we have seen, all the addresses on Internet have a network id and a host id; this means that there is a hierarchy in IP addressing
To reach a specific host, first we have to reach the network this host is part of, using the first portion of the address; then we will reach the host itself using the second portion of the IP address.
Then, classes A, B and C in IP addressing are designed with two levels of hierarchy

## Slide 24: Campus network example
Consider a large organization with class B addresses (140.203.0.0)
With two level addressing schema, the organization can’t have more than one physical network
Solution: allow subnets, allow a network to be split into several parts for internal use, but still act as a single network to the outside world

## Slide 25: Subnets (1)
Instead of having a single class B address with 14 bits for network and 16 bits for host number, some bits are taken away from the host number to create a subnet number
For example, if the university (large organization) has 35 departments it could use 6 bits for the subnet number and a 10 bit host number, allowing for up to 64 Ethernets, each with a maximum of 1022 hosts (all 0 and all 1 are not allowed); this split can be changed later if it proves to be wrong

## Slide 26: Subnets (2)
To implement subnetting, the main router will need a subnet mask that indicates the split between network + subnet number and host number
The masking process extracts the address of the physical network from an IP address (bitwise AND between the IP and mask); masking can be done either we have subnetting or not
Subnet mask is also written in dotted decimal notation or as a slash followed by the number of bits in the network
Subnet mask for this example is 255.255.252.0; an alternative notation is /22 to indicate that the subnet mask is 22 bit long, so we can have 255.255.252/22

## Slide 27: Subnets (3)
In our example, the subnets are as follows:
  Subnet 1: 10001100 11001011 000001|00 00000000
    Subnet: 140.203.4.0
    Subnet mask: 255.255.252.0
    First host in the subnet 1: 140.203.4.1
  Subnet 2: 10001100 11001011 000010|00 00000000
    Subnet: 140.203.8.0
    Subnet mask: 255.255.252.0
    First host in the subnet 2: 140.203.8.1
  Subnet 3: 10001100 11001011 000011|00 00000000
    Subnet: 140.203.12.0
    Subnet mask: 255.255.252.0
    First host in the subnet 3: 140.203.12.1
Notes: <number>
Outside the network, the subnetting is not visible, so allocating a new subnet doesn’t require contacting any official organization (that assigns IP addresses) nor changing any external databases

## Slide 28: Another Practical example
Consider network address 141.14.0.0, create 256 subnets with 254 hosts per subnet

## Slide 29: Masking

## Slide 30: Three level hierarchy network

## Slide 31: IP addresses shortage
IP is running out of addresses
  Class A networks (with 16 million host addresses) is too big for most of the organizations
  Class C networks (with 256 host addresses) is too small for most of the organizations
  Class B networks (with 65,536 host addresses) is about right for a medium sized organizations
In reality a class B address is too large for most of the organizations; studies show that half of the class B networks have less than 50 hosts….
Two solutions to cope with the shortage problem
  Use of CIDR (Classless InterDomain Routing)
  Use of NAT (Network Address Translation)

## Slide 32: CIDR
Basic idea is to allocate the remaining IP addresses in variable-sized blocks, without regard to the classes.
If a site needs, say 2000 addresses, it is given a block of 2048 addresses on a 2048 byte boundary
Dropping classes makes the routing more complicated, the old routing algorithm is not working anymore

## Slide 33: Old routing algorithm
Incoming packet to the router (i.e. with destination address 140.203.8.22
Router extracts the destination IP address and shift a copy of it with 28 bits to the right to obtain a 4 bit class number (i.e. 1000)
Have a 16 way branch that sorts the packet into A, B, C and D (if supported):
  8 cases for class A; 4 cases for class B, 2 cases for class C and one case for each D and E
Once the router knows the class (in our example class B), it will know what mask to apply (i.e. 16 bit mask, or 255.255.0.0), in order to find out the network address (140.203.0.0) and look it up into appropriate class routing tables (class B routing tables) to find out the outgoing physical line

## Slide 34: CIDR routing algorithm
Each routing table entry is extended by giving it a 32 bit mask
There is now a single routing table for all networks consisting of (net IP address, subnet mask, outgoing line) triplets
When a packet comes in:
  its destination address is first extracted
  The routing table is scanned entry by entry to find a match
    It is possible to find multiple matches (entries), the one having the longest mask is used (i.e. between /20 entry and /24 entry, /24 is used)
  The packet is forwarded on the outgoing line
Commercial VLSI chipsets for routers have been developed using this new algorithm, in order to speed up the address matching process

## Slide 35: CIDR practical example (1)
Addresses are available at 194.24.0.0
Suppose that:
  Cambridge needs 2048 addresses and it is assigned 194.24.0.0 through 194.24.7.255 with mask 255.255.248.0
  Oxford asks for 4096 addresses and it is assigned 194.24.16.0 through 194.24.31.255 with mask 255.255.240.0
  Edinburgh asks for 1024 addresses and it is assigned 194.24.8.0 through 194.24.11.255 with mask 255.255.252.0

## Slide 36: CIDR practical example (2)
The routing tables all over the world will update to contain the following entries:
  C: 11000010 00011000 00000000 00000000 with mask 11111111 11111111 11111000 00000000
  E: 11000010 00011000 00001000 00000000 with mask 11111111 11111111 11111100 00000000
  O: 11000010 00011000 00010000 00000000 with mask 11111111 11111111 11110000 00000000
Packet coming for destination 194.24.17.4 or in binary: 11000010 00011000 00010001 00000100
  First it is ANDed with Cambridge mask
    11000010 000110000 00010000 00000000, this value doesn’t match the Cambridge base address

## Slide 37: CIDR practical example (3)
  The original address is ANDed with Edinburgh mask:
    11000010 000110000 00010000 00000000, this value doesn’t match the Edinburgh base address
  Next original address is ANDed with Oxford mask:
    11000010 000110000 00010000 00000000, this does match the Oxford base address
If no other matches are found, then the packet will be forwarded on the outside line corresponding to the Oxford entry.

## Slide 38: NAT (Network Address Translation)
It comes into play whenever a need for more hosts than real IP addresses are available (i.e. an ISP may have a class B address, having a 65,534 possible hosts, but has more customers than that)
NAT (RFC 3022) – basic idea is to assign each company a single IP address (or a small number of them) for Internet traffic. Within company, every computer gets a unique IP address, which is used for routing internal traffic; when a packet exits the company and goes to the ISP, an address translation takes place
To make this thing possible, three ranges of IP addresses have been declared as private, companies can use them internally as they wish; the only rule is that no packets containing these addresses may appear on the internet itself

## Slide 39: NAT
10.0.0.0 – 10.255.255.255/8 (16,777,216 hosts)
172.16.0.0 – 172.31.255.255/12 (1, 048,576 hosts)
192.168.0.0 – 192.168.255.255 (65,536 hosts)

## Slide 40: NAT Operation
host
10.0.0.3
Web server
140.203.8.22
10.0.0.0
host
10.0.0.4
10.0.0.1
Payload
(request)
5503
80
10.0.0.3
140.203.8.22
Payload
(request)
5503
80
10.0.0.3
140.203.8.22
Payload
(request)
5001
80
140.203.14.66
140.203.8.22
NAT
140.203.14.66
Orig Source Port
Orig IP Address
Index
5503
10.0.0.3
5001
…
…
…
NAT translation table
Payload
(response)
80
5503
140.203.8.22
10.0.0.3
Payload
(response)
80
5001
140.203.8.22
140.203.14.16
NAT
NAT box
Payload
(response)
80
5503
140.203.8.22
10.0.0.3
Payload
(request)
5001
80
140.203.14.66
140.203.8.22
Payload
(response)
80
5001
140.203.8.22
140.203.14.66

## Slide 41: NAT problems
Violates the architecture of IP model, which states that every host worldwide should be identified by a unique IP
Changes the Internet from a connectionless network in a kind of connection-oriented network
Violates the most elementary rule of protocol layering, that layer k should not make any assumption of what layer k+1 put in the payload
Will not work with any protocols on the Internet (beside TCP or UDP)
Some applications insert IP addresses in the text (payload); the receiver will extract these addresses and use them; NAT will not work with those applications since it doesn’t know about this insertion (i.e. MS Messenger)

## Slide 42: Internet Control Protocols
ICMP (Internet Control Message Protocol)
ARP (Address Resolution Protocol)
RARP (Reverse Address Resolution Protocol)
BOOTP (BOOTstrap Protocol, alternative to RARP)
DHCP (Dynamic Host Configuration Protocol)

## Slide 43: ICMP
Used to report something unexpected; each ICMP message is encapsulated in an IP packet
Used to test the internet
Destination unreachable – is used when the subnet or a router can’t locate the destination or when a packet with DF bit set can’t be delivered because a “small packet” network stands in the way
Time exceeded – is sent when a packet is dropped because its counter reached zero; this event is a symptom that packets are looping, there is an enormous congestion or the timer values were set to low
Parameter problem – indicates that an illegal value has been detected in a header field; this message indicates a bug in the sender’s IP software or possible in the transited routers
Source quench – message formerly used to slow down stations that were sending too many packets; it is not used anymore, because when congestion occurs, those packets tend to throw more fuel into the fire; congestion control is done now in the transport layer
Redirect – is used when a router notices that a packets seem to be routed wrong. It is used by the router to tell the sending host about the probable error
Echo and Echo reply – are used to see if a given destination is reachable and alive; upon receiving the echo message, the receiving station is suppose to answer with the echo reply message
Timestamp request and Timestamp reply – are similar with echo messages, except that the arrival time of the message and the departure time of the reply are recoded in the reply; it is used me measure network performance
Notes: <number>
Destination unreachable – is used when the subnet or a router can’t locate the destination or when a packet with DF bit set can’t be delivered because a “small packet” network stands in the way
Time exceeded – is sent when a packet is dropped because its counter reached zero; this event is a symptom that packets are looping, there is an enormous congestion or the timer values were set to low
Parameter problem – indicates that an illegal value has been detected in a header field; this message indicates a bug in the sender’s IP software or possible in the transited routers
Source quench – message formerly used to slow down stations that were sending too many packets; it is not used anymore, because when congestion occurs, those packets tend to throw more fuel into the fire; congestion control is done now in the transport layer
Redirect – is used when a router notices that a packets seem to be routed wrong. It is used by the router to tell the sending host about the probable error
Echo and Echo reply – are used to see if a given destination is reachable and alive; upon receiving the echo message, the receiving station is suppose to answer with the echo reply message
Timestamp request and Timestamp reply – are similar with echo messages, except that the arrival time of the message and the departure time of the reply are recoded in the reply; it is used me measure network performance

## Slide 44: ARP and RARP
ARP is a network layer (3) protocol and is required to allow a sending station gather address information used in forming a layer 2 frame complete with destination and source MAC addresses
Although ARP is a layer 3 protocol it does not use an IP header, it has its own packet format and is a broadcast on the local LAN within the data field of a layer 2 (Ethernet) frame without needing to be routed.
The Ethernet Type field uses the value 0x0806 to indicate an ARP request and 0x0835 to indicate an ARP response.
If a station does not know its IP address it may send out a RARP (Reverse Address Resolution Protocol) request read by a RARP server which has a table of hardware addresses and IP addresses. The RARP uses the same packet format as the ARP
Most hosts on a network will send out a Gratuitous ARP when they are initializing their IP stack. This Gratuitous ARP is an ARP request for their own IP address and is used to check for a duplicate IP address. If there is a duplicate address then the stack does not complete initialization.
RFC 826 describes ARP in detail, while RFC 903 describes RARP.
Notes: <number>
Every router maintains a table listing IP addresses and respective hardware addresses (e.g. MAC addresses) of devices that exist on the network. This table is called an ARP cache and is referenced by the router when it is looking up a hardware address of a device for which it knows the IP address and needs to forward a datagram to it. If no hardware address is found in the ARP cache then an ARP broadcast is sent on to the adjacent media (ARP only applies to the connecting wire). This broadcast is read by every station including the destination station. The destination station sends back an ARP reply with its hardware address so that the IP datagram can now be forwarded to it by the router.

## Slide 45: ARP packet format
Hardware Type – (i.e. this is 1 for Ethernet).
Protocol Type - the protocol used at the network layer (i.e. IP).
Length of Hardware Address - this is the length in bytes, so it would be 6 for Ethernet.
Length of Protocol Address - for TCP/IP the value is 4 bytes.
Operation Code - this code indicates whether the packet is an ARP Request, ARP Response, RARP Request or RARP Response.
Source Hardware Address - hardware address of the source node.
Source Protocol Address - layer 3 address of the source node.
Destination Hardware Address - used in a RARP request, the response carries both the destination's hardware and layer 3 addresses.
Destination Protocol Address - used in an ARP request, the response carries both the destination's hardware and layer 3 addresses.

## Slide 46: RARP, BOOTP and DHCP
Given an data-link address (i.e. Ethernet address) what is the corresponding net address (IP address)
  RARP
    Is using a broadcasting destination address of all 1s (it is not forwarded by the routers), so a RARP server needs to be in each network
  BOOTP
    Is using UDP messages, so they will be forwarded over routers
    It is specifically designed for diskless stations, so it provides additional information, such as IP of the file server holding the operating system image, etc…
    It requires manual configuration of the tables mapping the IP addresses with Ethernet addresses
  DHCP (Dynamic Host Configuration Protocol)
    Special server that allows automatic and manual IP assignment
    It may require a DHCP relay agent on the local networks, so the DISCOVER packet would be forwarded outside the local LAN
    RFC 2131 and RFC2132

## Slide 47: DHCP operation
DHCP relay agent intercepts all broadcast DISCOVER packets and forwards them as unicast packets to DHCP server
DHCP relay agent needs to know the IP address of the DHCP server

## Slide 48: IPv6
CIDR and NAT may “buy” a few more years, but the days of IPv4 are numbered (shortage problem)
1990, IETF started to work on IPv6, with the following goals:
  Support billion of hosts
  Reduce the size of the routing tables
  Simplify the protocol, to allow routers to process faster
  Provide better security (auth and privacy) than IPv4
  Pay more attention to type of service (for real time data)
  Aid multicasting (by allowing scopes to be specified)
  Make roaming possible without change of address
  Allow protocol expansion
  Permit the old and new protocols to coexist for years

## Slide 49: IPv6 features
16 bytes IP addresses
Header simplification (contains only 7 fields versus 13 fields in IPv4)
Better support for options;
  the way options are represented is different, making it simple for the routers to skip over options not intended for them; this feature speeds up processing in the routers
Improved security features – authentication and privacy are key features of the new protocol.
Better handling of quality of service

## Slide 50: IPv6 header
Version field is always 6 for IPv6 or 4 for IPv4; routers will be able to examine this field and process the packet accordingly
Traffic class – is used to distinguish between packets with different real time delivery requirements
Flow label – experimental field, used to allow a source and a destination to setup a pseudo-connection with particular properties and requirements; i.e. a stream of packets on a certain source host to a certain destination host may have stringent delay requirements, thus need reserved bandwidth.
Payload length – how many bytes follow the 40byte header of the packet. The 40 bytes header is not counted anymore in the length of the packet.
Next header – there can be optional (extra) headers for the given packet. This field tells which (if any) of the currently supported six extension headers follow this header; if this header is the last IP header, the next header field tells which transport protocol handler (TCP, UDP, etc..) to pass the packet to
Hop limit – used to keep packets from living forever; it is practically the same time to live field as in IPv4 header.
Source and Destination address – each 16 bytes. There is a new notation:
8000:0000:0000:0000:0123:4567:89AB:CDEF – eight groups of four hexadecimal digits, with colons between the groups
Notes: <number>
Version - is always 6 for IPv6 or 4 for IPv4; routers will be able to examine this field and process the packet accordingly
Traffic class – is used to distinguish between packets with different real time delivery requirements
Flow label – experimental field, used to allow a source and a destination to setup a pseudo-connection with particular properties and requirements; i.e. a stream of packets on a certain source host to a certain destination host may have stringent delay requirements, thus need reserved bandwidth. The flow can be setup in advance and given an identifier. When a packet with a non zero flow label gets to a router, the router will lookup his tables to determine what kind of special treatment it requires. In effect, the flow label is an attempt to have it both ways: the flexibility of a datagram subnet and the guarantees of a virtual circuit subnet. Many flows could be active at the same time between two given IP addresses.
Payload length – how many bytes follow the 40byte header of the packet. The 40 bytes header is not counted anymore in the length of the packet.
Next header – there can be optional (extra) headers for the given packet. This field tells which (if any) of the currently supported six extension headers follow this header; if this header is the last IP header, the next header field tells which transport protocol handler (TCP, UDP, etc..) to pass the packet to
Hop limit – used to keep packets from living forever; it is practically the same time to live field as in IPv4 header
Source and Destination address – each 16 bytes. There is a new notation:
8000:0000:0000:0000:0123:4567:89AB:CDEF – eight groups of four hexadecimal digits, with colons between the groups

## Slide 51: IPv4 versus IPv6
Protocol filed – was taken out because the next header field tells what follows the last IP header (i.e. UDP or TCP segment)
Fragmentation fields were removed
  IPV6 hosts are expected to dynamically determine the datagram size to use.
  The minimum has been raised from 576 to 1280 to allow 1024 bytes of data and many headers
  If an IPV6 host sends a too large packet, the routers will issue an error message; this message tells the host to break up all future packets to that destination
Checksum field – not existing because calculating it greatly reduces performance. However, since transport layer have their own checksum, it is not making sense to do it twice

## Slide 52: IPv6 extension headers

## Slide 53: IPv6 extension headers
It is used to carry information that all the headers along the path must examine. One option has been defined so far: support for datagrams that exceeds 64K; when used, the payload length field in the main header is set to zero.
Destination options - intended for fields that may be interpreted only at the destination host
Routing header – lists one or more routers that must be visited prior to reaching the destination
Fragmentation – deals with fragmentation, similarly with IPv4; this header holds the datagram identifier, fragment number and a bit telling whether more fragments will follow; in IPv6 only the source host can fragment the packet (unlike IPv4)
Authentication – header that provides a mechanism so the receiving station is sure of who sent the packet (who is the source)
Encrypted security payload – header that makes possible to encrypt the content of a packet so that only the intended recipient can read it; these headers use cryptographic techniques to accomplish their mission
Notes: <number>
They are optional, if exist, they should appear after the fixed 8 bytes header, preferably in the listed order
Hop by hop options - it is used to carry information that all the headers along the path must examine. One option has been defined so far: support for datagrams that exceeds 64K; when used, the payload length field in the main header is set to zero
Destination options - intended for fields that may be interpreted only at the destination host
Routing header – lists one or more routers that must be visited prior to reaching the destination
Fragmentation – deals with fragmentation, similarly with IPv4; this header holds the datagram identifier, fragment number and a bit telling whether more fragments will follow; in IPv6 only the source host can fragment the packet (unlike IPv4)
Authentication – header that provides a mechanism so the receiving station is sure of who sent the packet (who is the source)
Encrypted security payload – header that makes possible to encrypt the content of a packet so that only the intended recipient can read it; these headers use cryptographic techniques to accomplish their mission

## Slide 54: Hop by hop extension header
Datagrams using this header are called jumbograms
Their use is important for supercomputers that must transfer gigabytes of data, in an efficient way, over Internet
Next header – byte that shows what kind of header is next
Header length – how long the hop-by-hop header is in bytes, excluding the first 8 bytes that are mandatory
Type – for this case is code 194 showing that this option defines the datagram size
Length – one byte representing the length of the option, saying that the option value is represented on 4 bytes. It is followed by 4 bytes containing the option value; sizes less than 65536 bytes are not permitted and the routers will issue an error message if happens.
Notes: <number>
Next header – byte that shows what kind of header is next
Header length – how long the hop-by-hop header is in bytes, excluding the first 8 bytes that are mandatory
Type – for this case is code 194 showing that this option defines the datagram size
Length – one byte representing the length of the option, saying that the option value is represented on 4 bytes. It is followed by 4 bytes containing the option value; sizes less than 65536 bytes are not permitted and the routers will issue an error message if happens.

## Slide 55: References
Behrouz A. Forouzan – Data Communications and Networking, ISBN: 0-07-118160-1
Andrew S. Tanenbaum – Computer Networks, ISBN: 0-13066102-3

## Slide 56: Additional Slides
More on Networking Devices

## Slide 57: Repeaters
Receives the signal before it becomes to weak or corrupted, regenerates the original bit pattern and puts the refreshed copy back onto the link
Allows the extension of the physical length of a network
Doesn’t change the functionality of the network in any way

## Slide 58: Repeaters…
Station A sends a frame to station B that will be received by station C and D as well
The repeater is not an amplifier
An amplifier cant discriminate between the intended signal and noise; it amplifies both
A repeater does amplify only the signal; it regenerates it
Notes: <number>
An amplifier cant discriminate between the intended signal and noise; it amplifies both
A repeater does amplify only the signal; it regenerates it

## Slide 59: Repeaters…
The location of the repeater on the link is vital: it must be placed so that a signal reaches it before any noise changes the meaning of the carried information
A little noise can alter the precision of a bit voltage without destroying its identity; if the corrupted bit travels much further, the accumulated noise can change its meaning completely; at that point the original voltage is unrecoverable
A repeater placed on the line before this complete lost takes place, will still read the signal well enough to determine the intended voltages and replicate them in their original form

## Slide 60: Bridges
Operate in both physical and data link layer of OSI
Can divide a large network into smaller segments
Can relay frames between two originally separate LANs
Keep the traffic for each segment separated, filtering the traffic. They are useful to keep the congestion low

## Slide 61: Bridges…
The bridge, beside regenerating the signal, will check the physical address of the destination and forwards the new copy only to the segment to which the address belongs
It reads the address contained in the frame and it compares it against an internal table with all the addresses of the stations on both segments. When it finds a first match, it discovers to which segment the station belongs and relays the packet only to that segment.

## Slide 62: Bridges…
The bridge will block a packet from station A addressed to station D from crossing into the lower segment
The bridge will allow a packet from station A to station G to cross into the lower segment and relays it to the entire lower segment where it is received by station G

## Slide 63: Simple bridge
Links two segments and contains a table that lists he addresses of all the stations included in each of them
Addresses must be entered manually (before a simple bridge can be used, an operator has to sit down and enter the addresses of every station)
Whenever a new station has been added, the table has to be modified; when a station is removed, the table has to be modified, the newly invalid address has to be deleted
The bridge is simple to build and inexpensive to manufacture but installation and maintenance are time consuming, probably more expensive than the price saving resulted out of the cheap manufacturing cost

## Slide 64: Multiport bridge
Connects more than two LANs
For this bridge, there are three tables, each holding the physical addresses of stations reachable through the corresponding port

## Slide 65: Transparent bridge
This learning bridge builds its table of station addresses on its own as it performs bridge functions
When first installed, its table is empty; as it encounters each packet, it looks at both the destination and the source addresses. It checks the destination and decides where to send the packet; if it doesn’t recognize yet the destination address, it sends the packet on all of the ports
It uses the source address to build its table; with the first packet transmitted by each station, it learns the segment associated with that station
Continuing this process even after each station has been learned, it assures that it is self-updating

## Slide 66: Bridges connecting different LANs
Frame format – frames from different LANs have different formats (i.e. Ethernet frame and Token Ring frame)
Payload size – the size of the data that can be encapsulated in a frame varies from protocol to protocol (i.e. Ethernet has 1500 + headers while Token Ring has 4500 + headers)
Data rate – different protocols use different data rates (i.e. 10 Mb/s for Ethernet and 16Mb/s for Token Ring)
Address bit order – the bit order of addresses in different types of LANs is not the same (i.e. a bridge should reverse an address if it is connecting an Ethernet LAN to a Token Ring LAN)
Other issues: collision, acknowledgements, priority, etc…

## Slide 67: Routers
Relay packets among multiple interconnected networks and operate at physical, data link and network layer of OSI/TCP model
Have access to network layer addresses and have two or more networks at the same time
Notes: <number>
They have special software that enables them to determine which of the several possible paths between addresses is best for a particular transmission

## Slide 68: Routers
A packet sent from a station on one network to a station on a neighboring network, goes first to the jointly held router, which forwards it to the destination network
If the router is not connected to both source and destination network, then the sending router transfers the packet across one of its connected networks to the next router, in the direction of the destination, and so on, until the destination is reached